## Slide 2
LESSON 1
HYDRAULIC RESERVOIRS, FILTERS, PUMPS, ACCUMULATORS, AND MOTORS
STP Tasks: 552-758-1063
552-758-1071

## Slide 3
INTRODUCTION
A means of storing hydraulic fluid and minimizing contamination is necessary to any aircraft hydraulic
system. These functions are performed by reservoirs and filters. The component which causes fluid
flow in a hydraulic system--the heart of any hydraulic system--can be a hand pump, power-driven pump,
accumulator, or any combination of the three. Finally, a means of converting hydraulic pressure to
mechanical rotation is sometimes necessary, and this is accomplished by a hydraulic motor

## Slide 4
HYDRAULIC RESERVOIRS
The hydraulic reservoir is a container for holding the fluid required to supply the system, including a
reserve to cover any losses from minor leakage and evaporation. The reservoir can be designed to
provide space for fluid expansion, permit air entrained in the fluid to escape, and to help cool the fluid.
Figure 1-1 shows two typical reservoirs. Compare the two reservoirs item by item and, except for the
filters and bypass valve, notice the similarities

## Slide 5
Filling reservoirs to the top during servicing leaves no space for expansion. Most reservoirs are
designed with the rim at the filler neck below the top of the reservoir to prevent overfilling. Some
means of checking the fluid level is usually provided on a reservoir. This may be a glass or plastic sight
gage, a tube, or a dipstick. Hydraulic reservoirs are either vented to the atmosphere or closed to the
atmosphere and pressurized. A description of each type follows.

## Slide 6
Vented Reservoir. A vented reservoir is one that is open to atmospheric pressure through a vent line.
Because atmospheric pressure and gravity are the forces which cause the fluid to flow to the pump, a
vented reservoir is mounted at the highest point in the hydraulic system. Air is drawn into and
exhausted from the reservoir through a vent line. A filter is usually installed in the vent line to prevent
foreign material from being taken into the system.
Pressurized Reservoir. A pressurized reservoir is sealed from the atmosphere. This reservoir is
pressurized either by engine bleed air or by hydraulic pressure produced within the hydraulic system
itself. Pressurized reservoirs are used on aircraft intended for high altitude flight, where atmospheric
pressure is not enough to cause fluid flow to the pump.

## Slide 7
In reservoirs pressurized by engine bleed air, the amount of air pressure is determined by an air
pressure regulator--usually 10 to 15 pounds per square inch (psi) gage. An example of a
hydraulically pressurized reservoir used in the CH-47 hydraulic system is shown in Figure 1-2.
This reservoir, or tank as it is referred to by Boeing-Vertol, is constructed of a metal housing with
two internal pistons, one fixed and the other a floating piston which slides along a central tube.
Attached to the floating piston is a larger tube that projects through the forward end of the tank and is
calibrated to indicate FULL and REFILL fluid levels for ramp-up and ramp-down positions.

## Slide 9
Hydraulic fluid at 3,000 psi flows into the central tube as shown in Figure 1-2, passes through two
outlet holes, and applies pressure at the piston area between the two tubes. Because the smaller piston
has a .5-square-inch (sq in) exposed surface and the floating piston has a 30-sq-in exposed surface, the
3,000-psi pressure acting upon the smaller forward area produces an opposing pressure of 50 psi on the
return fluid stored at the rear of the piston

## Slide 10
Additional Reservoir Components. Many reservoirs, as shown in Figure 1-1, are constructed with
baffles or fins to keep the fluid from swirling and foaming. Foaming can cause air to become entrained
in the system.
Filters are incorporated in some reservoirs to filter the fluid before it leaves the reservoir.
A bypass valve is used to ensure that the pump does not starve if the filter becomes clogged.
A standpipe is used in a reservoir which supplies a normal and an emergency system. The main
system draws its fluid from the standpipe, which is located at a higher elevation. This ensures an
adequate fluid supply to the secondary system if the main system fails.

## Slide 12
HYDRAULIC FILTER
Contamination of hydraulic fluid is one of the common causes of hydraulic system troubles. Installing
filter units in the pressure and return lines of a hydraulic system allows
contamination to be removed from the fluid before it reaches the various operating components. Filters
of this type are referred to as line filters.
Line Filter Construction. A typical line filter is shown in Figure 1-3. It has two major parts--the
filter case, or bowl, and the filter head. The bowl holds the head that screws into it. The head has an
inlet port, outlet port, and relief valve. Normal fluid flow is through the inlet port, around the outside of
the element, through the element to the inner chamber, and out through the outlet port. The bypass
valve lets the fluid bypass the filter element if it becomes clogged.

## Slide 14
Types of Filter Elements. The most common filtering element used on Army aircraft is the micronic
type. It is a disposable unit made of treated cellulose and is formed into accordion pleats, as shown in
Figure 1-3. Most filter elements are
capable of removing all contaminants larger than 10 to 25 microns (1 micron equals 0.00004 inch).
Another type is the cuno filter element. It has a stack of closely spaced disks shaped like spoked
wheels. The hydraulic fluid is filtered as it passes between the disks.

## Slide 15
HAND-OPERATED HYDRAULIC PUMP
The heart of any hydraulic system is the pump which converts mechanical energy into hydraulic energy.
The source of mechanical energy may be an electric motor, the engine, or the operator's muscle.
Pumps powered by muscle are called hand pumps. They are used in emergencies as backups for power
pumps and for ground checks of the hydraulic system. The double-action hand pump produces fluid
flow with every stroke and is the only type used on Army aircraft

## Slide 16
Handle to the Right. The double-action hand pump, shown in Figure 1-4, consists of a cylinder
piston with built-in check valve, piston rod, operating handle, and a check valve built into the inlet port.
As the handle is moved to the right, the piston and rod also move to the right. On this stroke, the inlet
check valve opens as a result of the partial vacuum caused by the movement of the piston, allowing fluid
to be drawn into the left chamber. At the same time, the inner check valve closes. As the piston moves
to the right, the fluid in the right chamber is forced out into the system.

## Slide 18
Handle to the Left. When the handle is moved to the left, the piston and rod assembly also move to
the left. The inlet check valve now closes, preventing the fluid in the left chamber from returning to the
reservoir. At the same time, the pistonhead check valve opens, allowing the fluid to enter the right
chamber.
Fluid Into the System. The pump produces pressure on both strokes because of the difference in
volume between the right and left chambers. The piston rod takes up a good share of the space in the
right chamber. Therefore, the excess fluid is forced out of the pump and into the hydraulic system,
creating fluid pressure.

## Slide 19
PUMP-DRIVEN HYDRAULIC PUMPS
Power-driven pumps receive their driving force from an external power source, such as the aircraft
engine. This force is converted into energy in the form of fluid pressure. The four basic types of powerdriven
hydraulic pumps are gear, vane, diaphragm, and piston. Of these, the piston type is most
commonly found in Army aircraft. The reason for this is that it operates more efficiently at higher
pressures and has a longer life than any of the others. Piston pumps are further categorized as either
constant delivery or variable delivery.
Pumps are coupled to their driving units by a short, splined coupling shaft, commonly called a drive
coupling. As shown in Figure 1-5, the shaft is designed with a weakened center section called a shear
section, with just enough strength to run the pump under normal circumstances. Should some trouble
develop within the pump causing it to turn unusually hard, the shear section will break. This prevents
damage to the pump or driving unit.

## Slide 21
Constant-delivery piston pumps deliver a given quantity of fluid per revolution of the drive coupling,
regardless of pressure demands. The quantity of fluid delivered per minute depends on
pump revolutions per minute (rpm). In a system requiring constant pressure, this type of pump must be
used with a pressure regulator. The two types of constant-delivery piston pumps used in Army aircraft
are the angular and cam.
Angular Piston Pump Construction. The basic components of an angular piston pump are shown in
Figure 1-6. They are--
· (1) A rotating group consisting of a coupling shaft, universal link, connecting rods, pistons,
and cylinder block.
· (2) A stationary group consisting of the valve plate and the pump case or housing.
The cylinder bores lie parallel to, and are evenly spaced around, the pump axis. For this reason, a
piston pump is often referred to as an axial piston pump.

## Slide 22
Packings on seals are not required to control piston-to-bore leakage. This is controlled entirely by
close machining and accurate fit between piston and bore. The clearance is only enough to allow for
lubrication by the hydraulic fluid and slight expansion when the parts become heated. Pistons are
individually fitted to their bores during manufacture and must not be changed from pump to pump or
bore to bore.
Pump Operation. As the coupling shaft is turned by the pump power source, the pistons and cylinder
block turn along with it because they are interconnected. The angle that exists between the cylinder
block and coupling shaft causes the pistons to move back and forth in their respective cylinder bores as
the coupling is turned:

## Slide 23
· During the first half of a revolution of the pump, a cylinder is aligned with the inlet port in
the valve plate. At this time the piston is moving away from the valve plate and drawing
hydraulic fluid into the cylinder. During the second half of the revolution, the cylinder is
lining up with the outlet port in the valve plate. At this time, the piston is moving toward the
valve plate, thus causing fluid previously drawn into the cylinder to be forced out through the
outlet port.
· Fluid is constantly being drawn into and expelled out of the pump as it turns. This provides a
multiple overlap of the individual spurts of fluid forced from the cylinders and results in
delivery of a smooth, nonpulsating flow of fluid from the pump

## Slide 24
Cam-Piston Pumps. A cam is used to cause the stroking of the pistons in a cam-piston pump. Two
variations are used: in one the cam rotates and the cylinder block is stationary, and in the other the cam
is stationary and the cylinder block rotates. Both cam-piston pumps are described below:

## Slide 26
· Rotating-cam pump. The rotating-cam pump is the one most commonly used in Army
aviation. As the cam turns in a rotating-cam pump (Figure 1-7), its high and low points pass
alternately and in turn under each
piston. It pushes the piston further into its bore, causing fluid to be expelled from the bore. When the
falling face of the cam comes under a piston, the piston's return spring pulls the piston down in its bore.
This causes fluid to be drawn into the bore.

## Slide 27
Each bore has a check valve that opens to allow fluid to be expelled from the bore by the piston's
movement. These valves are closed by spring pressure during inlet strokes of the pistons. This fluid is
drawn into the bores only through the central inlet passages. The bores only through the central inlet
passages. The movement of the pistons in drawing in and expelling fluid is overlapping, resulting in a
nonpulsating fluid flow.

## Slide 29
· Stationary-cam pump. The operation and construction of a stationary-cam pump are
identical to that of the rotating cam except that the cylinder block turns, not the cam. The
stationary-cam pump is not used on the Army's OV-1, AH-1G, and UH-1C.

## Slide 30
VARIABLE-DELIVERY PISTON PUMPS
A variable-delivery piston pump automatically and instantly varies the amount of fluid delivered to the
pressure circuit of a hydraulic system to meet varying system demands. This is accomplished by using a
compensator, which is an integral part of the pump. The compensator is sensitive to the amount of
pressure present in the pump and in the hydraulic system pressure circuit. When the circuit pressure
rises, the compensator causes the pump output to decrease.
Conversely, when circuit pressure drops, the compensator causes pump output to increase. There are
two ways of varying output--demand principle (cam) and stroke-reduction principle (angular).
Demand Principle. The demand principle (Figure 1-8) is based on varying pump output to fill the
system's changing demands by making the piston stroke effective in varying degrees.

## Slide 32
The pistons are designed with large hollow centers. The centers are intersected by cross-drilled
relief holes that open into the pump case. Each piston is equipped with a movable sleeve, which can
block the relief holes. When these holes are not blocked, fluid displaced by the pistons is discharged
through the relief holes into the pump case, instead of past the pump check valves and out the outlet
port.
When full fluid flow is required, the sleeves are positioned to block the relief holes for the entire
length of piston stroke. When zero flow is required, the sleeves are positioned not to block the flow
during any portion of the piston stroke. For requirements between zero and full flow, the relief holes are
uncovered or blocked accordingly.

## Slide 33
The sleeves are moved into their required positions by a device called a pump compensator piston.
The sleeves and compensator piston are interconnected by means of a spider. Fluid pressure for the
compensator piston is obtained from the discharge port (system pressure) through a control orifice.
Stroke-Reduction Principle. The stroke-reduction principle (Figure 1-9) is based on varying the
angle of the cylinder block in an angular pump. This controls the length of the piston's stroke and thus
the volume per stroke.
The cylinder block angle change is achieved by using a yoke that swivels around a pivot pin called a
pintle. The angle is automatically controlled by using a compensator assembly consisting of a pressurecontrol
valve, pressure-control piston, and mechanical linkage that is connected to the yoke.

## Slide 34
As system pressure increases, the pilot valve opens a passageway allowing fluid to act on the control
piston. The piston moves, compressing its spring, and through mechanical linkage moves the yoke
toward the zero flow (zero angle) position. As system pressure decreases, the pressure is relieved on the
piston, and its spring moves the pump into the full flow position.
HYDRAULIC ACCUMULATORS
The purpose of a hydraulic accumulator is to store hydraulic fluid under pressure. It may be used to--:
· Dampen hydraulic shocks which may develop when pressure surges occur in hydraulic systems.
· Add to the output of a pump during peak load operation of the system, making it possible to use
a pump of much smaller capacity than would otherwise be required

## Slide 35
· Absorb the increases in fluid volume caused by increases in temperature.
· Act as a source of fluid pressure for starting aircraft auxiliary power units (APUs).
· Assist in emergency operations

## Slide 37
Accumulators are divided into types according to the means used to separate the air fluid chambers;
these are the diaphragm, bladder, and piston accumulators.
Diaphragm Accumulator. The diaphragm accumulator consists of two hollow, hemispherical metal
sections bolted together at the center. Notice in Figure 1-10 that one of the halves has a fitting to attach
the unit to the hydraulic system; the other half is equipped with an air valve for charging the unit with
compressed air or nitrogen. Mounted between the two halves is a synthetic rubber diaphragm that
divides the accumulator into two sections. The accumulator is initially charged with air through the air
valve to a pressure of approximately 50 percent of the hydraulic system pressure. This initial air charge
forces the diaphragm upward against the inner surface of the upper section of the accumulator

## Slide 39
When fluid pressure increases above the initial air charge, fluid is forced into the upper chamber
through the system
14 AL0926
pressure port, pushing the diaphragm down and further compressing the air in the bottom chamber.
Under peak load, the air pressure in the lower chamber forces fluid back into the hydraulic system to
maintain operating pressure. Also, if the power pump fails, the compressed air forces a limited amount
of pressurized fluid into the system.

## Slide 40
Bladder Accumulator. The bladder accumulator operates on the same principle and for the same
purpose as the diaphragm accumulator but varies in construction, as shown in Figure 1-11. The unit is a
one-piece metal sphere with a fluid pressure inlet at the top and an opening at the bottom for inserting
the bladder. A large screw-type plug at the bottom of the accumulator is a retainer for the bladder that
also seals the unit. A high-pressure air valve is also incorporated in the retainer plug. Fluid enters
through the system pressure port. As fluid pressure increases above the initial air charge of the
accumulator, it forces the bladder downward against the air

## Slide 42
charge, filling the upper chamber with fluid pressure. The broken lines in Figure 1-11 indicate the
approximate position of the bladder at the time of the initial air charge.
Piston Accumulator. The piston accumulator serves the same purpose and operates by the same
principles as do the diaphragm and bladder accumulators. As shown in Figure 1-12, the unit consists of
a cylinder and piston assembly with ports on each end. Fluid pressure from the system enters the left
port, forcing the piston down against the initial air charge in the right chamber of the cylinder. A highpressure
air valve is located at the right port for charging the unit. A drilled passage from the fluid side
of the piston to the outside of the piston provides lubrication between the cylinder walls and the piston

## Slide 44
HYDRAULIC MOTORS
Hydraulic motors are installed in hydraulic systems to use hydraulic pressure in obtaining powered
rotation. A hydraulic motor does just the opposite of what a power-driven pump does. A pump receives
rotative force from an engine or other driving unit and converts it into hydraulic pressure. A hydraulic
motor receives hydraulic fluid pressure and converts it into rotative force.
Figure 1-13 shows a typical hydraulic motor. The two main ports through which fluid pressure is
received and return fluid is discharged are marked A and B, respectively. The motor has a cylinder
block-and-piston assembly in which the bores and pistons are in axial arrangement, the same as in a
hydraulic pump. Hydraulic motors can be instantly started, stopped, or reversed under any degree of
load; they can be stalled by

## Slide 45
overload without damage. The direction of rotation of a hydraulic motor can be changed by reversing
the flow of fluid into the ports of the motor.

## Slide 47
SUMMARY
The basic components of any hydraulic system are reservoirs, filters, and pumps (hand or power-driven).
The reservoir holds the fluid supply for the system and helps cool the fluid. Filters are used to ensure
that no contamination reaches the components in a hydraulic system. The pleated micronic filter is the
most common.
The pump converts mechanical energy to fluid flow. The most common power-driven pump is the
piston pump. In all but the simplest hydraulic systems, variable-delivery pumps are used. A variabledelivery
pump delivers only the amount of fluid demanded by the system. This is accomplished through
the use of a compensator.
Depending on the type of aircraft, hydraulic accumulators and hydraulic motors can also be found in the
system. Accumulators are used primarily to supply pressure for starting auxiliary power units and
emergency hydraulic pressure. Hydraulic motors perform a variety of functions, including raising and
lowering cargo doors, operating rescue hoists, and positioning wing flaps.

## Slide 48
LESSON 2
BASIC CONSTRUCTION AND OPERATION OF HYDRAULIC
ACTUATING DEVICES, FLOW CONTROL, AND DIRECTIONAL DEVICES
STP Tasks: 552-758-1003
552-758-1071

## Slide 49
INTRODUCTION
So that fluid pressure produced by a pump can be used to move some object, the pressure must be
converted to usable forces by
means of an actuating unit. A device called an actuating cylinder is used to impart powered straight-line
motion to a mechanism.
Hydraulic systems must also have devices to control or direct the fluid pressure to the various
components. Such devices include selector valves, check valves, ratchet valves, irreversible valves,
sequence valves, and priority valves. Each is described in the paragraphs that follow

## Slide 50
ACTUATING CYLINDERS
A basic actuating cylinder consists of a cylinder housing, one or more pistons and piston rods, and one
or more seals. The cylinder housing contains a polished bore in which the piston operates and one or
more ports through which fluid enters and leaves the bore. The piston and rod form an assembly which
moves forward and backward within the cylinder bore. The piston rod moves into and out of the
cylinder housing through an opening in one or both ends. The seals are used to prevent leakage between
the piston and cylinder bore, and between the piston rod and housing. The two major types of actuating
cylinders are single-action and double-action.

## Slide 51
Single-Action Actuating Cylinder. The single-action actuating cylinder, shown in Figure 2-1,
consists of a cylinder housing with one fluid port, a piston and rod assembly, a piston return spring, and
seals.
When no pressure is applied to the piston, the return spring holds it and the rod assembly in the
retracted position. When hydraulic pressure is applied to the inlet port, the piston, sealed to the cylinder
wall by an O-ring, does not allow the fluid to pass. This causes the piston to extend.
As the piston and rod extend, the return spring compresses. A vent on the spring side of the piston
allows air to escape. When pressure is relieved, the return spring forces the piston to retract, pushing the
fluid out of the cylinder. A wiper in the housing keeps the piston rod clean.
The cylinder can be pressure-operated in one direction only. A three-way control valve is normally
used to control cylinder operation.

## Slide 52
Double-Action Actuating Cylinder. The double-action actuating cylinder consists of a cylinder with
a port at either end and a piston and rod assembly extending through one end of the cylinder (Figure 2-2).
Pressure applied at port A causes the piston to extend, forcing the fluid on the opposite side of the
piston out of port B. When pressure is applied to port B, the piston and rod retract, forcing the fluid in
the opposite chamber out through port A.

## Slide 54
This type of cylinder is powered in both directions by hydraulic pressure. A selector valve is
normally used to control a double-action actuating cylinder. Selector valves are discussed in the next
paragraph.

## Slide 56
SELECTOR VALVES
Used in hydraulic systems to control the direction of operation of a mechanism, selector valves are also
referred to as directional control valves or control valves. They provide pathways for the simultaneous
flow of two streams of fluid, one under pressure into the actuating unit, and the other, a return stream,
out of the actuating unit. The selector valves have
various numbers of ports determined by the requirements of the system in which the valve is used.
Selector valves with four ports are the most commonly used; they are referred to as four-way valves.
Selector valves are further classified as closed-center or open-center types.

## Slide 57
Closed-Center Selector Valve. When a closed-center selector valve is placed in the the OFF
position, its pressure passage is blocked to the flow of fluid. Therefore, no fluid can flow through its
pressure port, and the hydraulic system stays at operating pressure at all times. The four-way, closedcenter
selector valve is the most commonly used selector valve in aircraft hydraulics. There are two
types:

## Slide 58
· The rotor-type, closed-center selector valve is shown in Figure 2-3. It has a rotor as its valving
device. The rotor is a thick circular disk with drilled fluid passages. It is placed in its various
operating positions by relative movement of the valve control handle. In the OFF position, the
rotor is positioned to close all ports. In the first ON position, the rotor interconnects the pressure
port with the number 1 cylinder port. The number 2 cylinder port is open to return. In the
second ON position the reverse takes place.

## Slide 59
· The spool-type, closed-center selector valve, is shown in Figure 2-4. This valve has a housing
containing four ports and a spool (pilot valve). The spool is made from a round shaft having
machined sections forming spaces to allow hydraulic fluid to pass. A drilled passage in the spool
interconnects the two end chambers of the selector valve. The large diameters of the spool are
the bearing and sealing surfaces and are called "lands" (see Glossary). In operation, the spool
valve is identical to the rotor type.

## Slide 62
Open-Center Selector Valve. In external appearance, the open-center selector valve looks like the
closed-center one. Like closed-center valves, open-center selector valves have four ports and operate in
one OFF and two ON

## Slide 63
positions. The difference between the closed-center and open-center valves is in the OFF position. In
the closed-center valve none of the ports are open to each other in the OFF position. In the open-center
valve, the pressure and return ports are open to each other when the valve is OFF. In this position, the
output of the system pump is returned through the selector valve to the reservoir with little resistance.
Hence, in an open-center system, operating pressure is present only when the actuating unit is being
operated.
An open-center, rotor-type selector valve is shown in Figure 2-5. As you can see, when the valve is
in the OFF position, fluid from the pump enters the pressure port, passes through the open center
passage in the rotor, and back to the reservoir. When the valve is in either of the two ON positions, it
functions the same as a closed-center valve.

## Slide 65
An open-center, spool-type selector valve is shown in Figure 2-6. Notice that this valve differs from
the closed-center type in that a third land is machined on the spool. This land is used to cover the
pressure port when the valve is in the OFF position. It provides an inter-passage in the spool which
allows fluid from the pump to return to the reservoir. Operation in both of the ON positions is the same
as the closed-center selector valve.

## Slide 68
Hydraulic systems are classified as open-center or closed-center depending upon the type of selector
valves used. In an open-
center system that has more than one selector valve, the valves are arranged one behind the other (in
series).
In a closed-center system, the valves are arranged parallel to each other. An open-center system has
fluid flow but no pressure in the system when the selector valve is off.
In a closed-center system, fluid is under pressure throughout the system when the hydraulic pump is
operating. Both systems are discussed in the paragraphs that follow.
Open-Center System. Figure 2-7 shows a basic open-center hydraulic system which uses a relief
valve to limit system pressure. As was mentioned earlier, this type of sys

## Slide 70
has fluid flow but no pressure until some hydraulic device is operated. When the selector valves are
OFF, fluid flows from the reservoir to the pump through the open-center passage of each valve, then
back to the reservoir. No restrictions exist in the system; therefore, no pressure is present. When one
valve is placed in the operating position, a restriction is created by the device the valve controls. Fluid
then flows under pressure to that hydraulic device.
Closed-Center System. Figure 2-8 shows a basic closed-center system. Fluid is under pressure
throughout a closed-center system when the pump is operating. When the selector valves are in the OFF
position, fluid cannot flow through the closed centers. This causes pressure to build in the system; it is
available at any time a selector valve is turned on. A relief valve is used to keep system pressure from
going above a predetermined amount when all valves are off.

## Slide 72
HYDRAULIC SERVO
A servo is a combination of a selector valve and an actuating cylinder in a single unit. When the pilot
valve of a servo is opened by the operator, it is automatically closed by movement of the servo (or
actuating) unit as explained below. Hydraulic servos are used in aircraft when precise control is
necessary over the distance a component moves.
Typical Hydraulic Servo. Figure 2-9 shows a typical hydraulic servo. In operation, when the pilot
valve is displaced from center, pressure is directed to one chamber of the power piston. The other
chamber is open to return flow. As the power piston travels the pilot valve housing travels because the
two are attached. The pilot valve itself is being held stationary by the operator, and the ports again
become blocked by the lands of the pilot valve stopping the piston when it has moved the required
distance.

## Slide 74
Servo Sloppy Link. Notice the servo sloppy link in Figure 2-9. It is the connection point between
the control linkage, pilot valve, and servo piston rod. Its purpose is to permit the servo piston to be
moved either by fluid pressure or manually. The sloppy link provides a limited amount of slack between
connecting linkage and pilot valve. Because of the slack between the piston rod and the connecting
linkage, the pilot valve can be moved to an ON position by the connecting linkage without moving the
piston rod.
Bypass Valve. A bypass valve is provided to minimize the resistance of the servo piston to
movement when it must be moved manually. The valve opens automatically when there is no operating
pressure on the servo. This allows fluid to flow freely between the chambers on each side of the piston.

## Slide 75
IRREVERSIBLE VALVE
During normal aircraft operation, external forces from an aircraft's control surfaces, such as rotor blades
and ailerons, tend to move servo cylinders. This movement creates a pumplike action in the servo called
feedback. The irreversible valve prevents feedback through the servo to the control stick.
Figure 2-10 is a simplified schematic version of an irreversible valve. The broken-line block represents
the housing of the

## Slide 77
valve. The check valve allows fluid from the pump to flow in the normal direction as shown by the
arrow. Feedback forces tend to move the servo piston opposite to the direction of pump-produced
pressure. This tends to force fluid backward through the irreversible valve. The check valve keeps the
servo piston from yielding to feedback by locking the rear-ward flow of fluid. The relief valve is a
safety device to limit the pressure produced by feedback-induced movement of the servo piston. It
opens to allow fluid to bypass to the return line if the feedback pressure exceeds a predetermined safe
limit.

## Slide 78
RATCHET VALVE
A ratchet valve is used with a double-action actuating cylinder to aid in holding a load in the position
where it has been moved. The ratchet valve ensures that there is trapped fluid on each side of the
actuating cylinder piston. This is necessary for the cylinder to lock a load against movement in either
direction.
A typical ratchet valve is shown in Figure 2-11. It consists of a housing with four ports, a polished bore,
two ball check valves and a piston. The piston has extensions on either end to unseat the two ball check
valves. Springs keep these valves on their seats when no pressure is applied to the system

## Slide 79
Valve Operation With no Pressure. In A, Figure 2-11, the ratchet valve is shown with no pressure
applied. The piston is centered in its bore and both ball check valves are closed. This locks the
actuating cylinder in position by trapping all fluid in the cylinder.
Valve Operation With Pressure Applied. In B, Figure 2-11, the ratchet valve is shown with pressure
applied to port 1. This forces the piston to the right where it unseats ball check valve b. Pressure
entering port 1 also unseats ball check valve a on the left side. Fluid then flows through the ratchet
valve and the piston moves to the right.

## Slide 80
CHECK VALVES
A check valve is installed in a hydraulic system to control the direction flow of hydraulic fluid. The
check valve allows free flow of fluid in one direction, but no flow or a restricted one in the other
direction.
There are two general designs in check valves. One has its own housing and is connected to other
components with tubing or hose. Check valves of this design are called in-line check valves. In the
other design, the check valve is part of another component and is called an integral check valve. It will
not be covered because its operation is identical to the in-line check valve. The two types of in-line
check valves, simple and orifice, are described in the following paragraphs.

## Slide 81
Simple In-Line Check Valve. As illustrated in Figure 2-12, the simple inline check valve consists of
a casing, inlet and outlet ports, and a ball-and-spring assembly. The ball and spring permit full fluid
flow in one direction and block flow completely in the opposite direction. Fluid pressure forces the ball
off its seat against the spring pressure, permitting fluid flow. When flow stops, the spring forces the ball
against its seat, blocking reverse flow.
Orifice In-Line Check Valve. The orifice check valve shown in Figure 2-13 is used to allow free
flow in one direction and limited flow in the opposite direction. This is accomplished by drilling a
passage in the valve seat connecting the inlet side of the valve to the outlet side.

## Slide 84
SEQUENCE VALVE
A sequence valve, shown in Figure 2-14, is placed in a hydraulic system to delay the operation of one
portion of that system until another portion of the same system has functioned. For
.
example, it would be undesirable for the landing gear to retract before the gear compartment doors are
completely open. A sequence valve actuated by the fully open door would allow pressure to enter the
landing gear retract cylinder.
The sequence valve consists of a valve body with two ports, a ball and seal spring-loaded to the closed
position, and a spring-loaded plunger. Compressing the plunger spring off-seats the ball and allows the
passage of fluid to the desired actuator. The typical sequence valve is mechanically operated, or it can
be solenoid-operated by means of microswitches. In either case, the valve is operated at the completion
of one phase of a multiphase hydraulic cycle.

## Slide 86
PRIORITY VALVE
A priority valve is installed in some hydraulic systems to provide adequate fluid flow to essential units.
The valve is installed in the line between a nonessential actuating unit and its source of pressure. It
permits free, unrestrained flow of fluid to nonessential units as long as system pressure is
normal. When system pressure drops below normal, the priority valve automatically reduces the flow of
fluid to the nonessential units.
The priority valve (Figure 2-15) resembles a check valve in both external appearance and internal
operation. A spring acts against a hollow piston to maintain contact with a valve seat. With no system
pressure, the priority valve is in the Spring-loaded position, closed. The piston is against the valve seat.
As pressure is applied to the system, fluid passes through the valve seat and also through drilled
passages to act against the face of the piston. With normal flow and pressure, the piston moves against
the spring tension and allows passage of fluid. If pressure decreases, the spring forces the piston to seat,
assuring a supply of fluid for the essential portion of the system.

## Slide 88
SUMMARY
The hydraulic actuating cylinder is used to convert fluid pressure to straight-line motion. The two types
are single-and double-acting.
Selector valves are used with actuating cylinders to control their operation. The typical selector valve
has two ON
positions to extend and retract the cylinder and one OFF position.
Hydraulic systems are classified as either open-center or closed-center. Open-center systems have only
open-center selector valves and closed-center systems only closed-center valves.
Hydraulic servos are physical combinations of actuators and selector valves. They are used when
precise control of movement is required and normally found in the flight control system of an aircraft.
Irreversible valves are used in line with servos to prevent feedback to the flight controls.
Ratchet valves are locking devices for actuating cylinders; they
hold the cylinders in any desired position.

## Slide 89
If full fluid flow in one direction only is required, a simple in-line check valve is used. When full flow
in one direction and restricted flow in the opposite direction is desired, an orifice check valve is used.
When more than one function must be performed in a hydraulic system and a definite order must be
followed, sequence valves are used. Sequence valves ensure that the proper order of operations is
maintained. In a reduction of pressure or fluid flow, certain components can be cut out of the hydraulic
system to ensure an adequate supply of fluid for the essential components, such as flight controls.
Priority valves are used to automatically shut off the supply of fluid to nonessential components

## Slide 90
LESSON 3
HYDRAULIC PRESSURE-LIMITING, CONTROLLING, AND SENSING DEVICES
STP Tasks: 552-758-1003
552-758-1006
552-758-1071

## Slide 91
INTRODUCTION
The hydraulic systems in modern Army aircraft operate at pressures up to 3,000 psi. These systems
must be protected against excessively high pressure that can cause seals and lines to fail. Pressure relief
valves are used to keep system pressure from exceeding a predetermined safe limit.
A complex hydraulic system can use any number of components: actuators, servos, irreversible valves,
selector valves, check valves, accumulators, hydraulic motors, etc. Each of these various components in
one hydraulic system can operate most efficiently at a different pressure. In systems having a single
hydraulic pump, pressure reducers are used to vary operating pressures to the different components.

## Slide 92
If hydraulic pressure becomes too low for safe operation, a hydraulic pressure switch can be used to
close an electrical circuit. This actuates a warning light in the cockpit or turns on a secondary system, or
does both.
In this chapter you will learn of the devices used to limit, control, and sense hydraulic pressure

## Slide 93
PRESSURE RELIEF VALVES
A relief valve is installed in any system containing a confined liquid subject to pressure. The use of
relief valves falls into one or more of three categories:
· In the first category, a relief valve is used to protect a hydraulic system if the pump compensator
fails. The relief valve is adjusted to open at a pressure slightly higher than normal system
operating pressure.
· In the second category, a relief valve is used to protect a system subject to pressure increases
caused by thermal expansion.
· In the third category, a relief valve is used as the sole means of pressure control in a hydraulic
system.

## Slide 94
Relief Valves. The configurations for relief valves are either two-port or four-port. Both types
operate in the same way. The main reason for additional ports is convenience in connecting the
plumbing. For simplicity, only the two-port pressure relief valve is described in this text.
Two-Port Relief Valve. A typical two-port relief valve is shown in Figure 3-1. It consists of a
housing with an inlet and an outlet port, a valving device, a compression spring, and an adjustment
screw. When the hydraulic system is pressurized, the pressure acts against the valving device; in this
case, a ball. The ball is held against its seat by a coil spring. When the fluid pressure is great enough
against the ball to overcome the

## Slide 95
force of the spring, the ball is unseated and allows fluid to pass.
The exact pressure at which this takes place is called the cracking pressure. This pressure can be
adjusted to any desired pressure by means of the pressure adjustment screw. Fluid passing the valving
ball flows into return lines and back to the reservoir

## Slide 97
PRESSURE REDUCER
A pressure reducer provides more than one level of pressure in a system that has a single hydraulic
pump. The reducer (Figure 3-2) consists of a three-port housing, piston, poppet and spring, adjusting
spring, and adjusting screw. A poppet is a valving device with a flat face. The three ports of the
housing are input pressure port, reduced-pressure port, and return port

## Slide 99
Withholding Pressure. The pressure reducer operates on the principle of withholding pressure rather
than relieving it. With no pressure in the system, the adjusting spring tension holds the poppet open. As
system pressure builds up, fluid passes through the poppet to the reduced-pressure port. When the
pressure acting against the piston exceeds the force of the adjusting spring in the pressure reducer, the
poppet moves to close the inlet port. Further buildup of system pressure does not affect the reduced
pressure until it decreases enough to allow the inlet to be opened by spring tension.
Relieving Pressure. Pressure reducers also relieve increased pressure resulting from thermal
expansion. As the pressure at the reduced pressure port increases, the piston moves against the adjusting
spring, opening the return port and relieving the excessive pressure

## Slide 100
PRESSURE SWITCHES
A pressure switch is designed to open or close an electrical circuit in response to a predetermined
hydraulic pressure; the switch activates a warning or protective device. At a set minimum pressure, the
switch can turn on a light to warn the pilot, turn a pump off, or activate a solenoid-controlled valve. The
types of pressure switches, piston and diaphragm, commonly used in Army aircraft are described in the
following paragraphs.
Piston Pressure Switch. The piston pressure switch (Figure 3-3) consists of a housing, a cylinder
bore and piston, an adjustable spring for loading the piston, a microswitch and linkage for transmitting
movements of the piston to the microswitch. The housing has a pressure port for connection to system
pressure and an electrical receptable for connecting the switch to an electrical circui

## Slide 102
Diaphragm Pressure Switch. The diaphragm pressure switch consists of a housing, a diaphragm, an
adjustable spring to load the diaphragm, a microswitch, and linkage for transmitting movements of the
diaphragm to the microswitch. The housing has ports for the same functions as those in the piston
switch.
Pressure Switch Operation. The two types of pressure switches have the same operating principles;
only the piston one is covered here. Fluid pressure enters the pressure port and moves the face of the
piston against the adjustment spring

## Slide 103
When the pressure becomes great enough to overcome the force of the spring, the piston moves and
causes the pivot lever to rotate. The movement of the lever is transmitted through the linkage to the
microswitch button. This closes the electrical circuit.

## Slide 104
SUMMARY
Hydraulic systems have devices to protect against excessive pressure. These are called pressure relief
valves. The valves are adjustable and are set to open at a point slightly above maximum system
pressure. When this occurs, the fluid is returned to the system reservoir.
Pressure reducers are used to deliver the correct pressure to each component in a hydraulic system. This
makes it possible to use one hydraulic pump, delivering one set pressure in a system that requires several
different pressures.
Pressure switches are physical combinations of a hydraulic device (pressure port, piston, and sprint) and
an electrical device (microswitch and wiring). Pressure switches are used to sense hydraulic pressure.
Depending on the switch, if the pressure is too high or too low, the microswitch closes and energizes a
valve, stops or starts a pump, or illuminates a warning light.