## Slide 1: US ARMY ENGINEER SCHOOL ENGINEER CONSTRUCTION EQUIPMENT DIESEL FUEL SYSTEMS

## Slide 2
Lesson 1
MULTIPLE PUMP FUEL SYSTEMS

## Slide 3
Learning Event 1
SYSTEM COMPONENTS AND OPERATION
In the multiple pump fuel system, each cylinder has an individual injection pump
which meters the fuel and delivers it under high pressure to the spray nozzles
which lead into the combustion chambers. The pumps mounted in a common housing are
operated by a common camshaft, and utilize the same control mechanism to ensure an
equal amount of fuel in each cylinder at the proper time. The flow of fuel in a
typical multiple pump fuel system is shown in Figure 1.

## Slide 5
Diesel fuel oil flows from the supply tank through a fuel filter to the fuel supply
pump. The fuel supply pump forces the fuel through an additional filter to the
injection pumps (Figure 2). The fuel injection pumps force a measured amount of
fuel through highpressure
lines to the spray nozzles in the combustion chamber.
Surplus fuel flows from the injector pumps through a check valve on the common
housing and is returned to the fuel supply tank

## Slide 7
FUEL INJECTION PUMPS
A phantom crosssectional
view of a typical multiple pump is shown in Figure 1.
The unit is mounted on the engine in such a manner as to permit it to be driven by
the engine.

## Slide 8
The pump camshaft, near the bottom of the housing, is carried on ball bearings.
The cam lobes cause the upward movement of the plungers and springs to produce the
downward motion. The cams are arranged to activate the individual pumps in the
same sequence as the firing order of the engine to eliminate the necessity for
crossing lines leading from the pumps to the spray nozzles. On the fourstrokecycle
engine, the injection pump is driven at one half engine speed; on the twostrokecycle
engine it is driven at engine speed.

## Slide 9
The individual pumps are the lapped plunger, the constant stroke, the metering, and
the bypass. The quantity of fuel delivered to the spray nozzles is regulated by
the time the plunger covers the bypass port. The plunger stroke remains constant
at all loads. The injection must be timed to occur as demanded by the requirements
of the engine. Volumetric control is affected by rotating the plunger. Two ports
lead to the plunger barrel as shown in Figure 2 on page 3 and Figure 3; one is the
inlet port and the other is the bypass port. The plunger has a groove around its
circumference, which has a circular lower edge and helical upper edge. The space
formed is connected to the top face of the plunger through a vertical slot. Hence,
any fuel above the plunger will flow down the vertical slot and fill the helical
space. At the lower end of the plunger there are two lugs which fit in
corresponding slots in the bottom of an outer sleeve fitted around the pump barrel.
The upper portion of the sleeve is fastened to a gear segment which meshes with a
horizontal toothed rack. Any movement of the rack rotates the outer sleeve and
plunger relative to the bypass port in the stationary pump barrel.

## Slide 10
Fuel from the sump rushes into the barrel as soon as the upper edge of the plunger
opens the two opposite ports in the barrel. This action begins during the downward
stroke of the plunger and the ports remain open until the plunger starts moving
upward. After the plunger covers the ports on its upward stroke, the pressure
exerted on the fuel causes the springloaded
delivery valve to lift off its seat,
thereby, permitting the fuel to discharge into the tubing which leads to the spray
nozzle. The delivery of the fuel ceases as soon as the helix on the plunger
uncovers the bypass port in the barrel. At this instant, the pressure chamber is
connected to the sump through a vertical groove and the helix on the plunger which
relieves the pressure in the barrel. The delivery valve is quickly returned to its
seat by the combined action of its spring and the great difference in pressure that
exists between the barrel and the high pressure line. In returning to its seat,
the delivery valve performs a double function. It prevents

## Slide 12
excessive draining of the fuel from the high pressure line and relieves the
pressure in the high pressure line. This pressure relief is accomplished by an
accurately lapped displacement piston on the delivery valve. Before the delivery
valve actually reseats, it reduces the pressure in the high pressure line by
increasing the volume by a quantity equal to the volume of the displacement pist

## Slide 13
The positions of the plunger from no fuel to maximum fuel delivery are shown in
Figure 4 on page 6. For maximum delivery, the plunger is positioned in the barrel
so that it will complete its stroke before the helix indexes with the bypass port.
For zero delivery, the plunger is turned in its barrel until the vertical slot
registers with the bypass port. In this position, the pressure chamber is
connected with the sump during the entire stroke of the plunger. Any position
between no fuel to maximum fuel delivery can be obtained by moving the control rack
in or out, as the movement of the rack causes the plunger to rotate a proportionate
amount. The same rack controls the position of all the plungers simultaneously,
thereby ensuring the injection of equal amounts of fuel in each cylinder of the
engine.

## Slide 15
For proper engine performance, the fuel oil must be injected into the combustion
space in a definite spray form. This is accomplished by the spray nozzle, which is
held in the correct position in the cylinder head by the nozzle holder. The type
of unit most often used with the multiple pump system is shown in Figure 5. The
fuel delivered by the

## Slide 17
injection pump flows through the high pressure line and enters the nozzle holder
inlet stud. Then it passes through the edge filter, flows through the ducts in the
holder and nozzle body and down into the pressure chamber of the spray nozzle above
the valve seat. There, the pressure of the fuel oil acts on the differential area
of the nozzle valve. At the moment when the pressure of the fuel exceeds the
pressure exerted by the adjusting spring, the nozzle valve is lifted off its seat
and the fuel is forced through the orifices and sprayed into the combustion chamber
of the engine. The nozzle valve returns to its seat after the injection pump has
ceased to deliver fuel. The hydraulic opening pressure of the spray nozzle may
vary from 1,000 to 4,000 pounds per square inch (psi), depending on engine
combustionchamber
requirements.

## Slide 18
Spray Nozzles. Because of the requirements in the shapes of the fuel spray for
various combustion chamber designs and the wide range in engine power demands,
there is a wide variety of nozzles used with multiple pump injection systems. The
two basic groups are the pintle nozzles and the hole nozzles (Figure 6). Pintle
nozzles are generally used in engines having precombustion turbulence or divided
chambers, whereas the hole nozzles are generally used with open combustion chamber
designs.

## Slide 19
In pintle nozzles (Figure 7), the nozzle valve carries an extension at its lower
end in the form of a pin (pintle) which protrudes through the hole in the nozzle
bottom. This requires the injected fuel to pass through an annular orifice,
producing a hollow, coneshaped
spray, the nominal included angle of which may be
from 0 to 60 The
projection of the pintle through the nozzle orifice induces a selfcleaning
effect,
discouraging the accumulation of carbon at this point. A specific type of pintle
nozzle mostly used in small bore high speed diesel engines is the throttling
nozzle. It differs from the standard pintle nozzle in that the pintle projects
from the nozzle body for a much greater distance and the orifice in the bottom of
the nozzle body is much longer. These differences are readily apparent from the
crosssectional
views shown in Figure 7. The outstanding feature of the throttling
nozzle is its control of the rate at which fuel is injected into the combustion
chambers. The pintle extends through the nozzle orifice when no fuel is being
injected. Hydraulic pressure from the injection pump causes the pintle to rise for
fuel delivery.

## Slide 22
The hole nozzles have no pintles but are similar in construction to the pintle
type. They have one or more spray orifices which are straight, round passages
through the tip of the nozzle body beneath the valve seat (Figure 6). The spray
from each orifice is relatively dense and compact and the general spray pattern is
determined by the number and arrangement of the holes. As many as 18 spray holes
are provided in the larger nozzles and the diameter of these drilled orifices may
be as small as 0.006 inch. The spray pattern may or may not be symmetrical,
depending on the engine combustion chamber design and fuel distribution
requirements. The size of the hole determines the degree of atomization attained.
The smaller the hole, the greater the atomization, but if the hole is too small, it
will be impossible to get enough fuel into the chamber during the short time
allowed for injection. If the hole is too large, there will be an overrich
mixture near the nozzle tip and a lean mixture at a distance from it. Multiple
hole nozzles overcome this difficulty, because the holes can be drilled small
enough to provide proper atomization and a sufficient number can be provided to
allow the proper amount of fuel to enter during the injection period.

## Slide 23
Nozzle Holders. The nozzle holder holds the spray nozzle in its correct position
in the engine cylinder, provides a means of conducting fuel oil to the nozzle, and
conducts heat away from the nozzle. The holder also contains the necessary spring
and a means of pressure adjustment to provide proper action of the nozzle valve.
The component parts of a typical nozzle holder are shown in Figure 5 on page 7.
The body has drilled passages for conducting the fuel from the inlet connection to
the nozzle. Its lower end is provided with an accurately ground and lapped surface
which makes a leak proof and pressure tight seal with the corresponding lapped
surface at the upper end of the nozzle. The nozzle is secured by means of the cap
nut. At its upper end, the nozzle valve has an extension of reduced diameter
(referred to as the stem) which makes contact with the lower end of the spring
loaded spindle. Adjustment of the nozzle valve opening pressure is accomplished by
means of the spring pressure adjusting screw. The adjustment in other types of
holders is accomplished by means of spaces between the top of the spring and the
upper spring seat.

## Slide 24
Learning Event 2
TROUBLESHOOTING THE MULTIPLE PUMP FUEL SYSTEM
The information covered in this learning event is applicable to any item of
equipment that uses a diesel engine with a multiple pump fuel system. Component
location may vary depending on the item of equipment used. Use the appropriate
technical manual for the exact component location. The Caterpillar Model 12 road
grader will be used throughout this learning event. The applicable manual is TM 5380520915.

## Slide 25
We will begin this learning event by locating and identifying the components in the
fuel system. In order to check the fuel system, you must first make sure that you
can identify, locate, and state the function of each component in the fuel system.
The first component to locate is the fuel supply tank (Figure 8). The next item,
the fuel shutoff valve, is located on the bottom of the fuel supply tank. The
shutoff valve controls the flow of fuel from the tank to the rest of the fuel
system.

## Slide 27
Follow the fuel supply lines from the fuel supply tank to the primary fuel filter
(Figure 8 on page 11). The primary fuel filter is mounted inside the sediment bowl
(Figure 9) mounted on the fuel transfer pump housing Just below the final fuel
filter. The primary fuel filter strains out foreign material from the fuel before
it enters the fuel transfer pump.
From the primary fuel filter, the fuel flows to the fuel transfer pump (Figure 8).
The transfer pump draws fuel from the supply tank through the primary filter and
passes it to the secondary fuel filter.

## Slide 29
As the fuel flows to the secondary fuel filter, a bypass valve (Figure 8) is
provided to control the fuel pressure. The fuel transfer pump supplies more fuel
than is required for engine operation. The fuel bypass valve prevents excessive
pressure within the system. The bypass valve is installed in the fuel transfer
pump body. On this item of equipment you will not have a fuel return line to the
fuel supply tank. The bypass line is built into the pump housing.

## Slide 30
The next item to locate is the vent valve (or bleed valve) (Figure 9). This valve
is used to vent or bleed air from the fuel system. From the vent valve, the fuel
flows into the final fuel Filter (Figure 9). This filter cleans the fuel the
second time before it flows into the fuel manifold. The fuel manifold (Figure 8)
is located just to the rear of the fuel filter housing. It carries fuel to the
individual injection pumps. From the fuel manifold, the fuel is picked up by the
individual fuel injection pumps (Figure 8). Each fuel injection pump will have a
high pressure fuel line connecting the injection pump assembly and the fuel
injector.

## Slide 31
The last item in the fuel system is the fuel injection valve (Figure 10). The fuel
injection valve injects and atomizes the fuel into the combustion chamber

## Slide 33
Now that you are able to locate, identify, and state the function of each
component, you are ready to move into the troubleshooting procedures. All
troubleshooting will be done in accordance with the troubleshooting chart shown in
Figure 11. Anytime you encounter a problem with the fuel system that cannot be
pinpointed, start at the fuel supply tank and follow the system.

## Slide 36
Inspect the fuel supply tank first. Check the fuel level and drain some fuel to
check for water in the fuel. Look for leaks. Ensure the tank is securely mounted.
The next item to inspect is the fuel shutoff valve. Inspect the valve for leaks or
loose mountings.
Now inspect the fuel lines between the shutoff valve and the primary fuel filter.
Inspect the lines for leaks, broken, crushed, or loose connections. Tighten or
replace any faulty items.

## Slide 37
The primary fuel filter is the next item to inspect. Inspect the condition of the
fuel in the sediment bowl and the filter element. Clean the bowl, and replace the
filter element as necessary. Inspect all parts for cracks, breaks, and other
damage. Replace any defective parts.
The next item that may have caused the problem is a faulty fuel transfer pump.
Inspect the pump housing for cracks, leaks, or other damage.
Don't forget the fuel bypass valve. A broken spring or a piece of dirt under the
valve may cause low or no fuel pressure. Remove and replace faulty components

## Slide 38
Another problem with the fuel system is a low pressure indication while the engine
is operating. Any leaks in the line between the transfer pump and the line between
the transfer pump and the tank will result in air being drawn into the system.
Check and repair any loose or crushed lines or a leaking fuel filter gasket.
The operator of the equipment may also report good fuel pressure at the start of
the day but two hours later the equipment stopped from low fuel pressure. Check
first for a loose fuel line. Then you should check the fuel filters.

## Slide 39
A sudden drop in fuel pressure is another common problem. Again, you must look at
the items between the tank and the pump. First check the fuel tank and be sure
there is plenty of fuel. Next, inspect for a broken or loose fuel line between the
tank and the transfer pump. Also a faulty bypass valve or a broken spring may be
the problem. The last item to inspect is a defective fuel transfer pump. If the
fuel transfer pump is faulty, refer to Learning Event 3 of this lesson.

## Slide 40
Now, let's talk about the diesel engine that misfires under load and at low speed.
First, be sure the engine is at the correct operating temperature. Inspect all the
items shown on the troubleshooting chart (Figure 11 on page 14) under the heading
"diesel engine misfires or operates erratically." If this does not solve the
problem, check for correct engine speed.

## Slide 41
Learning Event 3
COMPONENT ADJUSTMENT, REPAIR, OR REPLACEMENT
During this learning event, you will be shown how to adjust, repair, or replace
components of the multiple pump fuel system. All work described will be in
accordance with the maintenance allocation chart shown in Figure 12.

## Slide 44
FUEL INJECTION VALVES
Testing Valves. Whenever an engine performs in such a manner that a fuel injection
valve is suspected of causing trouble, test all the fuel injection valves. To test
the injection valves, loosen the fuel injection line nuts at the fuel injection
pumps one at a time while the engine is running. When a nut is loosened and the
exhaust smoking is completely or partially eliminated and the irregularity in
running is not affected, this identifies the defective valve and a new one should
be installed in that cylinder.

## Slide 45
Removal.
1. Before removing a valve, clean the dirt from around the valve and connections.
2. Remove the glow plugs so they will not be damaged.
3. Loosen the fuel injection line at the pump and disconnect it from the fuel
injection valve. Install a plug in the end of the line and a cover on the
fuel injection valve (Figure 13).
4. Remove the valve retainer nut and lift out the fuel injection nozzle assembly
and body as a unit (Figure 13).

## Slide 47
Cleaning and Inspection.
1. Clean all parts with an approved cleaning solvent and dry thoroughly.
2. Inspect all parts for damage and replace any defective parts.
3. If the orifice in the nozzle becomes partially filled with carbon, remove the
nozzle assembly from the body and clean the fuel discharge hole, using the
drill and chuck supplied in the 5B1401 Cleaning Tool Group. If the valve
does not operate properly after cleaning, the nozzle should be checked for
leakage.

## Slide 48
Installation. Refer to Figures 13 and 14.
1. Screw the injection valve body into the fuel injection nozzle assembly only
finger tight.
2. Insert the nozzle assembly and valve body as a unit into the precombustion
chamber opening. Turning the body in a clockwise direction, and at the same
time pressing down will assure alignment of the serrations.
3. Install a new large seal on the retainer nut. A light coating of lubricant
on the seal will permit it to seal properly.

## Slide 50
4. Tighten the retainer nut tight to prevent leaks between the nozzle assembly
and the nozzle assembly seats. A torque of 100 to 110 footpounds
is
adequate to tighten the retainer nuts.
5. Remove the cover from the injection valve body and place a new small seal
over the threads on the top of the valve body and on the retainer nut.
6. Remove the plug from the end of the injection line and connect it to the fuel
injection valve and tighten. Remember to tighten the line connection at the
pump.

## Slide 51
PRIMARY FUEL FILTER
Removal.
1. Shut off the fuel valve on the fuel supply tank.
2. Remove the nut on the bail and remove the sediment bowl. The primary fuel
filter is mounted inside the sediment bowl (Figure 9 on page 12).
3. Remove the element assembly (Figure 15) from the cover on the fuel transfer
pump.

## Slide 53
Cleaning and Inspection.
1. Clean all parts with an approved cleaning solvent and dry thoroughly.
2. Inspect all parts for cracks, breaks, and other damage.
3. Replace the defective parts.
4. Inspect the gasket between the sediment bowl and the fuel transfer pump.
5. Replace the gasket if it is damaged.

## Slide 54
Installation.
1. Install the element assembly by screwing it into the cover on the fuel
transfer pump.
2. Place the sediment bowl in position and center the bail under the sediment
bowl.
3. Screw the nut on the bail to fasten the sediment bowl in position (Figure 15).

## Slide 55
FINAL FUEL FILTER
Removal. Refer to Figure 16.
1. Close the fuel shutoff valve on the bottom of the fuel supply tank.
2. Drain the fuel filter housing by removing the drain plug.
3. . Disconnect the fuel pressure gage line.
4. Disconnect the drain line.
5. Remove fuel filter housing retaining bolts.
6. Remove the fuel filter housing by sliding it toward the front of the engine
to clear the adapter.

## Slide 56
Installation. Refer to Figure 16.
1. Place the fuel filter housing in position and install the retaining bolts.
2. Connect the drain line.
3. Connect the fuel pressure gage line.
4. Install the drain plug.
5. Open the fuel shutoff valve.
6. Prime the fuel system.

## Slide 57
Removing Used Filter Element. Refer to Figure 16.
1. Close the fuel shutoff valve.
2. Remove the filter housing drain plug.
3. Open the fuel filter bleed valve.
4. Thoroughly clean the top of the cover and around the edges of the gasket
joint and cover to prevent dirt from dropping into the filter housing when
the cover is removed.
5. Remove the housing cover nuts.
6. Remove the housing cover

## Slide 59
7. Lift the filter element, rod, and spring from the housing (Figure 17).
Cleaning and Inspection.
1. Clean all parts with an approved cleaning solvent and dry thoroughly.
2. Clean the inside of the housing and dry thoroughly.
3. Inspect all parts for cracks, breaks, and other damage. Replace any
defective parts.
Installing New Filter Element. Refer to Figure 17.
1. Replace the spring and the rod in the housing. Make certain that the rod
enters the drilled hole in the bottom of the housing and that the spring is
piloted on the bosses of the housing and rod.
2. Place a new filter element over the rod.
3. Place a new gasket on the filter housing.

## Slide 61
4. Replace the cover.
5. Fasten the nuts.
FUEL TRANSFER PUMP
Removal. Refer to Figure 18.
1. Close the fuel shutoff valve.
2. Remove the two bolts (3) and the service meter.
3. Disconnect the drain line and fuel supply line.
4. Remove the two bolts (1) and then remove the seven bolts (2).
5. Pull the fuel transfer pump outward from the accessory drive housing

## Slide 63
Cleaning and Inspection.
1. Clean the pump and hardware in an approved cleaning solvent and dry
thoroughly.
2. Inspect the mating surfaces of the pump and filter housings for nicks, burrs,
and scratches. Replace a defective pump.
3. Inspect the pump housing for cracks, leaks, or other damages. Replace a
defective pump.
4. Inspect the gasket and replace if it is damaged.
5. Inspect all hardware for damaged threads. Replace all damaged hardware.

## Slide 64
Installation. Refer to Figure 18.
1. Place the fuel transfer pump in position and install the bolts (1) and (2).
2. Connect the drain line and fuel supply line.
3. Place the service meter in position and install the bolts (3).
4. Open the fuel shutoff valve

## Slide 65
BYPASS VALVE
Removal and Installation. Refer to Figure 19 to remove and install the plunger and
the bolts on the bypass valve.
Cleaning and Inspection.
1. Clean all parts in an approved cleaning solvent and dry thoroughly;
2. Inspect all parts for damage and replace any defective parts.
3. Ensure that the seat is smooth and flat, and that the sealing surface of the
plunger is in good condition. Replace any defective parts

## Slide 67
FUEL PRIMING PUMP
Removal and Installation. Refer to Figure 20 to remove and install the plunger,
nut (1), outlet line pump housing, nut (2), nut (3), and inlet line on the fuel
priming pump.
Disassembly.
1. Disassemble the fuel priming pump as shown in Figure 20.

## Slide 69
2. The outlet check valve may be removed by removing the outlet screw (Figure
21).
3. The inlet check valve may be removed by removing the inlet screw (Figure 21)

## Slide 71
Cleaning and Inspection.
1. Clean all parts with an approved cleaning solvent and dry thoroughly.
2. Inspect all parts for damage and replace any defective parts.
3. Inspect the 0rings
and check valves and replace if necessary.
Reassembly. Refer to Figure 20 to reassemble the fuel priming pump.

## Slide 72
FUEL INJECTION PUMP PLUNGERS
Removal. Refer to Figure 22.
1. Remove the fuel injection line from the fuel injection pump.
2. Remove the cap and felt washer under the cap.
3. Use a 1M6952 wrench to remove the fuel injection pump retaining bushing from
the fuel injection pump housing.
4. Use a 1M6954 extractor to remove the fuel injection pump from the housing.

## Slide 74
Disassembly and Assembly. Refer to Figure 23.
1. Remove the seal.
CAUTION
All disassembly and assembly
should be done with clean hands
and a clean lintfree
cloth.

## Slide 75
2. Remove the retaining ring and separate the bonnet and barrel assembly.
NOTE: Considerable care should be taken not to drop and lose the check valve and
spring retained in the bonnet,
3. Separate the spring, washer, and plunger from the barrel.
4. Remove the washer and spring from the plunger.
CAUTION
Considerable care should be taken
when removing the spring and
washer to prevent damage to the
plunger surfaces.
5. Clean all parts with clean diesel fuel and assemble, replacing any worn or
damaged parts.
CAUTION
The barrel and the plunger
assembly are matched and the
individual parts are not
interchangeable with other barrels
or plunger assemblies. Use
extreme care in inserting the
plunger into the bore of the
barrel.

## Slide 77
Installation.
1. Remove the cover on the end of the accessory drive housing and position the
fuel rack by using the 8M530 rack setting gage (Figure 24). When the rack is
properly positioned, the reading on the gage should be .000

## Slide 79
2. Align the notches on the bonnet and on the barrel with the slot in the gear
segment (Figure 25).

## Slide 81
3. Insert the assembly into the bore of the housing with the extractor. The
notches in the bonnet and the barrel must engage with the two locating dowels
in the bore of the pump housing. These dowels align the pump barrel fuel
inlet port with the fuel manifold outlet port.

## Slide 82
4. After each new plunger and barrel assembly is installed, place a new rubber
seal over the bonnet and start the retainer bushing into the housing. Push
the plunger and barrel assembly into the housing until the dowel is engaged
with the bonnet and screw the retainer bushing finger tight.
5. Tighten the bushing to the torque specified.
NOTE: Prior to installation of the plunger and barrel assembly, make certain the
lifter for the assembly to be installed is at the bottom of its stroke

## Slide 83
CAUTION
With a torque less than that
listed in the specifications, the
pump will leak. If the torque
value is greater, the housing can
be damaged.
The procedure thus far has aligned the center notch on the rack for each pump with
the center tooth of the gear segment on the injection pump plunger (Figure 26).

## Slide 85
6. The rack travel must be measured to make certain that the plunger gear
segment is properly meshed with the fuel rack. The gear segment and rack are
so constructed that the maximum travel of the rack in either direction can be
obtained only when the fourth tooth of the gear segment is meshed with the
fourth notch on the rack. If the gear segment is misplaced in either
direction, the rack travel will be reduced in both directions. It is,
therefore, necessary to measure the rack travel in only one direction to make
certain that the gear segment is properly meshed with the fuel rack. The
rack is moved to its extreme fuelon
position. A micrometer reading of .688
inch or less indicates that the gear segment is properly positioned with the
rack. The rack collar must be removed in order to obtain this much rack
travel.

## Slide 86
7. If this measurement is not obtained, the gears are improperly positioned and
the procedure must be repeated.
8. Install the felt washer and connect the fuel injection line

## Slide 87
GOVERNOR ADJUSTMENTS
High and Low Idle Speeds.
1. The low and high idle speeds can be adjusted by removing the cover on top of
the governor housing and adjusting the low idle adjusting screw or high idle
adjusting screw. Turning either screw in a clockwise direction will decrease
idle speed. The holes in the cover are shaped to act as retainers to prevent
the screws from turning after the adjustment has been made (Figure 27).
2. After setting the idling speed, move the governor control lever to change the
engine speed. Return it to the desired idle position and recheck the idle
speed. Repeat this procedure until the desired idle speed is obtained

## Slide 89
Learning Event 1
SYSTEM COMPONENTS AND OPERATION
In the unit injection system, fuel is drawn from the fuel tank (Figure 28) through
the strainer by the fuel pump. From the fuel pump, the fuel is forced under
pressure through the fuel filter. From the fuel filter, the fuel is forced into
the inlet manifold and to the inlet side of the injectors. Excess fuel or fuel not
used in engine operation is returned through the outlet manifold to the fuel tank
through the fuel return line. The fuel manifolds are cast as an integral part of
the cylinder head. The elbow or fitting from the outlet fuel manifold has a
restricted opening to maintain the proper pressure within the fuel system. The
injectors are located in the cylinder head and are protected by the valve rocker
cover. Fuel connectors in the cylinder head connect the injectors to the fuel
manifolds with fuel inlet and outlet pipes delivering fuel to and from the
injectors.
NOTE: Fuel manifolds are an integral part of the cylinder head.

## Slide 91
Injector Mounting. Unit injectors (Figure 29) combine the injection pump, the fuel
valves, and the nozzle in a single housing to eliminate the high pressure lines.
These units provide a complete and independent injection system for each cylinder
and are mounted in the cylinder head with their spray tips slightly below the top
of the inside surface of the combustion chambers. A clamp, bolted to the cylinder
head and fitted into a machined recess in each side of the injector body, holds the
injector in place in a water cooled copper tube which passes through the cylinder
head. The tapered lower end of the injector seats in the copper tube, forming a
tight seal to withstand the high pressures inside the cylinders.

## Slide 94
Injector Operation. The cross section of a typical unit injector (Figure 29) shows
the various parts. Fuel oil is supplied to the injector at a pressure of about 20
psi and enters the body at the top through the filter cap. After passing through
the finegrained
filter element in the inlet passage, the fuel oil fills the ring
shaped supply chamber between the bushing and the spill deflector. The plunger
operates up and down in this bushing, the bore of which is connected to the fuel
supply in the ring shaped chamber by two funnelshaped
ports, one on each side at
different heights

## Slide 95
The injector rocker arms (Figure 29) are actuated through push rods from the engine
camshaft. The motion of the injector rocker arm is transmitted to the plunger by
the follower, which bears against the return spring. In addition to this
reciprocating motion, the plunger can be

## Slide 96
rotated in operation around its axis by the gear, which is in mesh with the control
rack. Each injector control rack is connected by an easily detachable joint to a
lever on a common control tube which, in turn, is linked to the governor and
throttle. For metering purposes, a recess with an upper helix and a lower helix or
a straight cutoff is machined into the lower end of the plunger. The relation of
this upper helix and lower cutoff to the two ports changes with the rotation of the
plunger. As the plunger moves downward, the fuel oil in the high pressure cylinder
or bushing is first displaced through the ports back into the supply chamber until
the lower edge of the plunger closes the lower port. The remaining oil is then
forced upward through the center passage in the plunger into the recess between the
upper helix and the lower cutoff, from which it can flow back into the supply
chamber until the helix closes the upper port. The rotation of the plunger, by
changing the position of the helix, retards or advances the closing of the ports
and the beginning and ending of the injection period. At the same time, it is
increasing or decreasing the desired amount of fuel which remains under the plunger
for injection into the cylinder.

## Slide 97
Figure 30 shows the various plunger positions from noinjection
to fullload
injection. With the control rack pulled out completely (noinjection),
the upper
port is not closed by the helix until after the lower port is uncovered. With the
control rack in this position, all the fuel charge is forced back into the supply
chamber and no injection of fuel takes place.

## Slide 98
With the control rack pushed in completely (fullload),
the upper port is closed
shortly after the lower port has been covered, thus producing a full effective
stroke and maximum injection. From the noinjection
position to fullload
position
(full rack movement), the contour of the helix advances the closing of the ports
and the beginning of injection.

## Slide 99
Figure 31 shows various positions for downward travel of the plunger with the rack
in a fixed position. On the downward travel of the plunger, the metered amount of
fuel is forced through the center passage of the valve assembly, through the check
valve, and against the spray tip valve. When sufficient fuel pressure is built up,
the spray tip valve is forced off its seat and fuel is sprayed through several
small orifices (or holes) in the spray tip and atomized in the combustion chamber.
The check valve prevents air leakage from the combustion chamber into the fuel
system if the spray tip valve is accidentally held open by a small particle of
dirt, allowing the injector to operate until the

## Slide 102
particle works through the valve. On the return upward movement of the plunger,
the high pressure cylinder is again filled with oil through the ports. The
constant circulation of fresh cool fuel through the injector which renews the
surplus fuel supply in the chamber, helps to maintain even operating temperature of
the injectors. It also effectively removes all traces of air which might otherwise
accumulate in the system.
The amount of fuel circulated through the injector is in excess of maximum needs,
thus ensuring sufficient fuel for all conditions.

## Slide 103
Learning Event 2
TROUBLESHOOTING THE UNIT INJECTOR FUEL SYSTEM
The information covered in this learning event is applicable to any item of
equipment that uses a diesel engine with a unit injector fuel system. Component
location may vary depending on the item of equipment used. Use the appropriate
technical manual for the exact component location. The LeTourneauWestinghouse
model 440HA road grader will be used throughout this learning event. The
applicable manual is TM 5380523712.
We will begin this learning event by locating the components of the fuel system

## Slide 104
In order to check the fuel system, you must first make sure the fuel tank is filled
with fuel. Inspect the fuel tank cap and screen. If the fuel shows signs of water
or other contamination, drain the fuel tank and refill with clean fuel. Inspect
the fuel tank mountings and fuel lines for any signs of fuel leaks. Tighten
mountings and fuel lines as necessary.
Check the fuel shut off valve and make sure its in the open positi

## Slide 105
The next items that should be inspected are the lines from the fuel tank to the
check valve. All lines must be in good condition with no leaks. Tighten or
replace defective fuel lines. On equipment where the fuel tank is above or higher
than the engine, there will be no check valve.
Misfiring or a faulty injector tip may cause a loss of engine power.
To check for a faulty injector in a unit injector fuel system, you should hold down
each injector's follower, noting when there is no change in the engine's
performance.
A loss of compression will result if one or more of the valves are adjusted
incorrectly.
If the flared end of a fuel jumper line begins to leak, there will probably be a
dilution of the lubrication oil.
A dirty air cleaner will cause the engine to run rough and lose power.
A leak in the fuel strainer gasket will cause air to enter the fuel supply.

## Slide 106
To check for air in the fuel system, hold the fuel return line in a container of
fuel and watch closely for air bubbles.
The fuel strainer and fuel filter should be inspected next. Inspect the strainer
and filter for leaks or signs of loose lines and mountings. Drain water and
sediment from the fuel filter and strainer by opening the drain cocks on the bottom
of the filters.
Next inspect the fuel pump. Check the fuel lines for leaks or damage. Check the
fuel pump for loose mounting and damage. Observe any fuel leaks on the pump
assembly. A defective fuel pump must be replaced.

## Slide 107
The fuel manifolds are the next item in the fuel system to inspect. On this item
of equipment, the manifolds are a part of the cylinder head. Inspect the fuel line
connections to the fuel manifold. Tighten or replace any defective parts. The
fuel manifolds are held in place by the fuel connectors.
Next inspect the fuel connectors, fuel jumper lines, and injectors. The fuel
travels from the fuel connectors to the injectors through the fuel jumper lines.
Inspect the fuel lines and connectors for fuel lea

## Slide 108
As the fuel leaves the injector, it passes through the return lines to the outlet
manifold and to the restricted elbow. Notice that the elbow has the letter R
stamped on its front or side. This elbow is responsible for maintaining the fuel
pressure in the system. Without this fitting, you will not maintain the correct
fuel pressure. From the restricted elbow, the fuel flows through the return line
to the fuel tank.

## Slide 109
Learning Event 3
COMPONENT ADJUSTMENT, REPAIR, OR REPLACEMENT
During this learning event, you will be shown how to adjust, repair, or replace
components of the unit injector fuel system. All work described will be in
accordance with the maintenance allocation chart shown in Figure 32.

## Slide 111
FUEL PUMP
Inspection. Check the fuel pump for secure mounting. Tighten the mounting bolts
if necessary. Check the fuel tubes for leaks and tighten or replace tubes as
necessary.
Testing. Test the fuel flow as follows:
1. Disconnect the fuel return tube from the hose to fuel tank. Connect a hose
to the fuel return tube and hold the hose in a convenient receptacle.
2. . Start the engine and run it at 1,200 revolutions per minute.
3. Measure the fuel flow from the tube for one minute.
4. A minimum of onehalf
gallon of fuel should flow in one minute.
5. If the fuel flow is less than onehalf
gallon per minute, check the fuel
filters and service as necessary.
6. Check the fuel flow again (3 and 4 above). If the flow is still below
minimum, replace the pump using the replacement procedures

## Slide 112
Replacement. Refer to Figure 33.
1. Disconnect the fuel pumptofuel
filter fuel line from the fuel pump.
2. Disconnect the fuel strainertofuel
filter fuel line from the fuel pump.
3. Remove the three fuel pump mounting screws with the seal washers.
4. Remove the fuel pump from the blower.

## Slide 114
FUEL TANK
Inspection. Refer to Figure 34.
1. Remove the cap and check the gasket.
2. Check the overflow tube for damage.
3. Inspect the fuel tank for leaks and damage.
COLD WEATHER STARTING AID
Inspection. Check the fuel primer for damage. Operate the priming knob in the
operator's compartment and check the primer for correct operation.

## Slide 115
Removal and Installation.
1. Disconnect the cable from the priming pump.
2. Disconnect the fluid tube to the engine from the priming pump.
3. Remove the four mounting screws securing the starting aid to the engine
compartment and remove the starting aid.
4. Install the new starting aid in reverse order if removal.
FUEL FILTER AND FUEL STRAINER
General. The fuel strainer and fuel filter are mounted on the right side of the
engine forward of the blower. The fuel strainer has a cloth or socktype
element
and is connected between the fuel tank and the fuel pump. The fuel filter is
connected between the fuel pump and the fuel manifold

## Slide 116
Element Replacement. Refer to Figure 35.
NOTE: Drain the water and sediment from the filter and strainer daily.
1. Drain the filter or strainer.
2. Remove the cover screw.
3. Remove the shell from the filter cover. Remove the gasket from the cover.
4. Remove the filter or strainer element from the shell.

## Slide 119
5. Clean the shell with an approved cleaning solvent and a clean cloth.
6. After installation of new elements, prime the filter and strainer by filling
the shell with clean fuel.
7. Install the shell and cover gasket in the cover and secure with the cover
screw.
NOTE: Change the filter and strainer elements every 300 hours of operation

## Slide 120
Filter and Strainer Replacement. Refer to Figure 36.
1. Open the drain cocks, and drain the filter and strainer.
2. Disconnect the fuel tanktostrainer
fuel line from the strainer.
3. Remove the screw and washer and remove the clamp.
4. Disconnect the fuel strainertofuel
pump fuel line from the strainer and the
fuel pump.
5. Remove the two screws, lock washers, and nuts and remove the fuel strainer
from the bracket.
6. Remove the two screws and lock washers and remove the fuel strainer mounting
bracket.
7. Disconnect the fuel pumptofuel
filter fuel line from the fuel filter and
fuel pump. Remove the nylon ties and remove the fuel line.
8. Disconnect the fuel filtertofuel
manifold fuel line from the fuel filter.
9. Remove the two screws, lock washers, and flat washers and remove the fuel
filter.
10. Disconnect the fuel filtertofuel
manifold fuel line from the elbow in the
manifold. Remove the elbow from the manifold.
11. Disconnect the fuel return line from the elbow in the fuel manifold and fuel
tank return line. Remove the elbow from the manifold.

## Slide 121
12. Remove the nut and lock washer and remove the clamp and fuel return line.
NOTE: After installing, fill the filter and strainer with clean diesel fuel to
prime the fuel system.

## Slide 123
GOVERNOR LINKAGE
Inspection. Check the governor lever (Figure 37) and shutoff rod for damage and
smooth operation. Pull the ball in the operator's compartment to check the lever
and rod operation. The lever must move enough to completely close the governor to
stop the engine. If the lever or rod is damaged, replace the defective parts.

## Slide 124
Removal and Installation. Refer to Figure 37.
1. Remove the ball from the shutoff rod in the operator's compartment. Remove
the retaining ring and insulating bushing.
2. Remove the cotter pin and washer and remove the shutoff rod from the lever.
3. Remove the shoulder bolt, lock washer, and nut securing the lever to the
bracket.
4. Disconnect the lever from the ball Joint and remove the lever.
5. Remove the ball Joint from the governor rod and the rod from the governor
lever.
6. Install the new governor rod in the governor lever and connect the ball Joint
to the rod.
7. Install the lever on the bracket and secure with the shoulder bolt, lock
washer, and nut.
8. Connect the ball joint to the lever.
9. Slide the new shutoff rod into the operator's compartment through the
insulating bushing and secure with the retaining ring. Install the ball on
the rod.
10. Install the shutoff rod through the hole in the lever and secure with the
cotter pin and washer.
11. Operate the rod from the operator's compartment to check operation.

## Slide 126
THROTTLE LINKAGE
Inspection. Check the operation of the throttle linkage by depressing both foot
pedals and moving the governor control lever through complete travel. The linkage
should operate smoothly and completely control the governor. The governor control
lever should stop and hold in any position, due to friction bearings in the shaft.
Check the rods for bent condition or damage. Replace the damaged parts in the
linkage.

## Slide 127
Removal. Refer to Figure 38.
1. Remove the cotter pin and straight pin.
2. Remove the two cotter pins, washer, and straight pin.
3. Remove the acceleratordecelerator.
4. Remove the ball joint and rod from the lever.
5. Remove the cotter pin and washer.
6. Remove the cotter pin and straight pin and remove the rod and clevis

## Slide 128
Adjustment. Refer to Figure 38.
1. With the engine off, place the governor control lever against the full speed
stop (all the way back). Adjust the rod, attached to the lever through the
floor plate, until the acceleratordecelerator
rod is pulled out of its
housing 3/16 to 1/4 inch. When the governor control lever is against the low
speed stop, the rod should be pushed into the housing the same distance.
2. After making the above adjustments, adjust the length of the rod from the
pedal support to the acceleratordecelerator
to prevent either pedal from
striking the floor plate.
3. After making all the adjustments, hook a spring scale to the governor control
lever as close to the ball as possible. A pull of 8 to 25 pounds should be
required to move the lever through the full range of travel.

## Slide 129
EXHAUST VALVE CLEARANCE
General. Exhaust valve clearance at normal engine operating temperature is
important to smooth, efficient operation of the engine. Whenever the cylinder head
is overhauled, the exhaust valves are reconditioned or replaced, or the valve
operating mechanism is replaced or disturbed, the valve clearance must be adjusted
to the cold setting to allow for normal expansion as the engine warms up.

## Slide 131
Adjustment.
1. Loosen the two bolts and remove the valve rocker cover and gasket from the
engine (Figure 39).
2. Remove the two pins from the bolts and remove the two bolts and washers from
the cover.
3. Remove the two studs from the cylinder head.
4. Place the governor speed control lever in the nofuel
position.
5. Rotate the crankshaft until the injector follower on number 1 cylinder is
fully depressed.
6. Loosen the push rod locknut (Figure 40).
7. Place a 0.013inch
feeler gage (Figure 40) between the valve stem and the
rocker arm.
8. Adjust the push rod to obtain a smooth pull on the feeler gage. Remove the
feeler gage.

## Slide 132
9. Hold the push rod with a 5/16inch
wrench and tighten the locknut with a 1/2inch
wrench.
10. Check the clearance again. If the clearance is correct a 0.011inch
feeler
gage will pass freely between the valve stem and the rocker arm, but a 0.013inch
feeler gage will not.
11. Set the remaining seven exhaust valve clearances in the same manner in firing
order (1342)
sequence.
12. Stop and operate the engine until it reaches operating temperature (160°F to
185°F). Stop the engine.
13. With the engine at operating temperature, rotate the crankshaft until the
injector follower on number 1 cylinder is fully depressed.
14. Check the valve clearance as described above and as shown in Figure 40. If
the valve clearance is correct, a 0.008inch
feeler gage will pass freely
between the rocker arm and the valve stem but a 0.010inch
gage will not pass
through. Adjust the push rod, if necessary, to obtain this clearance

## Slide 135
NOTE: If the engine cools off before adjustments are completed, bring the engine
to operating temperature before continuing with the adjustments.
15. Check all valves in the same manner it firing order (1342)
sequence.
16. Refer to items 1 through 3 and install the valve rocker cover. Install the
valve rocker cover in reverse order of removal.

## Slide 136
INJECTOR TIMING
General. The injectors are timed properly when the injector follower is adjusted
to a definite height in relation to the injector body. This height varies with the
type of injectors incorporated in the engine. All of the injectors should be timed
in firing order sequence.
Adjustment.
1. Refer to Figure 39 on page 63 and remove the valve rocker cover.
2. Place the governor speed control lever in the nofuel
position.
3. Rotate the crankshaft until the exhaust valve on number 1 cylinder is fully
depressed.
4. Place the small end of an injector timing gage in the hole provided in top of
the injector body with the flat of the gage toward the injector body as shown
in Figure 41.

## Slide 137
NOTE: The injector timing gage has a timing dimension of 1.460 inches as shown in
Figure 41. The gage number is 72582J1853
and is available from General
Motors Corporation, Detroit Diesel Engine Division, 13400 West Outer Drive,
Detroit, Michigan 48239.
5. Loosen the injector rod locknut (Figure 41). Turn the push rod and adjust
the injector rocker arm until the extended part of the follower will Just
pass over the top of the injector follower.
6. Hold the push rod and tighten locknut. Check the adjustment and, if
necessary, readjust the push rod.
7. Adjust the timing of the remaining injectors in the same manner.

## Slide 138
8. Refer to Figure 39 on page 63 and replace the rocker valve cover.
GOVERNOR GAP
General. When the governor speed control lever is at fullfuel
position, a gap
must be maintained between the spacing plunger and the plunger guide in the
governor control housing.

## Slide 140
Adjustment. Refer to Figure 42.
1. Remove the governor cover.
2. Set the governor speed control lever in the fullfuel
position (all the way
back).
3. Insert a 0.006inch
feeler gage between the spacing plunger and the plunger
guide. Check the pressure on the feeler gage.
4. If necessary, loosen the locknut and turn the adjusting screw in or out until
a slight drag is felt on the feeler gage.
5. Hold the adjusting screw and tighten the locknut to secure adjustment. Check
the gap, after tightening the nut, to be sure the gap is correct. Readjust
if necessary.
6. Install the governor cover.

## Slide 141
INJECTOR RACK CONTROL
General. Properly positioned injector rack control levers determine the amount of
fuel injected into each cylinder and equalizes distribution of the load. The
control levers must be positioned with the governor at the fullload
setting.
Adjustment.
1. Adjust the governor gap.
2. Remove the valve rocker cover.
3. Disconnect the throttle linkage from the governor stop lever.
4. Loosen the locknut and back out the buffer screw (Figure 43) approximately
5/8 inch.
5. Loosen all eight inner and outer control lever adjusting screws (Figure 44 on
page 69).
6. Move the governor speed control lever (Figure 43) to the maximum speed
position (all the way back).

## Slide 144
7. Move the stop lever (Figure 44) to the run position (forward). Hold the
lever in run the position with light finger pressure.
8. Turn the inner adjusting screw (Figure 44) on No. 1 injector rack control
lever down until a step up in effort to hold the stop lever in run position
is noted. This places the No. 1 injector rack control lever in the fullfuel
position.
9. Turn down the outer adjusting screw (Figure 44) until it bottoms lightly on
the injector control tube.
10. Alternately tighten the inner and outer adjusting screws to hold adjustment.

## Slide 145
NOTE: The above step should result in placing the governor linkage and the control
tube in the same positions they will attain while running at full load.
11. Check adjustment as follows: Refer to Figure 44.
a. Hold the stop lever in the run position.
b. Press down on the injector rack control lever with a screwdriver or
fingertip, causing the injector control tube to rotate. When the control
lever is released, the injector rack should return to its original
position. If the rack does not return to its original position, the
setting is too loose. To correct, back off outer adjusting screw slightly
and tighten inner adjusting screw slightly.

## Slide 146
c. Setting is too tight if, when moving the stop lever from the stop to the
run position, the injector rack becomes tight before the stop lever
reaches the end of its travel. If this occurs, back off the inner
adjusting screw slightly and tighten outer adjusting screws slightly.
d. Continue the adjustments above until the injector control rack operates
smoothly through its complete length of travel.
e. Completion of these adjustments should establish No. 1 injector rack
control lever in the fullfuel
position

## Slide 147
12. With No. 1 cylinder fuel injector adjusted as above, adjust the remaining
injectors as follows:
a. Manually hold No. 1 injector rack in the fullfuel
position (all the way
in).
b. Turn the inner adjusting screw on No. 2 control down until No. 2
injector rack control lever has moved into the fullfuel
position and the
adjusting screw is bottoming on the injector control tube.
c. Turn the outer adjusting screw down until it bottoms lightly on the
control tube. Alternately tighten both inner and outer adjusting screws
until tight.

## Slide 149
d. Recheck No. 1 injector rack control lever to be sure it has remained snug
on the ball end of the control lever while positioning No. 2 rack. If
the rack on No. I has become loose, back off the inner adjusting screw on
No. 2 injector rack control lever slightly and tighten outer adjusting
screw slightly.
e. Continue the adjustments until No. 2 injector rack functions in accordance
with No. 1 injector rack.
13. Adjust remaining injectors in the same manner.
14. Install the valve rocker cover.
15. Connect the linkage to the stop lever.

## Slide 150
Lesson 3
ROOSA MASTER DISTRIBUTOR FUEL SYSTEMS

## Slide 151
Learning Event 1
SYSTEM COMPONENTS AND OPERATION
General. The Roosa Master pump is of the single cylinder, opposed plunger, inlet
metering, distributor type. Simplicity is the prime advantage of this design. It
contributes to the ease of manufacture and servicing, lower maintenance costs,
greater dependability, and ability to operate at greater speeds than conventional
types. Since the basic Roosa Master model has eighty parts and only three main
rotating members, there is less chance of part failure. With the development of
smaller diesel engines with greater engine speeds, a simplified injection system is
needed. The problem is solved with the distributor type fuel pump. There are no
spring loaded lapped surfaces, no ball bearings or gears, and most accessories are
built in. Selflubricated
by the filtered fuel, the unit operates in any position
and has the same number of parts regardless of the number of cylinders served.

## Slide 152
A mechanicalcentrifugal
governor is an integral part of the pump. The governor
controls fuel delivery and therefore engine speed. Drive for the governor is
supplied by the pump drive shaft.
A transfer pump, mounted on the front of the pump, draws fuel from the tank and
delivers it to the injection pump. The transfer pump is of the positive
displacement, vane type. Lubrication for the pump is supplied by the fuel oil. No
other lubrication is required.
A switch, mounted on top of the pump, controls fuel flow out of the pump. The
switch activates a solenoid, which when energized, opens the metering valve and
allows fuel to flow from the pump to the engine. When the master switch on the
instrument panel is placed in the off position, the solenoid closes the valve,
ending fuel delivery and stopping the engine.

## Slide 153
Charging Cycle. As the rotor revolves, the charging passage in the rotor registers
with one of the charging ports in the charging ring. Fuel, at transfer pump
pressure, then passes into the pumping cylinder, forcing the plungers apart a
distance proportionate to the amount of fuel required for injection on the
following stroke. Only at full load will the plungers move to the most outward
position, controlled by the leaf spring setting (maximum fuel adjustment).
While the charging passage in the rotor is in register with one of the charging
ports in the hydraulic head, the discharge passage is out of register with the head
outlet poet. The rollers are between the cam lobes.

## Slide 154
Discharging Cycle. As the rotor continues to revolve, the charging passage passes
out of register with the charging port. For a brief interval the fuel is trapped
until the rotor discharge passage registers with one of the head outlet ports. As
this registration takes place, both rollers contact the rise of the cam lobes and
are forced together. This is the discharge or injection stroke. The fuel trapped
between the plungers is forced through the axial passage and out one of the head
outlet ports to an injection nozzle.

## Slide 155
Metering Units. The metering pump is a closely fitted reciprocating pump,
obtaining its motion through a link from the plunger lever. The plunger lever
(Figure 45) is operated by a vertical lever controlled in turn by an eccentric
rocker lever running directly off a cam on the fuel pump main shaft. The position
of the vertical lever in the eccentric of the rocker lever determines the travel of
the plunger lever and, consequently, the travel of the metering plunger. As the
metering plunger starts upward on its controlled stroke, it pushes fuel to the
injector through passages formed by the rotating distributor disk. The stroke of
the metering plunger, which determines the amount of fuel going to each injector,
is varied by changing the position of the vertical lever between the stop pins in
the cam rocker lever. When the roller is against the inside stop pin, there is no
travel on the vertical lever or on the metering plunger, therefore, no fuel is
going to the engine. If the vertical lever is moved over to the outside pin, the
stroke of the metering plunger is sufficient to deliver enough fuel to the engine
for full speed and load.

## Slide 156
Injector. The injector consists of a forged body with a properly fitted plunger
(Figure 46 on page 80). This plunger is forced down against spring action by a
rocker arm activated by push rods from the engine camshaft. Mounted on the end of
the body is the cup which contains the nozzle tip. On the intake stroke of the
engine, the fuel metering pump forces a charge of fuel of the exact amount
necessary to meet the load and speed of the engine into this cup.

## Slide 158
Operation. The operation of the metering pump requires that the fuel line and
passage leading to the cup be filled with fuel (1, Figure 47 on page 80). It
naturally follows that any fuel added at the fuel metering pump end will push the
same amount of fuel into the injector cup. The fuel lies in the cup during the
compression stroke of the engine and the compressed air is forced through the small
spray holes in the cup. The fuel oil in the tip of the cup is exposed to the
intense heat and blasting of the compression and is thus preheated and broken up
(2, Figure 47). A few degrees before top center, the plunger Ls forced down and
the preheated fuel charge is driven out into the cylinder (3, Figure 47) and the
plunger ends its stroke (4, Figure 47). A small check valve is located in the
lower end of the fuel passage in the injector body. This check valve prevents the
compression pressures from blowing the fuel back and filling the lines with air.

## Slide 161
Learning Event 2
TROUBLESHOOTING THE ROOSA MASTER FUEL SYSTEM
The information covered in this learning event is applicable to any item of
equipment that uses a Roosa Master fuel system on the engine. Component location
may vary depending on equipment used. Use the appropriate technical manual for the
exact component location. The AllisChalmers
Model 645M scoop loader will be used
throughout the remainder of this lesson. The applicable manual is TM 5380523912.
We will begin this learning event by locating and identifying the components of the
fuel system. In order to troubleshoot the fuel system, you must make sure that you
can identify, locate, and state the function of each component

## Slide 162
The main components of the fuel system include the fuel tank, fuel sediment bowl,
hand primer pump, fuel filters, transfer pump, fuel injection pump, fuel injection
nozzles, and the fuel lines. Two systems comprise the overall fuel system for the
engine. A low pressure system brings the fuel from the tank through the sediment
bowl, primer pump, and fuel filters, to the transfer pump, and the return lines to
the tank. The high pressure system includes the fuel injection pump, fuel lines to
the injectors, and the injectors. Figure 48 on page 82 shows the fuel system in
order of flow

## Slide 163
Fuel Tank. The fuel tank is mounted at the rear of the loader beneath the
radiator. The filler pipe extends through the radiator grill for access in filling
the tank. A fuel tank drain is located on the bottom of the tank for draining
purposes.
Fuel Sediment Bowl. Follow the fuel supply line from the fuel tank to the fuel
sediment bowl. It is mounted on a bracket along the frame on the left side of the
engine near the fuel injection pump. This component acts as a primary fuel filter.
Hand Primer Pump. The hand primer pump is mounted on the same bracket as the
sediment bowl. It is used to prime the system after replacement of the fuel filter
or cleaning of the fuel sediment bowl.

## Slide 164
Secondary Fuel Filter. Sometimes called a combination fuel filter is located on
the left side of the engine. The secondary filter provides additional cleaning of
the fuel before it enters the fuel pump.

## Slide 166
Fuel Injection Pump. The Roosa Master fuel pump is mounted at the front of the
engine on the left side. The function of the fuel pump is to draw fuel from the
tank and send fuel to the injectors under high pressure.
Fuel Injection Lines. From the fuel pump, the pressurized fuel flows through
individual lines to each injector. Remember, these lines carry high pressure fuel
to each injector.

## Slide 167
Fuel Injection Nozzle. Each cylinder is supplied with fuel through an injection
nozzle. The high pressure fuel enters through the nozzle ports and is atomized
instantly within the cylinder to combine with the air to provide the explosive
mixture.
Fuel Return Line. The fuel return line carries unused fuel from the injectors back
to the tank.
You are troubleshooting the scoop loader fuel system and determine that there is a
loss of fuel to the fuel pump. Now you must check the following components in the
low pressure tank system to correct the problem. The first components that should
be inspected are the fuel tank and shutoff valve.

## Slide 168
Check the tank and shutoff valve for leakage. Make sure the valve is in the open
position and that the tank has been filled with fuel. Check all fuel lines from
the tank to the Roosa Master pump for leakage or damage that could cause the loss
of fuel. Check the primary filter for a cracked or leaking sediment bowl, damaged
gaskets, or leaks at the fuel Line fittings.
Check the hand primer for external leaks and make sure the pump is pushed into the
pump body and locked in place by the pump bail. Check the secondary filter for
leaks or a loose bleed screw. And finally, check the pump for leaking lines.

## Slide 169
The next troubleshooting problem is a rough or erratic running engine. Leaking
fuel lines or air in the fuel lines will cause a rough running engine. Because you
have already checked the low pressure side of the system, this inspection will
cover the fuel flow from the Roosa Master pump to the injectors. Check the pump
and high pressure fuel outlet fittings for leaks or damage. Check each injector
for signs of leakage. Start the engine to check each injector for proper
operation. Loosen each injector inlet connector one at a time in sequence and wrap
a rag around the fitting to prevent fuel spray. If the engine runs worse with
number one injector line loose, that is not the faulty injector. Continue checking
until you find the injector that does not cause a change in engine operation with
the inlet line loose. Check the fuel injectors.

## Slide 170
If the scoop loader engine fails to start and you have checked the fuel tank for
proper servicing, you should check the electrical solenoid connections on the Roosa
Master pump. If the solenoid does not open, the fuel will not flow into the pump.
Check the solenoid wire for proper installation, cleanliness, and security

## Slide 171
Another problem you my have with the scoop loader is that the engine stops
frequently. This is an idle speed problem. See Learning Event 3 of this lesson
for low and high idle speed adjustment

## Slide 172
Learning Event 3
COMPONENT ADJUSTMENT, REPAIR, OR REPLACEMENT
During this learning event, you will be shown how to adjust, repair, or replace
components of the Roosa Master fuel system. All work described will be in
accordance with the maintenance allocation chart shown in Figure 49.

## Slide 174
FUEL FILTER ELEMENT
Replacement and Installation. Refer to Figure 50.
1. Remove the vent plug.
2. Remove the screw and gasket.
3. Inspect the gasket and replace if necessary.
4. Remove the retaining ring.
5. Remove and discard the element.
6. Remove the body. Check the rubber seat and spring. Clean the body with a
clean cloth and cleaning solvent.
7. Remove the drain plug and drain the fuel filter before servicing.
NOTE: After installing the new fuel filter element, vent the system by loosening
the vent plug and pumping the fuel primer until the flow of fuel around the
vent plug is free of air bubbles. Tighten the vent plug.
NOTE: Service the fuel filter every 500 hours

## Slide 175
FUEL SEDIMENT BOWL
Replacement and Installation. Refer to Figure 51.
1. Loosen the bowl nut and move the bail to one side.
2. Remove and empty the fuel sediment bowl.
3. Clean the bowl with a clean cloth.
4. Check the bowl gasket and replace if necessary.
5. Install the fuel sediment bowl and secure with the bail and screw.
6. Vent the fuel system.

## Slide 178
LOW PRESSURE FUEL SYSTEM
Venting and Priming. After replacement of the fuel filter or cleaning the sediment
bowl, vent and prime the fuel system as follows:
1. Loosen the vent plug in the top of the fuel filter.
2. Remove the screw and move the bail on the fuel primer pump to one side.
3. Move the primer pump plunger back and forth in a pumping motion to pump the
fuel through the fuel filter.
4. Continue pumping until the fuel filter has been filled with fuel and the flow
of fuel around the vent plug is free of air bubbles.
5. Tighten the vent plug securely into the top of the fuel filter.
6. Install the bail an the primer pump and secure with the locking screw.

## Slide 179
HIGH PRESSURE FUEL SYSTEM
Venting and Priming. If fuel lines have been removed, the engine has run out of
fuel, or if the loader has not been operated for sometime, it may be necessary to
vent the high pressure system to facilitate starting the engine. The correct
venting procedures are as follows:
1. Disconnect the fuel lines at all six nozzles and holders (Figure 52).
2. Depress the accelerator and crank the engine.
3. Observe the fuel lines and check to see that the fuel flows from each line
with no air bubbles present. Discontinue cranking.
4. Connect the lines to the nozzle holders and tighten securely.

## Slide 180
HAND PRIMER PUMP AND SEDIMENT BOWL
Removal and Installation.
1. Disconnect the fuel lines from the sediment bowl and primer pump

## Slide 182
2. Remove the two screws, nuts, and lock washers securing the hand primer pump
to the bracket.
3. Remove the hand primer pump and sediment bowl from the bracket.
4. Remove the sediment bowl from the fitting in the hand primer pump.
5. To install the hand primer pump and sediment bowl reverse the procedures
above.

## Slide 183
THROTTLE LINKAGE
Removal and Installation. Refer to Figure 53.
1. Disconnect the two ball joints, and remove the clamp and rear rod.
2. Disconnect the two ball joints, and remove the front cod.
3. Remove the four Jam nuts and lock washers, two lever bearings, and cross over
lever.
4. Remove the two cotter pins, the pivot pin, and the accelerator.
5. Remove the pedal spring and limit control rod.
6. Install the throttle linkage in reverse order of removal.

## Slide 184
Adjustment.
1. With the rear rod disconnected from the speed control lever, start the
engine, rotate the low speed adjustment screw in or out to set the low idle
speed. Rotate the high speed adjustment screw to set the high idle speed.
2. Connect the rear rod to the speed control lever. Adjust the length of the
rod to have the low speed adjustment screw against the lever stop when the
accelerator is fully released.

## Slide 185
COLD WEATHER STARTING AID
Removal. Refer to Figure 54.
1. Remove the two screws and disconnect the control cable. Remove the clamp
from the top of the hydraulic tank and control knob and remove the cable.

## Slide 188
2. Disconnect the latch and unscrew the cylinder from the valve. Install the
cap on the valve.
3. Disconnect the outlet tube from the valve and disconnect the injector from
the manifold. Install the plug in the manifold after removing the injector.
4. Remove the two screws and nuts and valve from the valve bracket.
5. Remove the two screws and nuts and valve bracket.
6. Remove the two screws and nuts and latch bracket.

## Slide 189
FUEL FILTER
Removal and Installation. Refer to Figure 55.
1. Disconnect the fuel lines from the fuel filter.
2. Remove the four screws and lock washers securing the fuel filter to the
bracket.
3. Remove the fuel filter from beneath the bracket

## Slide 190
FUEL TRANSFER STRAINER
Removal and Installation. Refer to Figure 56.
1. Disconnect the filter to the pump inlet line, and remove the elbow.
2. Remove the end plate sleeve and strainer.
3. Clean strainer, and install the strainer and end plate sleeve in the pump.
4. Install the elbow and connect the filter to the pump inlet line.
5. Prime and vent the fuel system if necessary.

## Slide 193
Lesson 4
PRESSURETIMED
FUEL SYSTEMS

## Slide 194
Learning Event 1
SYSTEM COMPONENTS AND OPERATION
The pressuretimed
injection system (Figure 57) has a metering system that is based
on the principle that the volume of liquid flow is proportional to the fluid
pressure, the time allowed to flow, and the size of the passage the liquid flows
through. The operation of the system is as follows:
1. A fuel tank with a vented filler cap stores the fuel supply.
2. Fuel is supplied from the tank to the pressuretimed
gear (PTG) pump through
the delivery line. An inline filter is placed in series in the line to trap
foreign matter and moisture.
3. A return line from the PTG pump to the fuel tank is provided to bleed off
excess fuel so that operating pressures can be regulated.
4. The PTG pump delivers controlled amounts of fuel to the pressuretimed
delivery (PTD) injectors

## Slide 196
5. Delivery of fuel to the PTD injectors is through a common rail type delivery
line.
6. A common rail type return line connects the PTD injectors to the fuel tank so
that excess fuel may be delivered back to the fuel tank.
PTG Injection Pump (Figure 58). The PTG pump is driven by the engine at a onetoone
speed ratio. The pump contains four main components. These four components
and their respective operations are as follows:

## Slide 197
1. The gear type pump draws fuel from the supply tank and forces it through the
pump filter screen to the governor. It is driven by the pump main shaft and
picks up and delivers fuel throughout the fuel system. A pulsation damper
mounted to the gear pump contains a steel diaphragm that absorbs pulsations
and smoothes fuel flow through the fuel system. From the gear pump, fuel
flows through the filter screen to the governor screen. The PTG pumps are
equipped with a bleed line that is attached to the engine injector return
line or to the tank. This prevents excessive fuel temperature within the
fuel pump by using the surplus fuel as a coolant. The bleed line functions
primarily when the pump throttle is set at

## Slide 199
idle speed, but gear pump output is high due to engine operating speed, as
occurs during downhill operation. A special check valve and/or fitting is
used in the gear pump to accomplish the bleed action.

## Slide 200
2. The governor controls the flow of the fuel from the gear pump, as well as the
maximum and idle speeds. The mechanical governor is actuated by a system of
springs and weights and has two functions. First, the governor maintains
sufficient fuel for idling with the throttle control in idle position;
second, it will restrict fuel to the injectors above maximum rated
revolutions per minute (rpm). The idle springs (in the governor spring pack)
position the governor plunger so the idle fuel port is opened enough to
permit passage of fuel to maintain engine idle speed. During operation
between idle and maximum speeds, fuel flows through the governor to the
injector in accordance with the engine requirements, as controlled by the
throttle and limited by the size of the idle spring plunger counterbore on
the PTG fuel pumps. When the engine reaches governed speed, the governor
weights move the governor plunger, and fuel flow to the injectors is
restricted. At the same time, another passage opens and dumps the fuel back
into the main pump body. In this manner, engine speed is controlled and
limited by the governor, regardless of throttle position. Fuel leaving the
pump flows through the shutdown valve, inlet supply lines, and into the
injectors.

## Slide 201
3. The throttle provides a means for the operator to manually control engine
speed above idle as required by varying operating conditions of speed and
load. In the PTG pump, fuel flows through the governor to the throttle
shaft. At idle speed, fuel flows through the idle port in the governor
barrel, past the throttle shaft. To operate above idle speed, fuel flows
through the main governor barrel port to the throttling hole in the shaft.

## Slide 202
4. The fuel shutdown valve is located on top of the fuel pump. It shuts off
fuel to the injectors. With the master switch on, the solenoid opens the
valve. With the switch off, the springloaded
valve returns to the off
position. In case of an electrical failure, rotation of the manual knob
clockwise will permit fuel to flow through the valve. The knob is located on
the front of the valve.

## Slide 203
PTD Injectors (Figure 59). A PTD injector is provided at each engine cylinder to
spray the fuel into the combustion chambers. The PTD injectors are of the unit
type, operated by an enginebased
camshaft. Fuel flows from a connection at the
top of the fuel pump shutdown valve through a supply line into the lower drilled
passage in the cylinder head at the front of the engine. A second drilling in the
head is aligned with the upper injector radial groove to drain away excess fuel. A
fuel drain at the flywheel end of the engine allows return of the unused fuel to
the fuel tank. There are four phases of injector operation.

## Slide 204
1. Metering (1, Figure 59). This phase begins with the plunger Just beginning
to move downward and the engine is on the beginning of the compress ton
stroke. The fuel is trapped in the cup, the check ball stops the fuel from
flowing backwards, and the fuel begins to be pressurized. The excess fuel
flows around the lower annular ring, up the barrel, and is trapped there.
2. Preinjection (2, Figure 59). The plunger is almost all the way down, the
engine is almost at the end of the compression stroke and the fuel is being
pressurized by the plunger.

## Slide 205
3. Injection (3, Figure 59). The plunger is almost all the way down, the fuel
is injected out the eight orifices, and the engine is on the very end of the
compression stroke.
4. Purging (4, Figure 59). The plunger is ail the way down, injection is
finished, and the fuel is flowing into the injector, around the lower annular
groove, up a drilled passageway in the barrel around the upper annular
groove, and out through the fuel drain. The cylinder is on the power stroke.
During the exhaust stroke, the plunger moves up and waits to begin the cycle
all over again.

## Slide 207
Learning Event 2
TROUBLESHOOTING THE PRESSURETIMED
FUEL SYSTEM
The information covered in this learning event is applicable to any item of
equipment that uses a pressure time fuel system. Component location may vary
depending on equipment used. Use the appropriate technical manual for the exact
component location. The BucyrusErie
Model 22BM crawler crane shovel will be used
throughout the remainder of the lesson. The applicable manual is TM 5381028912.
We will begin this learning event by locating and identifying the components in the
fuel system.

## Slide 208
The first item to locate and inspect is the fuel tank and fuel cap strainer. The
fuel tank is located at the back of the cab and directly below the engine. Inspect
the tank for leaks and loose mounting bolts or fuel line connections. Tighten as
necessary. Check the tank cap strainer for cleanliness and be sure the cap vent is
open. Have the operator service the fuel tank and fuel cap strainer as required.
Follow the fuel supply lines from the fuel tank to the primary fuel filter. Check
for leaks and crushed or damaged places on the fuel lines. All leaking or damaged
lines must be replaced.

## Slide 209
Next locate the primary and secondary fuel filters. They are located on the left
side of the engine. The fuel flows into the primary filter first. The primary and
secondary filters have a common filter head and a drain valve in each filter body
to drain any water or dirt which has been filtered from the fuel.
After the fuel leaves the secondary filters, it continues through a flexible line
to the fuel transfer pump which is mounted on the left side of the engine just
forward of the filters. The transfer pump has a filter screen which should be
checked for signs of leakage and will require normal servicing

## Slide 210
From the transfer pump, the pressurized fuel flows into the fuel inlet manifold
which is mounted on the left side of the engine.
The manifold distributes fuel to each injector. Check the manifold lines for any
damage or loose fittings.

## Slide 211
From the inlet manifold the fuel flows through an inlet connector to the injector.
The inlet tube connector contains a very small screen which acts as a final filter
for the fuel entering the injector. The inlet connectors and injectors are located
on the left side of the engine. Each injector and inlet connector fitting should
be checked for security and leakage.
The fuel pump will always supply more fuel to the injector metering valve than will
be used for engine operation. The drain or return manifold will return this excess
fuel to the tank through a return line. The drain manifold is similar in
appearance to the inlet manifold. The drain manifold should be checked for secure
mounting and leakage.

## Slide 212
Now that you are able to locate and state the function of each component in the
fuel system, you are ready to move into troubleshooting procedures. We will start
with some of the simple problems and continue to the more complex areas that you
would encounter to keep equipment in good operating condition.
You are assigned to troubleshoot a piece of equipment that has a loss of engine
power during operation. If the fuel line between the tank and the pump develops a
leak, air will be drawn into the system. This will cause the engine to run rough
and lose power

## Slide 213
You also notice that the engine misfires or surges, gaining or losing speed. These
are also symptoms of an air leak in a fuel line. The corrective action for this
problem is to check all fuel lines for any loose connections or cracks. Any loose
lines should be tightened and cracked lines or fittings replaced.
A loss of engine power can be caused by fuel contamination. It is a good practice
to drain a small amount of fuel from the tank and filters daily to remove any water
or dirt particles which will contaminate the fuel system. Encourage your operators
to drain these items daily.

## Slide 214
A dirty filter will also restrict the flow of fuel causing a loss of power. If you
think the fuel filters are clogged, this problem can be checked with the help of a
vacuum gage. The gage should be connected between the outlet port of the filters
and inlet port of the fuel pump with a tee fitting. Refer to the TM for a fuel
flow problem for the particular engine you are working on.

## Slide 215
Remember, the filter screens in the inlet connector screens must be cleaned and the
filter elements replaced.
The next problem is an engine which is smoking excessively while idling or under a
load. Excessive black smoke means that there is not enough air to burn all the
fuel reaching the cylinders.
The component to check is the air cleaner. Rave the operator open the air cleaner
and clean or replace it.

## Slide 216
Learning Event 3
COMPONENT ADJUSTMENT, REPAIR, OR REPLACEMENT
During this learning event you will be shown how to adjust, repair, or replace
components of a pressure time fuel system. All work described will be in
accordance with the maintenance allocation chart shown in Figure 60.

## Slide 218
Fuel Pump Service. Refer to Figure 61.
1. Remove the filter screen cover on top of the main housing.
2. Lift the cap, spring, and filter screen assembly from the main housing.
3. Discard the fiber filter screens.
4. Clean the metal filter screens with approved solvent and blow dry with
compressed air.

## Slide 220
Fuel Lines and Fittings Replacement. Refer to Figure 62.
1. Remove the fuel inlet manifold by loosening the tube and nut at each
injector. Remove the cap screw holding the tube support to the engine.
2. Remove the fuel drain manifold by loosening the tube nut at each injector.
Remove the cap screw and clip holding the manifold to the engine.

## Slide 222
Shutdown Valve Replacement. Disconnect the shutdown valve from the fuel pump by
removing the cap screw, two lock washers, and two flat washers. Discard the used
preformed packing. Install the shutdown valve, using new preformed packing.
Reassemble in reverse order

## Slide 223
Air Cleaner Replacement.
1. Remove the screw from each mounting ring.
2. Remove the screw from the outlet clamp.
3. Remove the air cleaner assembly.
Fuel Filter Replacement. Refer to Figure 63 and disassemble, replace, or clean the
fuel filters. Discard the filter cartridge assemblies. Wash the strainer element
and filter bodies in an approved cleaning solvent; blow dry with compressed air.

## Slide 225
Primer Assembly Replacement. Replace the primer unit (cold weather starting aid
"quick start") by loosening the holding clamp and removing the canister. Discard
properly, and install new unit in reverse order.
Throttle Control Replacement. Refer to the exploded view of the throttle control
assembly (Figure 64) to replace the throttle control.

## Slide 227
Fuel Tank Replacement. Refer to the exploded view of the fuel tank (Figure 65) to
replace the fuel tank.

## Slide 229
Lesson 5
FUEL SUPPLY UNITS

## Slide 230
Learning Event 1
FUEL SUPPLY PUMPS
General. Fuel injection pumps must be supplied with fuel oil under pressure
because they have insufficient suction ability. Therefore, all injection systems
require supply pumps to transfer fuel from the supply tanks to the injector pumps.
Pumps used for this purpose have a positive suction lift and their performance is
largely independent of any reasonable variations in viscosity, pressure, or
temperature of the fuel. The pumps in use today are of the vane, plunger, or gear
types.

## Slide 231
Vane Type. The fuel oil pump shown in Figures 66 and 67 is a vane type. An
integral steel rotor and shaft, one end supported in the pump flange and the other
end in the cover, revolves in the body, the bore of which is eccentric to the
rotor. Two sliding vanes are placed 180 degrees apart in slots in the rotor and
are pressed against the body bore by springs in the slots. Two oil seals on the
pump shaft prevent leakage of fuel or lubricating oil. A drain hole between the
two seals leads to the atmosphere. When the shaft is rotated, the vanes pick up
fuel at the inlet port and carry it around the body to the outlet side, where the
fuel is discharged. Pressure is produced by the wedging action of the fuel as it
is forced toward the outlet port by the vane. A springloaded
horizontal relief
valve is provided in the cover of the pump, connecting the inlet and outlet ports,
and opens at a pressure of approximately 55 psi. This valve does not normally open
since its purpose is to relieve excessive pump pressure if any of the fuel lines or
filters become plugged and build up an extremely high pressure in the pump. When
the relief valve opens, fuel passes from the discharge side (pressure side) to the
suction side of the pump.

## Slide 234
Plunger Type. The plungertype
pump shown in Figure 68 is usually mounted directly
on the housing of the injection pump and is driven by the injection pump camshaft.
It is a variablestroke,
selfregulating,
plungertype
pump that will build
pressure up to a predetermined point. As the injection pump cam allows the plunger
to be forced by its spring toward the camshaft, the suction effect created opens
the inlet valve and permits the fuel to enter the plunger spring chamber. As the
cam lobe drives the plunger against its spring, the fuel is forced by the plunger
through the outlet valve and around into the chamber created in back of the plunger
by its forward movement. As the injection pump cam continues to rotate, it allows
the plunger spring (which is now under compression) to press the plunger backward
again, forcing the fuel oil behind the plunger out into the fuel line leading to
the filters and injection pump. At the same time, the plunger is again creating a
suction effect, which allows additional fuel to flow through the inlet valve into
the spring chamber. This pumping action continues as long as the fuel is being
used by the injection pump fast enough to keep the supply pressure from rising to
the point where it equals the force exerted by the spring on the plunger. The
pressure between the supply pump and the injection pump holds the plunger
stationary against the spring and away from the rod. This prevents further pumping
action until the pressure drops enough to permit the plunger to resume operation.
This entire cycle is automatic and continues as long as the engine is running.

## Slide 236
Gear Type. The fuel pump shown in Figure 69 is a positive displacement gear type
pump. Drive for the fuel pump is supplied from the blower. The shaft rotates in
two oil seals to prevent leakage. The pump cover and body are set on two dowel
pins to assure correct shaft alignment. The cover and body mating surfaces are
perfectly flat and require no gasket. Two gears provide the pumping action. A
relief valve in the pump body will bypass fuel to prevent excessive discharge
pressures

## Slide 238
Learning Event 2
GOVERNORS
General. All diesel engines require governors to prevent overspeeding of the
engines under light loads. Automotive diesel engines also demand control of the
idling speed. Any of the installations provide a variable speed control which, in
addition to controlling minimum and maximum speeds, will maintain any intermediate
speed desired by the operator. Engine speed in a diesel engine is controlled by
the amount of fuel injected. The injection system is designed to supply the
maximum amount of fuel which will enable the engine to operate at full load and
reach a predetermined maximum speed. However, if the maximum fuel charge was
supplied to the cylinder with the engine operating under "partial load" or "no
load," the engine speed would increase beyond the critical range and soon cause
failure. The governor must control the amount of fuel injected in order to control
the engine speed.

## Slide 239
Actuation. Governors may be actuated through the movement of centrifugal
flyweights or by the airpressure
differential produced by a governor valve and
venture assembly. The centrifugal flyweight type may incorporate a mechanical
linkage system to control the injection pump or it may include a hydraulic system
to transmit the action of the weights to the pump. Where the rate of acceleration
must be high, the governorcontrolling
weights must be small to obtain the required
rapidity of response from the governor. These small weights may not exert
sufficient force to control the injection equipment; instead, the injection pump
will be controlled by a servo piston utilizing the pressure from a pump within the
governor. The centrifugal weights actuate a valve which controls the amount of oil
going to the servo piston.

## Slide 240
Mechanical (Centrifugal). The operation of the mechanical governor is based on the
centrifugal force of rotating weights counterbalanced by springs. When the speed
of the engine increases, the weights fly outward, pulling with them suitable
linkage to change the setting of the injection pump control rod. The governor
linkage is connected to the injection pump in such a manner that the spring moves
the control mechanism toward the fullfuel
position, and the action of the
flyweights reduces the amount of fuel delivered. A typical variable speed governor
is shown schematically in Figure 70 on page 124.

## Slide 242
With this type of governor, the operator varies the governor spring tension to
control the quantity of fuel and does not at any time move the injector control
rack directly. The control rack of the injection pump is connected to the yoke of
the governor in such a manner that any movement of the yoke will directly affect
the quantity of the fuel injected. The spring tension is controlled by the
operating lever, the movement of which is determined by the position of the foot
throttle. The travel of the operating lever is limited by the idle and maximum
speed screws. With the weights fully collapsed (engine stopped), the spring moves
the sliding sleeve and yoke so the fuel injection pump is in the fullfuel
position. When the weights are fully extended, the sliding sleeve and yoke move to
the right and decrease the amount of fuel delivered.

## Slide 243
If the load on the engine is decreased, the engine tends to accelerate. However,
when the engine accelerates, the governor flyweights move outward as a result of
increased centrifugal force. Since the flyweights are in contact with the sliding
sleeve assembly, this movement causes a longitudinal movement of the sleeve to the
right. This movement continues until an equilibrium is established between the
governor spring force and the centrifugal exerted by the flyweights. This occurs
when the engine returns to the original speed as determined by the position of the
foot throttle and its effect on the governor spring

## Slide 244
If the load on the engine increases, the engine tends to slow down, thereby causing
an inward movement of the flyweights. As the weights move inward, the compressed
governor spring shifts the sleeve to the left until the spring force and the
centrifugal force exerted by the flyweights are again balanced. In this way, the
yoke, following the movement of a sliding sleeve, moves the control rack of the
fuel injection pump toward the morefuel
position and thereby returns the engine to
the preset speed

## Slide 245
To accelerate the vehicle, the foot throttle is depressed, which, in turn increases
the spring tension. This causes the yoke to pivot to the left, thereby increasing
the supply of fuel. The flyweights move outward as a result of increased engine
speed and prevent the control rack from reaching the fullfuel
position unless the
foot throttle is depressed. Deceleration is accomplished in the reverse manner.
Spring pressure is decreased, the engine slows down, the flyweights move inward,
and a balanced condition between the flyweights and the spring is obtained at a
lower engine speed.

## Slide 246
The adjustable bumper spring prevents rapid oscillations of the control rack at low
noload
engine speeds. The spring contacts the yoke at idling speed and ensures
steady operation of the governor. The bumper spring also assists in preventing
stalling of the engine on sudden deceleration to idle speed, as it prevents the
control rack of the injection pump from moving into the fullstop
position when
this speed change occurs.

## Slide 247
Pneumatic (Vacuum Controlled). The actuating force for the pneumatic or vacuumcontrolled
governor (Figure 71) is the pressure drop caused by the velocity of air
passing through a venturi located in the air intake manifold. The governor
consists essentially of an atmosphericsuspended
diaphragm connected by linkage to
the control rack of the fuel injection pump. The chamber on one side of the
diaphragm is open to the atmosphere and the chamber on the other side is sealed and
connected to the venturi in the manifold. In addition, there is a spring acting on
the sealed side of the chamber, which moves the diaphragm and control rack to the
fullfuel
position when the engine is not operating and both sides of the diaphragm
are at atmospheric pressure

## Slide 248
When the engine is running, however, the pressure in the sealed chamber is reduced
below the atmospheric pressure existing in the other chamber. The amount of
pressure reduction depends on the position of the governor valve and the speed of
the engine. It is this pressure differential that positions the diaphragm and,
consequently, the control rack. The governor valve is controlled by a lever which
is connected by linkage to the foot throttle.
There is no actual connection between the foot throttle and the governor or fuel
injection pump

## Slide 250
If the engine is operating under load and the speed is below governed speed, the
velocity of air passing through the venturi is comparatively low and only a slight
pressure differential is present. The spring moves the diaphragm and control rack
toward the fullfuel
position and the engine speed approaches that of governed
speed. The same principle prevents the engine from overspeeding at light loads.
As the engine speeds up, the velocity of air through the venturi increases with the
result that the pressure differential at the diaphragm is increased. This
differential is sufficient to overcome the spring force and to cause the diaphragm
and control rack to move toward the stop position. When the engine is operating at
governed speed with the valve wide open, the pressure differential is just slightly
below that of the spring force and the diaphragm remains in the fulldelivery
position.

## Slide 251
For any position of the governor valve between idling and full load of the engine,
the diaphragm finds its relative position. Since any movement of the diaphragm is
also transmitted to the control rack, the amount of fuel delivery is definitely
controlled at all engine speeds. As the pressure drop between the chambers is
increased, the diaphragm is moved in the direction of less fuel delivery.
As the pressure drop is decreased, the spring can move the control rack in the
direction of greater fuel delivery. Therefore, in order to increase the speed of
the engine, the governor valve is opened; to decrease the engine speed, the valve
is closed.

## Slide 252
Learning Event 3
FUEL FILTERS
General. Thorough and careful filtration is necessary to keep diesel engines
efficient. Diesel fuels are more viscous than gasoline and contain more gums and
abrasive particles that may cause premature wear of injection equipment. The
abrasives may consist of material that is difficult to eliminate during refining or
they may enter the tank during careless refueling. Regardless of the source
abrasives must be removed from the fuel

## Slide 253
Configuration. Most diesel engine designs include at least two filters in the fuel
supply systems to protect the closely fitted parts in the pumps and nozzles. The
primary filter usually is located between the fuel tank and the fuel supply pump.
The primary filter contains a coarse filter medium that removes the larger foreign
matter. The secondary filter usually is located between the fuel supply pump and
the fuel injection pump. The secondary filter contains a fine filter medium that
removes even the most minute traces of foreign matter from the fuel. Additional
filtering elements frequently are installed between the injection pump and the
nozzle.

## Slide 254
Types. Diesel fuel oil filters are referred to as fullflow
filters, because all
the fuel must pass through them before reaching the injection pumps. A diesel fuel
filter usually incorporates an air valve to release any air that might accumulate
in the filter during operation.

## Slide 255
Primary Filters (Figure 72). Metal filters are used as primary filters because the
fine particles that will pass through them are not harmful to the supply pump.
Solids larger than 0.005 inch remain outside the metal disks, while the larger
foreign matter and the majority of the water settles to the bottom of the bowl.
From here, the foreign matter can be removed through a drain plug. A relief valve
in the filter cover enables the oil to bypass the filter element if the disks
become clogged

## Slide 257
Secondary Filters (Figure 73). Fabric filters, because of their greater filtering
qualities, are used primarily as main filters for protecting the fuel injection
pump. The filter medium is a large bag of close, evenly woven, lintless, acidresisting
textile material. Maximum benefit is derived from the bag's large area
by keeping the sides of the bag separated by a wirescreen
mat. The screen is the
same size as the bag and the two are fastened detachably to a central feeding spool
and wound around it. The fuel to be filtered flows from the filter inlet at the
top, through the spool, and out of the ports to the inside of its bag. The dirt,
solids, abrasives, and carbon are caught in the bag and the clean fuel passes
outward and to the fuel outlet. The bag may be removed, cleaned, and reinstalled.

## Slide 259
Learning Event 4
TIMING DEVICES
General. A large percentage of fuel injection pumps have timing devices
incorporated in them. Varying the time when fuel injection begins will improve
diesel engine performance and fuel economy for the same reasons that varying spark
timing will improve the performance of a gasoline engine.
Description (Figure 74). The timing device usually consists of an aluminum casting
with mounting flanges at both ends. A bore in the housing guides and supports the
spider assembly. A timing opening with cover is located in the top of the housing.
It is used to observe the position of the timing pointer in relation to the timing
mark on the timing device hub during injection pump timing procedures

## Slide 261
Operation (Figure 75). As the engine rotates the weight and spider assembly,
centrifugal force opens the flyweights from their collapsed position against the
force of the three timing device springs. As the flyweights swing out, the sliding
gear is forced toward the timing device hub. The longitudinal movement of the
sliding gear on its helical spline causes a slight change in the rotational
relationship in the injection pump to the engine, causing injection to begin
slightly earlier in the power stroke

## Slide 263
Learning Event 5
COLD WEATHER STARTING AIDS
General. Diesel engines are very difficult to start in cold weather. This is due
mainly to the low volatility of the fuel. The two most popular methods of
assisting a diesel engine in starting are preheating the induction air in the
intake manifold so that adequate vaporization will take place for combustion and
injecting a fuel into the engine that remains volatile enough in cold weather to
initiate combustion.
Intake Manifold Flame Heater System (Figure 76 on page 134). Engines are equipped
with a flametype
manifold heater for heating the induction air during cold weather
starting and warm up operations.

## Slide 264
Operation. The flame heater assembly is composed of a housing, spark plug, flow
control nozzle, and two solenoid control valves. The spark plug is energized by
the flame heater ignition unit. The nozzle sprays fuel under pressure into the
intake manifold elbow assembly. The fuel vapor is ignited by the spark plug and
burns in the intake manifold, heating the air before it enters the combustion
chambers. The flame fuel pump assembly is a rotary type, driven by an enclosed
electric motor. The fuel pump receives fuel from the vehicle fuel tank through the
vehicle's supply pump and delivers it to the spray nozzle. The pump is energized
by an ONOFF
switch located on the instrument panel. Two fuel solenoids are used
in the flame heater system.

## Slide 265
The valves are energized whenever the system is activated. The valves ensure that
fuel is delivered only when the system is operating. They stop fuel flow the
instant the engine or heater system is shut down.

## Slide 267
Ether Injection System (Figure 77). The ether injection system assists in the cold
weather starting of a diesel engine by injecting ether into the intake manifold.
Ether, which is very volatile, will vaporize readily in cold weather, initiating
combustion.
Operation. A pressurized canister containing ether is fitted to the engine. The
flow of ether from the canister to the spray nozzle is controlled by a solenoid
valve that closes when it is deenergized. The solenoid is controlled by a push
button switch on the instrument. When the switch is pushed, the solenoid is
energized. This opens the ether canister. Pressure from the canister pushes ether
through a connecting tube to the nozzle, where it discharges into the intake
manifold.