## Slide 1: CONSTRUCTIONEQUIPMENT REPAIRER (HYDRAULIC SYSTEMS) Subcourse EN 5260 EDITION B United States (US) Army Engineer School Fort Leonard Wood, Missouri 65473 4 Credit Hours Edition Date: November 1999

## Slide 2
INTRODUCTION
Hydraulics is the science of using force and motion to move confined liquid. In a
hydraulic device, a transfer of energy takes place when liquid is subject to pressure.
The following four basic principles govern hydraulics:

## Slide 3
Liquids have no shape of their own; they conform to the shape of their
container.
· Liquids are incompressible.
· Liquids transmit applied pressure in all directions.
· Liquids provide increased force.
The following key facts will help you gain an understanding of hydraulics:
· Hydraulic power is generated from mechanical power.
· Hydraulic energy is achieved by converting hydraulic power to mechanical
energy.
· Hydraulic energy consists of potential (pressure energy), kinetic (energy of
moving liquids), and heat (energy of resistance to fluid flow [friction]).
· Hydraulic energy is neither created nor destroyed, only converted to
another form.
· Energy in a hydraulic system is considered either work (gain) or heat (loss).
· Heat is created and energy is lost when a moving liquid is restricted.

## Slide 4
PART A: POSITIVEDISPLACEMENT
PUMPS
11.
General. Pumps are used to lift or transport liquid. They may raise the liquid
level or force the liquid through a hydraulic system.
a. Pumps in a hydraulic system are used to convert mechanical energy to
hydraulic energy. Mechanical power creates a partial vacuum at the pump's inlet port
so that atmospheric pressure in the reservoir can force liquid through the inlet line and
into the pump. Mechanical power then delivers this liquid to the outlet port, forcing
the liquid into the hydraulic system.

## Slide 5
b. Positivedisplacement
pumps are the most common hydraulic pumps on
engineer construction equipment. These pumps have a rotary motion that carries
liquid from the inlet port to the outlet port. They produce a pulsating flow of liquid.
Because these pumps have a positive internal seal to prevent leakage, their output is
relatively unaffected by system variations. For example, if an outlet port is blocked,
pressure in the pump will increase until the equipment stalls or the pump's motor fails.
Positivedisplacement
pumps are classified according to the element that transmits the
liquid¾gear, vane, or piston.

## Slide 6
12.
Gear Pump. The gear pump (Figure 11)
consists of a driving gear and a driven
gear enclosed in a fitted housing. The gears rotate in opposite directions, and the gear
teeth mesh in the housing between the inlet and outlet ports. As the teeth of the two
gears separate, a partial vacuum is formed, which draws liquid through the inlet port
into chamber A. Liquid in chamber A is then trapped between the teeth of the two
gears and the housing and is carried through two paths to chamber B. As the teeth
mesh again, liquid is forced through the outlet port.

## Slide 8
13.
Vane Pump. In a vane pump, a slotted rotor splined to the drive shaft rotates
between fitted side plates inside an ellipticalor
circleshaped
ring (Figure 12,
page
14).
Polished, hardened vanes slide in and out of the rotor slots and follow the ring's
contour by centrifugal force. Chambers formed between succeeding vanes carry oil
from the inlet port to the outlet port. A partial vacuum is created at the inlet as the
space between the vanes increases, forcing oil through the outlet as the area in the
pumping chamber decreases. Because the normal wear points on a vane pump are the
tips and the ring surface, these parts are specially hardened and ground.

## Slide 10
a. The vane pump is the only pump designed with automatic wear compensation.
As wear occurs, the vanes slide out of the rotor slots and continue to follow the ring's
contour. Thus, efficiency remains high throughout the life of the pump.
b. Vane pumps can be assembled to rotate either left or right. Corresponding
arrows stamped on the pump's body and cartridge indicate rotation direction. Rotation
is also indicated in the model number. Pumps assembled for lefthand
rotation
(counterclockwise when viewed from the driveshaft
end) have the letters "LH" added to
the model number. Pumps assembled for righthand
rotation have no markings.

## Slide 11
14.
Piston Pump. On an inline
piston pump, the drive shaft and the cylinder block
are on the same centerline (Figure 13).
Reciprocation of the pistons occurs when the
pistons run against a swash plate as the cylinder block rotates. The drive shaft turns
the cylinder block, which carries the pistons around the shaft. The piston shoes slide
against the swash plate and are held against it by the shoeretainer
plate. The angle of
the swash plate causes the cylinders to reciprocate in their bores. When a piston begins
to retract, the opening on the end of the bore slides over the inlet slot in the valve plate
and oil is drawn into the bore through less than onehalf
a revolution of the cylinder
block. A solid area is created in the valve plate, and the piston retracts. As the piston
begins to extend the opening, the cylinder barrel moves over the inlet port and oil is
forced through the outlet port.

## Slide 12
a. The major components of a piston pump consist of a housing, a
bearingsupported
drive shaft, a rotating group, a shaft seal, and a valve plate. The
valve plate contains the inlet and outlet ports and functions as the back cover. The
rotating group includes a cylinder block, which is splined to the drive shaft; a splined
spherical washer; a cylinderblock
spring; nine pistons with shoes; a swash plate; and a
shoeretainer
plate. When this group is assembled, the cylinderblock
spring forces the
cylinder block against the valve plate and the spherical washer against the sho

## Slide 13
retainer plate. The nine piston shoes are held positively against the swash plate,
ensuring that the pistons reciprocate as the cylinder turns. In fixeddisplacement
pumps, the swash plate is stationary

## Slide 15
b. Displacement (outflow) from the piston pump depends on the number of pistons,
their bore, and their stroke. The swash plate's angle determines the stroke; therefore,
the stroke can be changed by altering the angle (Figure 14).

## Slide 17
15.
General. The J. I. Case Model MW24C scoop loader has a twosection
pump¾one section provides hydraulic power for the steering system; the other section
Piston Piston
shoe
Spherical
washer
Drive shaft
Swash plate
Housing Shoe-retainer plate
Cylinder-block spring
To inlet port
To outlet port
Valve plate
Cylinder block
Maximum
displacement
Partial
displacement
Zero
displacement
0°
provides power for the loader system. This model has a geartype,
fixeddisplacement
pump located on the rear of, and it is driven by the transmission. Hydraulic lines carry
fluid from the reservoir to the pump and from the pump to the control, demand, and
relief valves.

## Slide 18
16.
Removal and Repair of the Gear Pump. When the gear pump breaks down or
does not operate properly, the maintenance supervisor instructs the constructionequipment
repairer in the procedures necessary to determine the extent of damage and
possible repairs. The first step in this process is to drain the reservoir. The pump is
then removed from the transmission and completely disassembled before cleaning or
repairs begin. The removalanddisassembly
process requires several steps; each step
must be performed in the order listed.

## Slide 19
a. Refer to Figure 15
and use the following steps to drain the reservoir on the gear
pump:
· Remove the filler plug (1) on the hydraulic reservoir slowly to relieve air
pressure.
· Remove the drain plug (2), and drain the fluid from the reservoir into a
container.
· Turn the frontend
loader fully to the left or right, and engage the locking
bar.

## Slide 21
b. Refer to Figure 16
and use the following steps to remove the gear pump:
· Remove the hose assemblies from the gear pump, and drain the hydraulic
fluid into a container.
· Support the hydraulic pump (3), and remove the two cap screws (1) and
lock washer (2).
· Remove the pump (3) and bracket (4) from the transmission carefully.
Place a protective cover over the splined drive shaft on the pump and the
mounting pad to prevent foreign material from entering the transmission

## Slide 23
c. Refer to Figure 17,
page 18,
and use the following steps to disassemble the
gear pump:
· Scribe a line lengthwise along the pump to aid in alignment during
reassembly.
· Remove the roller bearings (6, 18, and 30) with a bearing puller. Replace
them as necessary.
· Remove the seals (7, 10, 11, 19, 25, and 31) and discard.
· Remove the seal (32) from the shaft end cover (34).
· Discard the preformed packing and the seal (32).
1-

## Slide 25
d. Clean all metal parts using cleaning solvent (specification PD680)
and allow
parts to air dry. Do not use cloths to dry parts.
17.
Inspection of the Gear Pump. Refer to Figure 17,
and complete the following
steps to inspect the gear pump:

## Slide 26
a. Inspect the gear surfaces and the edges of the gear teeth for burrs, scoring, or
wear. Remove burrs with a fine stone. Replace the gears if they are worn or badly
scored.
NOTE: Gears must be replaced in sets.
b. Inspect the driving gear (22), and replace it if it is rough or damaged near the
seal or if wear at the bearing surfaces has caused the shaft diameter to differ from the
designated diameter by more than 0.001 inch

## Slide 27
c. Inspect the roller bearings (6, 18, and 30) for free rollers, pitting, or wear.
Replace the bearings as needed.
d. Inspect the gear housings (9 and 24) for wear and damage, and replace them as
needed. Inspect the mating surfaces of the gear housings (9 and 24), bearing carrier
(15), port end cover (3), and shaft end cover (34) for burrs and damage. Remove burrs
with a fine file or stone. Replace the entire part if the surface is badly damaged.
e. Inspect the thrust plates (4, 16, and 28) for wear and scoring. Replace the
plates as needed

## Slide 28
18.
Reassembly of the Gear Pump. Refer to Figure 17,
and complete the
following steps to reassemble the gear pump:
a. Coat the preformed packing, the pocket seals (5, 17, and 29), and the seals (7,
10, 11, 19, 25, 31, and 32) with an oilsoluble
grease before installing them.
b. Press the seal (32) into the shaft end cover (34) with the lip facing the inside of
the bore.
c. Use soft jaws to place the shaft end cover (34) in a vise. Install the preformed
packing and roller bearings (30) in the shaft end cover (34).

## Slide 29
d. Grease the six pocket seals (17) and install them in the two middle slots of the
thrust plates (16). Install the thrust plate (4) on the drive shaft with the pocket seal
facing the shaft end cover (34). Tap the thrust plate (4) in place. Leave a clearance of
0.03125 inch between the thrust plate (4) and the shaft end cover (34).

## Slide 30
e. Install the six outer pocket seals (5) in the thrust plate (4). Push the pocket
seals (5) into the slots until the ends make contact with the roller bearings (18). Tap
the thrust plate (4) solidly into position on the port end cover (3). Use a razor blade or
a sharp knife to trim the exposed ends on the pocket seals (5) so that they are flush
with the sides of the thrust plate (4).

## Slide 31
f. Use soft jaws to place the gear housing (24) in a vise. Install the thrust plate
(16) as described in paragraph 18d.
g. Place the port end cover (3) in a vise. Install the seal (7), the roller bearings
(6), and the thrust plate (4).
h. Place the bearing carrier (15) in a vise. Install the seals (19), the roller
bearings (18), and the thrust plates (16).
i. Place the assembled shaft end cover (34) in a vise. Coat the thrust plate (28)
with engine oil. Install the driving gear (22) and the driven gear (23) in the shaft end
cover (34).

## Slide 32
j. Install the seals (25) in the grooves on the gear housing (24). Install the
housing over the gears on the shaft end cover (34). Tap the gear housing (24) with a
leather hammer to seat it on the cover. Lubricate the gears with engine oil to provide
initial lubrication.
k. Install the connecting shaft (21) in the bore of the pump shaft and driving gear
(22). Install the bearing carrier (15) on the gear housing (24), and align the scribe
marks. Tap the bearing carrier (15) in place

## Slide 33
l. Install the driving gear (13) on the connecting shaft (21) and install the driven
gear (14) in the bore of the bearing carrier (15). Insert seals (10 and 11) in the grooves
on the gear housing (9). Place the gear housing (9) over the gears and tap the housing
in place. Lubricate gears with engine oil.

## Slide 34
m. Place the port end cover (3) on the gear housing (9) and tap in place. Thread
four studs through the port end cover (3) and into the shaft end cover (34) until the
stud's ends extend above the port end cover (3). Insert the four washers (2) and nuts
(1). Tighten the nuts (1) to a snug fit.
n. Rotate the connecting shaft (21) and the driving gear (22) with a 6inch
wrench. Check the ease of operation. If the connecting shaft (21) rotates freely, tighten
the nuts (1) to a torque of 200 footpounds.
Rotate the connecting shaft (21), and check
the ease of operation a second time. The pump should rotate freely with no evidence of
binding.

## Slide 35
o. Coat the splines of the connecting shaft (21) and the driving gear (22) with
grease.
19.
Installation of the Gear Pump. Complete the following steps to install the
assembled gear pump:

## Slide 36
a. Refer to Figure 17,
page 18.
Remove the protective cover from the splined
connecting shaft (21) of the gear pump, and coat the shaft with grease. Install the
pump on the mounting pad.
b. Refer to Figure 16,
page 17.
Install the gear pump and secure it with two
screws (1) and lock washers (2). Connect the hydraulic lines to the pump.
c. Refer to Figure 15,
page 16,
and continue with the following steps to install
the assembled gear pump:
· Replace the drain plug (2) and strainer assembly (6) in the reservoir.
· Replace the cover (4) and the gasket (5) on the reservoir, and secure the
cover with screws (3).
· Refill the reservoir with hydraulic fluid, and replace the filler plug (1).
· Start the engine, and check the pump and lines for leaks. Operate the
hydraulic controls and check pump operation.

## Slide 37
PART C: VANE PUMP
110.
General. A doublesection,
insert, hydraulic vane pump is used on Caterpillar
D7G tractors. The pump is bolted on the engine's rearpowertakeoff
housing and is
driven by the rearpowertakeoff
idler gear.
a. A vane pump consists of a small and a large section, both of which share a
common inlet. The large section provides hydraulic power for the bladelift
and scraper
circuits. The bladelift
circuit is controlled by a valve located in the hydraulic tank.
The scraper circuit is controlled by a valve located in the equipment operator's
compartment. The small section powers the bladetilt
circuit and is controlled by a
valve mounted in the hydraulic tank.

## Slide 38
b. The vane pump requires a continuous flow of clean oil to lubricate the closely
fitted parts. If inlet oil is not available, the pump may seize or sustain damage when
the engine is started. Insufficient oil supply may result from clogged or leaking inlet
lines or a low oil level. The pump may need to be removed for cleaning or repair.

## Slide 39
111.
Removal of the Vane Pump. To remove the vane pump from its mounting,
complete the following steps:
a. Close the shutoff
valve located on or near the reservoir.
b. Disconnect the suction (intake) and pressure (outlet) hos

## Slide 40
c. Remove the vane pump from its mounting bracket or housing.
112.
Disassembling the Vane Pump. Refer to Appendix D, pages D7
through D10,
to disassemble the vane pump.

## Slide 41
113.
Cleaning, Inspecting and Repairing the Vane Pump. After the vane pump
is disassembled, thoroughly clean and dry all parts (refer to Appendix D, pages D3
through D6
and D10).
Carefully inspect and repair cleaned parts according to the
following procedures:
a. Discard the intake and exhaust plate seals and Orings.
Wash all metal parts
in mineral oil solvent, and dry them with filtered, compressed air. Place the parts on a
clean surface for inspection.
b. Inspect the surfaces of the pump housing, rotor ring, and rotor for scoring and
wear. Remove light scoring marks by lapping with an extrafine
emery cloth or lapping
compound. Replace all heavily scored or badly worn parts.

## Slide 42
c. Check the intake and exhaust end plates for scoring and wear. Replace badly
worn or heavily scored end plates.
d. Inspect the vanes for burrs, wear, or play in the rotor slots. If too much play is
noted, replace the rotor and vanes. Refer to the repair and replacement standards
listed in the appropriate TM to determine if replacement is necessary.
e. Check the slip ring and slipring
washer for scoring and wear. Replace heavily
scored or badly worn parts.

## Slide 43
f. Check the bearings for wear and fit. To check for pitted or cracked balls or
race, apply pressure and slowly rotate the bearing. Replace the bearing if it is worn or
scored. Place the drive shaft into the pilot bearing and check for excessive play.
Replace the pilot bearing if necessary. Refer to the repair and replacement standards
listed in the appropriate TM to determine when replacement is necessary.
g. Inspect the oilsealmating
surface of the drive shaft for scoring and wear. If
marks on the drive shaft cannot be removed with light polishing, replace the drive
shaft.
h. Coat Orings
with a small amount of petroleum jelly to hold them in place
during reassembly.

## Slide 44
114.
Lubricating and Assembling the Vane Pump. Lubricate all parts with clean
oil. Refer to Appendix D, pages D10
through D14
to assemble the vane pump.

## Slide 45
115.
Testing the Vane Pump. Refer to Appendix D, pages D14
through D18,
to test
the vane pump.

## Slide 46
PART D: PISTON PUMP
116.
General. The piston pump is used on the ACE. The compensating hydraulic
pump is a tenpiston,
variabledisplacement,
constantpressure,
radial pump.
WARNING
The ACE's hydraulic system is under high pressure. Relieve pressure before
disconnecting any hydraulic components. After pressure is relieved, wait at
least 4 minutes before disconnecting any hose or fitting. Failure to comply
may result in severe injury.

## Slide 47
117
Removing the Piston Pump. Complete the following steps to remove the
piston pump from its mounting:
a. Refer to Figure 112
and disconnect the piston pump using the following steps:
· Disconnect the hoses (1, 2, and 3) from elbows (4, 5, and 6).
· Loosen the screw (8) on the clamp (9), and remove the clamp from the
pump (7).

## Slide 49
b. Refer to Figure 113,
page 114,
to remove the piston pump. Remove the two
selflocking
screws (10), washers (11), pump (7), and gasket (12) from the transfer case
(13). Discard the screws (10) and the gasket (12).

## Slide 51
118.
Disassembling the piston pump. Complete the following steps to disassemble
the piston pump:
a. Refer to Figure 114,
and disassemble the piston pump using the following
steps:

## Slide 53
· Remove the elbows (4 and 6) and the seals (14 and 15) from the pump
(7). Discard the packing.
· Remove the elbow (5), the reducer (16), the seal (17), the elbow (18), and
the seal (19) from the pump (7). Discard the seals (17 and 19).
b. Refer to Figure 115,
and disassemble the piston pump using the following
steps:
· Remove the four cap screws (1), compensator (2), gasket (3), and seal (4)
from the cover (5). Discard the gasket (3) and the seal (4

## Slide 55
· Remove the four screws (6), cover (5), and gasket (7) from the housing (8).
Discard the gasket.
WARNING
Remove the rotating group as an assembly. Failure to comply may result in
damage to equipment.
c. Refer to Figure 116,
page 116,
and disassemble the piston pump using the
following steps

## Slide 57
· Tip the housing (8) forward and remove the rotating group (9) from the
shaft (10

## Slide 59
· Remove the swash plate (11) and the two screws (13) from the yoke (12).
· Apply pressure to the yoke (12) and use a wood dowel to drive out the two
pintles (14).
· Remove the yoke (12), seat (15), and two springs (16) from the shaft (10)
and housing (8).
· Remove the packing (17) from the pintles (14). Discard the seal (17).

## Slide 60
119.
Reassembling the Piston Pump. Complete the following steps to reassemble
the piston pump:
NOTE: Lightly coat all parts with lubricating oil before assembly. Apply
lubricating oil to packing before installation.
a. Refer to Figure 116,
and reassemble the piston pump using the following
steps:
· Install the seal (17) on the pintles (14).
· Install the two springs (16), seat (15), and yoke (12) on the housing (8).
· Press down on the yoke (12) and align the screw holes with the holes in the
pintle (14) seat. Install two pintles on the housing (8) and the yoke (12).
NOTE: The pintle grooves must align in the center of the yoke's screw holes.

## Slide 61
· Install the two screws (13) on the yoke (12). Tighten the screws (13) to 75
to 80 footpounds.
· Install the swash plate (11) on the yoke (12), chamfered side first. Coat the
face of the swash plate (11) with lubricating oil.
· Lay the housing (8) on its side and carefully slide the rotating group (9) on
the shaft (10), aligning the splines. Coat the face of the rotating group (9)
with lubricating oil.

## Slide 62
NOTE: The cover will not fit flush until the screws are tightened.
b. Refer to Figure 115,
page 115,
and reassemble the piston pump using the
following steps:
· Install the gasket (7) and cover (5) on the housing with the four screws (6).
Tighten the screws (6) to 25 to 35 footpounds.
· Install the packing (4), gasket (3), and compensator (2) on the cover (5) with
four screws (1). Tighten the screws (1) to 60 to 70 footpounds.

## Slide 63
120.
Installing the Piston Pump. Complete the following steps to install the piston
pump:
NOTE: New pumps are delivered with a 0.25 by 0.25inch
key installed on the
shaft. Discard this key and use a 0.25 by 0.225inch
key.
a. Refer to Figure 112,
page 113.
Install the clamp (8) on the pump (7).
b. Refer to Figure 113,
page 114,
and install the piston pump using the
following steps:
· Clean the mounting surfaces of the pump (7) and transfer case (13).

## Slide 64
NOTE: Apply lubricating oil to the screw threads and packing before
installation.
· Install the gasket (12) and the pump (7) on the transfer case (13) with the
washer (11) and selflocking
screws (10).
c. Refer to Figure 114,
page 114.
Install the packing (14), elbow (4), packing
(15), elbow (6), packing (17), reducer (16), packing (19), elbow (18), and elbow (5) on
pump (7). The position of the elbow (6) should point slightly downward to prevent the
hose from interfering with the ejector

## Slide 65
d. Refer to Figure 112,
page 113,
and install the piston pump using the
following steps:
WARNING
Ensure that the pump is primed with lubricating oil. Failure to comply may
result in damage to equipment.
· Connect SPNSN PUMP7
hose (3) to the elbow (6).
· Turn the elbow (4) to an upright position. Fill the pump (7) with
lubricating oil through the upright elbow (4) until oil overflows from the
elbow (5).
· Turn the elbow (5) to a downward position.
· Connect SPNSN PUMP9
hose (2) to the elbow (5) and connect SPNSN
DRAIN7V
hose (1) to the elbow (4).

## Slide 66
LESSON 2
HYDRAULIC VALVES

## Slide 67
INTRODUCTION
Hydraulic systems use valves to move hydraulic fluid or oil from one point to another.
To ensure the efficient operation of equipment, the constructionequipment
repairer
must be knowledgeable in control and repair procedures. In a hydraulic system, valves
control the actuators. An actuator is a cylinder that converts hydraulic energy to
mechanical energy. For example, the tilt cylinder on a Caterpillar D7 or D8 dozer is an
actuator that controls the blade direction.

## Slide 68
a. Valves are often referred to as the "control" of the hydraulic system,
particularly when several are built into a single assembly. Valves assert control in the
hydraulic system to—
· Regulate pressure and create special pressure conditions.
· Regulate the flow rate and direction of fluid to parts of the hydraulic
system.

## Slide 69
b. Valves are rated by their size, pressure capabilities, and pressure drop versus
flow capabilities. Most are named for their function, but some are named for their
construction. For example, a pressurerelief
valve is named for its function, and a
poppet valve is named for its construction.
c. Valve construction ranges from a simple ballandseat
arrangement to a
multielement, spooltype
valve with jetpipe
pilot stage and electrical control. General
construction classification begins with simple valves and builds to complex designs.

## Slide 70
PART A: PRESSURECONTROL
VALVES
21.
General.
a. Pressurecontrol
valves are the most common valves on engineer construction
equipment with hydraulic systems. They are used to—
· Regulate pressure.
· Create specific pressure conditions.
· Control the order in which actuators operate

## Slide 71
b. Pressurecontrol
valves operate in hydraulic balance. Hydraulic balance occurs
when pressure on one side or end of a ball, poppet, or spool is opposed by a spring on
the opposite end. During operation, the position of the valve causes the hydraulic
pressure to balance with the force of the spring. Because spring force differs with
compression distance, the amount of pressure can differ. The pressurecontrol
valve
has infinite positioning. It can control conditions from a large to a small volume of fluid
flow, or it can completely restrict fluid movement.

## Slide 72
22.
Classification.
a. Pressurecontrol
valves are classified as normally closed or normally open. The
most common type, the normally closed, blocks the flow of fluid from the inlet port to
the outlet port until pressure builds high enough to cause unbalanced operation. Flow
in a normally open valve moves freely until the valve operates in balance. The flow is
then partly restricted or completely cut off.
b. Pressure override occurs when a normally closed valve operates in balance.
Because pressure increases as the height of the compression spring is reduced, the
pressure when the valve cracks or begins to pass flow through the outlet port is less
than when it passes a large volume (full flow). The difference between fullflow
pressure and cracking pressure is called override.

## Slide 73
23.
PressureRelief
Valve.
a. The relief valve is the most common pressurecontrol
valve. Relief valves have
two functions. They provide overload protection for circuit components, and they limit
the force (torque) exerted by a linear actuator or rotary motor. The function of the
relief valve may change, depending on the system's needs. These valves are classified
as simple or compound, depending on their design.
b. The internal design of all pressurerelief
valves is similar. The valves have two
sections—a body and a cover. The body contains a piston, which is retained on its seat
by one or more springs. The cover, also called the pilotvalve
section, contains the
adjusting screw. The adjusting screw controls fluid movement to the pump's body and
controls the pressure (expressed in pounds per square inch [psi]) within range of the
valve's rated capacity.

## Slide 74
24.
Simple PressureRelief
Valve.
a. A simple pressurerelief
valve has only one spring. The valve is installed so
that one port connects to the pressure line (inlet) and the other connects to the
reservoir (outlet). The ball on the simple pressurerelief
valve is held on its seat by the
thrust of the spring. The amount of thrust exerted can be modified by turning the
adjusting screw. When pressure at the inlet is insufficient to overcome the spring force,
the ball remains on its seat and the valve is closed as shown in Figure 21,
page 24.
The position of the ball prevents the flow of fluid through the valve. When the pressure
at the inlet exceeds the adjusted spring's force, the ball moves off its seat and the valve
opens, allowing hydraulic fluid or oil from the pressure line to flow through the valve to
the reservoir. This flow prevents a pressure increase in the pressure line. When
pressure decreases below the adjusted spring's force, the ball is reseated and the valve
closes.

## Slide 76
b. The spring force in a simple pressurerelief
valve causes greater fullflow
pressure than cracking pressure. When operating at fullflow
capacity, the high
pressure causes the valve to operate in an override mode. In some cases, the override
pressure is almost as high or higher than the valve's rated capacity

## Slide 77
25.
Compound PressureRelief
Valve.
a. A compound pressurerelief
valve has a poppet and a spring to adjust fluid flow
(Figure 22).
The closed view in Figure 22
shows that passage 1 is used to maintain
the hydraulic balance in the piston when the valve's inlet pressure is less than the
pressure setting. The valve setting is determined by the thrust of the adjusting spring
against the poppet. When the pressure at the valve inlet reaches the valve setting, the
pressure in passage 2 rises to overcome the thrust of spring 1. When the flow through
passage l creates sufficient pressure drop to overcome the thrust of spring 2, the piston
rises off its seat as shown in the open view. This allows hydraulic fluid or oil to pass
through the drainage port to the reservoir and prevents any further increase in
pressure.

## Slide 79
b. Pressurerelief
valves that provide emergency overload protection must be
periodically cleaned even if they are not operated often. To clean the valve, reduce the
pressure adjustment and operate the valve under reduced pressure for a few minutes to
clean out the accumulated sludge deposits. Adjust the pressure to the prescribed
setting.

## Slide 80
PART B: DIRECTIONALCONTROL
VALVES
26.
Complex DirectionalControl
Valves. Complex directionalcontrol
valves are
used on engineer construction equipment, including the J. I. Case Scoop Loader Model
MW24C. All complex directionalcontrol
valves control the direction of fluid flow, but
they vary considerably in physical characteristics and operation. The valving element
in these units is classified under one of the following types:
· Poppet—the piston or ball moves on and off a seat.
· Rotary—the spool rotates around its axis.
· Sliding spool—the spool slides axially within a bore.

## Slide 81
27.
Valve Classification.
a. Directionalcontrol
valves may be classified according to the method used to
actuate the valving element. A poppet valve is usually hydraulically operated. A
rotary spool valve may be operated manually (lever or piston action), mechanically (cam
or trip action), or electrically (solenoid action). The slidingspool
valve may be operated
manually, mechanically, electrically, hydraulically, or in combination.
b. Directionalcontrol
valves may also be classified according to the number of
positions in the valving element or by the total number of flow paths provided in the
extreme position. For example, a threeposition,
fourway
valve has two extreme
positions and a center (neutral) position. Each of the extreme positions has two flow
paths.

## Slide 82
28.
Poppet Valve. The operation of a simple poppet valve is shown in Figure 23.
The valve has a movable poppet that closes against a valve seat. Pressure from the
inlet holds the valve tightly closed. A slight force applied to the poppet stem opens the
valve. The poppet stem usually has an Oring
seal to prevent leakage. On some valves,
poppets are held in the seated position by springs.

## Slide 84
29.
SlidingSpool
Valve.
a. A slidingspool
valve is also known as a pistontype
valve because it has a
piston with two inner areas of equal size. Pressure from the inlet port acts equally on
both inner areas regardless of the position of the spool. The ports are sealed by a
machine fit between the spool and valve body or sleeve.

## Slide 85
b. The spool in a slidingspool
valve is classified based on the flow conditions
created when it is in the neutral (normal) position. For example, a closedcenter
spool
blocks all valve ports when it is in the neutral position. An opencenter
spool opens all
valve ports when it is in the neutral position. Closedcenter
and opencenter
valves are
two of many designs used for slidingspool,
directionalcontrol
valves.
c. The slidingspool
valve is shown in Figure 24.
During operation, the valve
element slides back and forth to block or uncover ports in the housing

## Slide 87
210.
TwoWay
Valves. Twoway
valves are used to control the direction of fluid flow
in a hydraulic circuit. These valves are usually the slidingspool
type. As the spool
moves back and forth, it allows or prevents the flow of fluid through the valve.
211.
FourWay
Valves. Fourway
valves also control the direction of fluid flow in a
hydraulic circuit. The fluid movement controls the direction of a work cylinder or the
rotation of a fluid motor

## Slide 88
a. Fourway
valves are usually the slidingspool
type. They have a rectangular
cast body, a sliding spool, and a control lever for positioning the spool. The spool is
precision fitted to a bore through the longitudinal axis of the valve's body. The lands of
the spool divide the bore into a series of separate chambers. Ports in the valve's body
lead into these chambers. The position of the spool determines which ports are open to
each other and which are sealed. Ports that are sealed in one position may be
interconnected in another position.
b. Fourway,
directionalcontrol
valves have four ports—a pressure, a return
(exhaust), and two working. The pressure port connects to the pressure line (inlet), the
return port connects to the reservoir (outlet), and the two working ports connect to the
actuating unit.

## Slide 89
PART C: CONTROLVALVE
REPAIR
212.
General. The control valve on a J. I. Case Scoop Loader Model MW24C enables
the operator to direct the flow of hydraulic fluid to the cylinders that operate the loader.
It serves a combination of purposes and functions as a pressurerelief,
directionalcontrol,
and overloadcheck
valve. The valve has three operating spools as shown in
Figure 25.

## Slide 91
a. The upper spool (1) controls the lift circuit, the center spool (2) controls the tilt
circuit, and the lower spool (3) controls the clam circuit.
b. When the spools are in the neutral position, oil flow from the pump is directed
through the valve to the outlet port and returned to the reservoir. When the spool is
moved by the control linkage, the bypass is closed and oil flows through the spoolload
check valve to the desired cylinder port. At the same time, a port at the opposite end of
the cylinder is opened to allow oil to flow to the control valve's outlet port.
213.
Disassembling the Control Valve. Refer to Figure 26,
and complete the
following steps to disassemble the control valve:

## Slide 93
NOTE: Before beginning the disassembly process, clean the valve's exterior
and ports with cleaningcompound
solvent and dry them thoroughly.
a. Place the controlvalve
assembly on a clean workbench.
b. Use an openend
wrench to loosen and remove the seal assembly (1).
c. Use a screwdriver to remove the wiper (2) from the seal assembly (1). Discard
the wiper (2).
d. Remove the Oring
(3) from the seal assembly (1). Discard the Oring
(3).

## Slide 94
WARNING
Do not overtighten the vise as it will cause damage to the controlvalve
body.
e. Place the control valve assembly in a softjawed
vise.
f. Loosen the detent housing (18).
g. Install a rod or small pry bar in the spool eye (31).
h. Loosen and remove the four screws (4).

## Slide 95
i. Pull the connector (6) up from the cap (9) just enough to gain access to the wires
soldered to the contacts. Tag and unsolder the wires from the connector (6) contacts.
Remove the connector (6).
j. Remove the setscrew (7).
k. Use a screwdriver to remove the retaining ring (8). Remove the cap (9).
l. Remove and discard the Oring
(10) from the cap (9).
NOTE: On some units, tape may be used to hold the coils (11 and 15) and
spacer (12) together, preventing their removal. If removal is not possible,
disregard paragraph 213(
m) and go to paragraph 213(
n).
m. Remove the coil (11) and the spacer (12) from the detent housing (18).
WARNING
Hold the coil (11) against the spring (21) tension when loosening the screw.
Failure to do so could result in serious injury from flying parts.

## Slide 96
n. Loosen the screw (13) with the coil (11) against the spring (21) tension.
· If tape is around the coils (11 and 15), and the spacer (12) and the screw
(13) have not been loosened from the stud (17), remove the coils (11 and
15), the spacer (12), the screw (13), the washers (14 and 16), the stud (17),
the washer (19), the spring (22), and the washer (24) as an assembly and go
to paragraph 213(
q).
· If tape is around the coils (11 and 15), the spacer (12), the screw (13), and
the washers (14 and 16) as an assembly, go to paragraph 213(
o).
· If tape is not used, loosen and remove the screw (13), the washer (14), and
the stud (17) as an assembly. If the screw (13) is loosened from the stud
(17), remove only the screw (13) and the washer (14) and go to paragraph 213(
s).

## Slide 97
o. Remove and discard the tape securing the coils (11 and 15) and the spacer
(12).
p. Tag and unsolder the coil (11 and 15) wires.
q. Separate the coils (11 and 15) and the spacer (12). If the screw (13) was not
loosened from the stud (17), and the washer (24) and the spring (22) were removed with
the stud (17), work the washer (24) from the stud (17) and remove the spring (22) and
the washer (19). Remove the screw (13) and the washer (14) from the stud (17).
r. Remove the coils (11 and 15) and the spacer (12). If the screw (13) was loosened
from the stud (17), the spring seat (20), the springs (21 and 22) and the washer (24);
and if screw (13) was loosened from stud (17), and spring seat (23), go to paragraph 213(
w).

## Slide 98
s. Remove the coil (15), the washer (16), and the detent housing (18).
t. Remove the washer (19) and the spring seat (20) from the spring (21).
u. Remove the two springs (21 and 22), the spring seat (20), and the washer (24).
v. Unscrew and remove the stud (17) from the spool (29) if it is not already
removed.
w. Remove the retainer (27) and the Orings
(26 and 28) from the spool (29) bore.
Discard the Orings
(26 and 28).

## Slide 99
x. Remove the retainer (27) and the Oring
(28) from the spool (29) bore. Discard
the Oring
(28).
NOTE: Clean all metal parts in cleaningcompound
solvent and let them air
dry. Do not use compressed air.

## Slide 100
214.
Inspecting and Repairing the Control Valve. Refer to Figure 26,
page 29,
and complete the following steps to inspect and repair the control valve:
a. Inspect the controlvalve
body for cracks, breaks, or other damage. Inspect the
spool bore for grooves, deep scratches, or other visible wear. If damage is discovered,
replace the entire controlvalve
body.
b. Inspect the spool (29) for grooves, deep scratches, or other visible wear. Replace
the spool if necessary.
c. The free length of the spring (22) should be 2.63 inches. Use a spring gauge and
check that the force required to compress the spring (22) to 1.375 inches is 13.5 to 16.5
pounds. The force required to compress the spring (22) to 0.938 inch should be 18 to 22
pounds. Replace the spring (22) if the free length or the force required to compress it is
not as specified

## Slide 101
d. The free length of the spring (21) should be 4.25 inches. Use a spring gauge and
check that the force required to compress the spring (21) to 2.25 inches is 27 to 33
pounds. The force required to compress the spring (21) to 1.375 inches should be 38 to
48 pounds. Replace the spring (21) if the free length or the force required to compress
it is not as specified

## Slide 102
e. Connect a multimeter across the coil (11) wires. The multimeter should indicate
a 45 to 65 ohms resistance. Connect a multimeter across one wire of the coil (11) and
its metal housing. The multimeter should indicate infinity (open circuit). Repeat the
multimeter test on the second coil wire and its metal housing. Again, the reading
should indicate infinity. Replace the coil if the multimeter reading is not as specified.
Repeat paragraph 214(
e) on the second coil (15).
f. Inspect the remaining parts for cracks, breaks, deformation, distortion, and
damaged or stripped threads.

## Slide 103
215.
Reassembling the Control Valve. Refer to Figure 26,
page 29,
and complete
the following steps to reassemble the control valve:
NOTE: Coat all valve parts and body bores with engine oil before beginning
the reassembly process.

## Slide 104
a. Place a rod through one hole in the spool (29). Place the spool (29) in a softjawed
vise.
b. Install the sleeve (33) on the spool (29), sleeve shoulder up.
c. Place a small amount of retaining compound on the threads of the spool (29).
d. Install a new Oring
(32) on the spool eye (31). Install the spool eye in the spool
(29) and tighten to 19 to 21 footpounds.
Install a new Oring
(30) in the spool bore of
the controlvalve
body.
e. Lubricate the spool (29) and its bore with clean lubricating oil. Install the spool
(24) in its bore.

## Slide 105
f. Install a rod or a pry bar in the spool eye (31).
g. Place the controlvalve
assembly in a softjawed
vise.
h. Install a new Oring
(28) in the bore on the controlvalve
body. Install the
retainer (27) in the bore.
i. Place a new Oring
(26) on the spool (29) and install the retainer (25).
j. Place the washer (24) and the spring seat (23) on the spool (29). Make sure that
the washer (24) is in the springseat
(23) hole.
k. Install the two springs (21 and 22) and the spring seat (20). Install the washer
(19) in the spring seat (20).
l. Install the detent housing in the controlvalve
body. Tighten the detent housing
to 30 to 32 footpounds.

## Slide 106
m. Install the washer (16).
n. Install the coil (15) and fasten the lead ends together with tape.
o. Apply a small amount of retaining compound to the stud's internal threads if the
screw (13) and stud (17) were separated. Install the washer (14), screw on the stud,
and tighten to 10 to 12 footpounds.
p. Apply a small amount of retaining compound to the stud (17) threads. Install
the stud (17) in the detent housing (18).

## Slide 107
q. Push down and turn the screw (13) to install the stud (17) in the spool (29).
Tighten to 19 to 21 footpounds.
r. Install the spacer (12) in the detent housing (18).
s. Install the coil (11).
t. Install a new Oring
(10) on the cap (9).
u. Feed the leads from the coils (11 and 15) through the cap (9) hole. Install the cap
in the detent housing (18), aligning the setscrew (7) hole with the hole in the detent
housing.
v. Install the retaining ring (8) and the setscrew (7). Tighten the setscrew (7).

## Slide 108
w. Solder the coil (11 and 15) leads to the connector (6) using a rosincore
solder.
Solder one lead from each coil (11 and 15) to contact B (5) in connector (6). Solder the
second lead from the coil (15) to contact A (5) in connector (6). Solder the second lead
from the coil (11) to contact C (5) in connector (6).
x. Position the connector (6) on the cap (9). Install and tighten the four screws (4).
y. Remove the rod or the pry bar from the spool eye (31).
z. Install a new Oring
(3) in the seal assembly (1).

## Slide 109
aa. Place the seal assembly (1) in a hydraulic press, threaded end down. Place
the wiper (2) on the seal assembly. Use a 1 3/4inch
diameter rod to press the wiper (2)
into the seal assembly (1) until the wiper is flush with the top of the pump.
bb. Install and tighten the seal assembly (1).
cc. Install the controlvalve
assembly.

## Slide 110
216.
Testing and Adjusting the Control Valve. Test the control valve assembly by
observing it during operation. With the oil at the recommended operating temperature
and the engine running at a fast idle, check the time required to raise the empty bucket
on the scoop loader from the ground to its highest raised position. This should take
approximately 6 seconds. If it takes more than 6 seconds for the bucket to raise, ensure
that the—
· Reservoir is filled to the proper oil level as stated in the appropriate TM.
· Oil is the type specified in the appropriate TM.

## Slide 111
· Suction line is unrestricted and the strainer is clean.
· Scoop loader is operating at the correct fastidle
speed, as stated in the
appropriate TM.
· Powersteering
pump and the demand valve are operating properly.
NOTE: Repeat this test with a loaded bucket. If the lifting time is good
(6 seconds) with an empty bucket but slow with a loaded bucket, check the
cylinder packing, main pressurerelief
valve, and hydraulic pump.