## Slide 1: ENGINEER CONSTRUCTION EQUIPMENT MAINTENANCE CONCEPTS AND OPERATIONS

## Slide 2
INTRODUCTION
The Army's mission "to perform prompt and sustained combat on land" implies
the readiness to go at any time with what we have in manpower and material
resources. Effective firepower and mobility depend on our ability to
perform the maintenance necessary to keep equipment and material in
operating condition. To maintain combat effectiveness, we need to
strengthen our entire maintenance system, with emphasis on the user level.
Our equipment continually becomes more complex. This all adds to the
requirement for improved maintenance at all levels. The growing demands for
force readiness mean that we must approach our maintenance responsibility
with added enthusiasm. How does a supervisor manage maintenance? Why does
he or she manage maintenance? What about all the other things that a
supervisor must manage, such as supply, training, operations, and personnel?
This subcourse answers some of those questions.

## Slide 3
LESSON 1
FUNDAMENTALS OF MAINTENANCE SUPERVISION

## Slide 4
Learning Event 1
THE ARMY MAINTENANCE SYSTEM
Unit maintenance is one part of an overall system to provide maintenance
support to the Army's equipment. The system is made up of three levels, as
shown in Table 1 below. Each level makes a different contribution to the
overall system.

## Slide 6
The maintenance system sustains the combat power which can be placed against
the enemy. It influences the outcome of a battle by returning equipment to
the combat unit while that battle is still being fought. Obviously,
equipment that takes longer to repair cannot be used to help win a current
battle, but it can contribute to winning future battles. Table 2
illustrates the battlefield role of the various maintenance levels

## Slide 8
The change to threelevel
Maintenance is based on the need to support a
highly mobile and sophisticated fighting system and the relative lack of
mobility by the old general support units that were in the corps area.
Table 3 shows a comparison of the old and new systems and their array on the
battlefield.

## Slide 10
UNIT MAINTENANCE
This level of the new system corresponds to the operator and organizational
categories of the old system. Maintenance is characterized by quick
turnaround time of replacement of parts and minor repairs. Operators and
maintenance personnel make maximum use of builtin
test equipment (BITE) to
support battle damage assessment and repair (BDAR). Systems mechanics
provide indepth
technical skill at the unit level. Repair parts stockage
is based on combat prescribed load lists (PLL), which consist of demand
support items desired in stock and those items required for stockage by a
maintenance parts list (MPL). Direct exchange (DX) is used to support quick
turnaround. Repair times at this level generally do not exceed 4 to 6
hours

## Slide 11
INTERMEDIATE MAINTENANCE
This level has two categories: intermediate direct support (IDS) maintenance
and intermediate general support (IGS) maintenance, as follows:
The IDS maintenance units are employed at different locations, but the tasks
performed are the same. These units are found in the brigade, division, and
corps, and in the echelons above corps (EAC) areas. Selected nondivisional
IDS maintenance units provide backup maintenance support to divisional
maintenance units. This type of maintenance is characterized by repair,
replacement, high mobility, forward orientation, and maintaining a highvolume,
fastmoving
operational readiness float (ORF). Units can be readily
organized into teams to support specific systems and to project support
forward on the battlefield. Suitcasetype
automatic test equipment (ATE) is
used to support BDAR. Repair parts stockage is based on a combat authorized
stockage list (ASL). Divisional IDS maintenance units are structured to
provide dedicated support to brigades and battalions. This includes repair
of selected highusage
components for DX. Repair times generally do not
exceed 36 hours.

## Slide 12
The IGS maintenance units are located behind the corps and provide support
to the theater supply system through repair of class VII and class IX items.
Their work is job or promotionoriented
and is performed by modular units
with commodityoriented
platoons in semifixed facilities. Teams may be
added to provide an area support capability as required. The General
Support (GS)type
ATE is used to support operations. The IGS maintenance
units do not have an ASL; however, they maintain a shop stock as required
for assigned missions. The units maintain theater reserve stocks in overall
support of theater requirements.

## Slide 13
DEPOT MAINTENANCE
Maintenance at this level is productionline
oriented and is performed in
support of the supply system. Work is done by special repair activities,
United States Army Materiel Command (AMC) depot employees, and/or contractor
personnel. The unit missions support overseas propositioning of materiel
configured to unit sets (POMCUS), repair cycle float (RCF), and war reserve
stocks. Repair parts supply support for depot maintenance is limited to
items to support assigned maintenance missions.

## Slide 14
As a supervisor, you must remember that unit maintenance is the foundation
of the Army's. maintenance system. It supports the needs of the user by
keeping equipment in operation. The quality and timeliness of unit
maintenance operations directly affect the combat readiness of the Army.

## Slide 15
Learning Event 2
MAINTENANCE SUPERVISION RESPONSIBILITIES
All supervisors have certain responsibilities for personnel and maintenance
supervision. Personnel are the most important resource and, as a
supervisor, you must ensure that this resource is not wasted. A goal for
the maintenance supervisor to establish is to have all table(s) of
organization and equipment (TOE) slots filled with personnel holding the
correct military occupational specialty (MOS) and pay grade. One of the
most difficult jobs of the maintenance supervisor is to establish priorities
in the face of conflicting requirements. The supervisor must work with the
assigned personnel to ensure that they

## Slide 16
· Are used correctly within the unit.
· Are accounted for.
· Are supervised.
· Are motivated.
· Have their skills developed.
All personnel, from the battalion commander to the vehicle driver, play an
important part in the supervision of resources such as manpower. All
resources must be in sufficient quantity when needed, if the maintenance job
is to be completed.
In this learning event, the maintenance responsibilities of each level of
command, from squad leader to battalion commander, will be discussed and you
will be shown how each level interfaces with the other levels

## Slide 17
PERSONNEL RESPONSIBILITIES
Platoon Leader. The platoon leader is responsible for all matters relating
to the discipline, training, welfare, and control of personnel assigned to
the platoon. The platoon leader is directly responsible for
· Advising the unit commander of platoon requirements in the maintenance
program.
· Executing the maintenance program at the platoon level.

## Slide 18
· Recommending program changes to the company commander to facilitate
mission requirements.
· Coordinating platoon maintenance requirements with the motor officer.
· Ensuring platoon compliance with the unit maintenance SOP.
· Managing the platoon maintenance training program.
· Accounting for the availability and serviceability of platoon
equipment.
· Reporting vehicle and equipment status to the motor officer as
required.
· Ensuring the availability of all personnel when required services are
due on platoon equipment.
· Accounting for everything the platoon does or fails to do in the
maintenance area

## Slide 19
Platoon Sergeant. The platoon sergeant assists the platoon leader in all
matters relating to discipline, training, welfare, and control of personnel
assigned to the platoon. The platoon sergeant's maintenance
responsibilities include

## Slide 20
· Advising the platoon leader on maintenance requirements.
· Assisting the platoon leader in the execution of the maintenance
program.
· Recommending changes to the platoon leader to facilitate mission
accomplishment.
· Ensuring the availability of needed expendables to support the platoon
maintenance program.
· Coordinating platoon maintenance requirements with the unit motor
sergeant.
· Supervising the platoon maintenance program.
· Ensuring that the platoon vehicle and equipment status reports are
prepared and submitted.

## Slide 21
Squad Leader. The squad leader is the link between the platoon sergeant and
the personnel in the squad. He assists the platoon sergeant in matters
relating to maintenance, discipline, training, welfare, and control of
personnel assigned to his squad. He is responsible for the accountability
of his personnel at all times. The squad leader ensures that his personnel
comply with the maintenance SOP and is responsible for ensuring that his
vehicles and equipment are scheduled for maintenance when necessary and are
always in an operational condition.

## Slide 22
Motor Sergeant. The unit motor sergeant is the noncommissioned officerincharge
(NCOIC) of the maintenance section. He assists the motor officer in
all matters relating to discipline, training, welfare, and control of the
people assigned to the maintenance section. The motor sergeant supervises
and assists the unit's maintenance personnel and equipment operators/crews
in the proper performance of unit maintenance on organizational vehicles,
materials handling equipment, electrical power generating equipment, and
similar unit items. The motor sergeant's responsibilities include the
following:

## Slide 23
· Controlling the daily dispatching of unit vehicles and equipment.
· Maintaining required records and reports pertaining to equipment
operation and maintenance.
· Instructing and assisting less skilled personnel in the proper
operating and maintenance practices and procedures.
· Assisting motor pool personnel in the correct interpretation and
application of instructions contained in appropriate technical manuals,
technical bulletins, lubrication orders, modification work orders, and other
publications and directives pertaining to the maintenance of vehicles and
equipment.
· Planning and organizing work schedules and coordinating equipment
downtime for maintenance with the using section.
· Assigning duties to the unit mechanics and personnel under his
control.
· Drafting and implementing the unit shop operations SOP.

## Slide 24
Motor Officer. The motor officer position is an additional duty assigned to
an officer, normally the executive officer, of the unit. The motor officer
is responsible for the following:
· Developing the unit maintenance program.
· Coordinating maintenance operations with supporting units.
· Drafting the unit maintenance SOP.
· Briefing all incoming officers and noncommissioned officers (NCO) on
the unit maintenance SOP.
· Keeping the commander informed daily on the operational status of all
equipment.

## Slide 25
· Monitoring all aspects of unit maintenance operations to ensure
maximum effective utilization of resources and equipment.
· Planning and organizing work schedules and coordinating equipment
downtime for maintenance with the using section.
· Assigning duties to the unit motor sergeant.
First Sergeant. The first sergeant is the senior NCO of the unit. The
first sergeant should be the source of most of the guidance received by the
platoon sergeants and the unit commander's source of information and advice
on all matters pertaining to the soldiers. In the maintenance realm, the
first sergeant sets the example for all other soldiers by

## Slide 26
· Attending scheduled maintenance periods.
· Ensuring that all firstline
supervisors, platoon sergeants, and staff
NCOs attend and participate during scheduled maintenance periods.
· Knowing the unit's personnel gains, losses, strengths, and weaknesses
and advising the commander accordingly.
· Checking maintenance operations continually, from the operator through
the motor sergeant, and correcting where necessary.

## Slide 27
· Identifying maintenance operational weaknesses and executing
corrective actions through the NCO chain, advising the commander as
appropriate.
Unit Commander. The unit commander is responsible for all matters relating
to mission accomplishment, discipline, training, welfare, and control of
personnel and equipment assigned to the unit. He must supervise and ensure
timely completion of all company activities. His responsibilities include
· Analyzing the unit maintenance situation.
· Directing the unit motor officer to prepare the unit maintenance
program in line with the battalion program.

## Slide 28
· Providing command guidance to the unit motor officer.
· Directing implementation of the unit maintenance program.
· Supervising the execution of the maintenance program.
· Evaluating the maintenance program.
· Suggesting changes to the battalion maintenance program.
Battalion Maintenance Sergeant. The battalion maintenance sergeant is the
NCOIC of organic motor pool operations. He is directly responsible for the
following

## Slide 29
· Supervising shop operations.
· Making daily work assignments.
· Supervising scheduled maintenance services, tests, troubleshooting
repairs, use of tools and test equipment, replacement of parts, safety, and
onthejob
(OJT) programs.
· Drafting and maintaining the shop operation SOP.
· Controlling the daily dispatching of battalion vehicles.
· Providing assistance to company motor sergeants when needed

## Slide 30
Battalion Maintenance Technician (Combat Service Support units only). The
battalion maintenance technician is the technical expert in the battalion
maintenance operation. He is the principal assistant to the battalion
maintenance officer (BMO). His responsibilities include
· Organizing and supervising the records and quality control sections.
· Supervising unit maintenance of material and auxiliary equipment.
· Controlling the flow of repair parts requests and assisting in the
scheduling of maintenance and repairs from the companies to the IDS unit.
· Monitoring preventive maintenance services, directing quality control
inspections of maintenance operations and records, and analyzing equipment
deficiencies and failures.

## Slide 31
· Recommending new maintenance procedures to the BMO.
· Reviewing equipment status reports for the BMO.
· Serving as battalion maintenance officer in the absence of the BMO.
Battalion Maintenance Officer. The BMO is the battalion commander for
maintenance operations. The BMO keeps the commander and staff informed of
the operational status of material and auxiliary equipment. The BMO's
responsibilities include

## Slide 32
· Analyzing the maintenance situation.
· Planning and evaluating the maintenance program.
· Coordinating operations with IDS units and other units, as required.
· Supervising prescribed load list (PLL) supply as well as recovery and
evacuation of equipment, components, and parts.
· Supervising maintenance services and monitoring the training and
licensing of vehicle drivers and equipment operators.
· Monitoring and coordinating unit maintenance operations

## Slide 33
· Compiling and consolidating material condition status reports for the
commander.
· Ensuring that all recurring maintenance reports are consolidated and
forwarded to higher headquarters as required.
· Drafting and maintaining the maintenance annex to the battalion SOP.
· Briefing all incoming officers on the maintenance SOP.
Battalion Supply Officer. The battalion supply officer (S4) is very
important to the maintenance and supply operations of the battalion. The S4
is responsible for
· Monitoring equipment shortages.
· Monitoring vehicle age and mileage.
· Coordinating with the BMO on turnin
procedu

## Slide 34
· Monitoring changes in equipment (deletions and additions of basic
issue items (BII), tool sets, and kits).
· Allocating funds for tools and housekeeping items.
· Ensuring that organic and attached units are provided rations, water,
gasoline, lubricants, unit and individual supplies, and ammunition.
· Advising the battalion commander on the status of unit supply and
maintenance.
· Maintaining property books for organic units when required.
· Ensuring that unit supply operations are conducted according to
regulations, including repair parts supply.

## Slide 35
Command Sergeant Major. The battalion command sergeant major is the senior
NCO of the unit. The command sergeant major should be the source of most of
the guidance received by the first sergeant, and should be the battalion
commander's source of information and advice on all matters pertaining to
soldiers. In the maintenance realm of responsibility, the command sergeant
major sets the example for all other soldiers by
· Attending scheduled maintenance periods.
· Ensuring that the unit first sergeants and staff NCOs, as well as
firstline
supervisors, attend and participate in scheduled maintenance
periods

## Slide 36
· Checking maintenance operations continually, from the operator through
the battalion motor sergeant, and correcting where applicable.
· Identifying maintenance operational weaknesses and executing
corrective action through the NCO chain.
· Knowing the units' personnel gains, losses, strengths, and weaknesses
and advising the battalion commander accordingly.

## Slide 37
Battalion Executive Officer. The battalion executive officer (XO) acts as
principal assistant and advisor to the battalion commander. The XO
supervises the details of operation and administration, thereby enabling the
commander to devote maximum time to new or unusual problems. The XO keeps
abreast of the logistical and tactical situations and future plans and is
constantly prepared to assume command in the absence of the commander. The
responsibilities of the XO in the maintenance field are

## Slide 38
· Supervising plans and reviewing periodic and special reports to be
submitted to higher headquarters.
· Serving as battalion logistics readiness officer.
· Directing staff analysis of the maintenance situations.
· Evaluating the maintenance program.
· Recommending changes to the maintenance program

## Slide 39
Battalion Commander. The battalion commander commands and provides
direction to the units of the battalion. He assigns the duties of the staff
officers and establishes the necessary policies and guidelines that will
enable the battalion to effectively accomplish its maintenance program. The
battalion commander's specific responsibilities in the maintenance program
include
· Rendering advice and assistance in planning the program for unit
maintenance that is performed by maintenance personnel on battalion
equipment.
· Exercising command supervision over maintenance activities throughout
the battalion.

## Slide 40
· Advising brigade or higher headquarters of all aspects of maintenance
and repair parts supply requirements and repair parts supply support,
problem areas, recommended solutions, and anticipated requirements.
· Directing maintenance and repair parts supply policies and guidelines
within the battalion.
· Monitoring The Army Maintenance Management System (TAMMS) data
accumulators, analysis, and transmission.

## Slide 41
SAFETY RESPONSIBILITIES
Safety is a command responsibility, and commanders at every level are
responsible for conducting a continuous, vigorous effort to prevent
accidents in all operations and activities. Commanders must ensure that
adequate provisions for safe practices and physical standards are
incorporated into all directives, SOPs, and training doctrine.

## Slide 42
All supervisory personnel assist the commander in the unit accident
prevention program by requiring adherence to established safety procedures.
They orient new personnel, teach safe practices, enforce rules and
regulations, investigate accidents, prepare and submit accident reports, and
conduct safety inspections and safety meetings as required. No one is
better qualified or in a more strategic position to discover and correct
safety hazards than the supervisors within an activity. They deal directly
with both the worker and the job. They are in the best position to improve
the worker's skill, knowledge of the job, and attitudes toward the job.
Additionally, they insist on safe

## Slide 43
practices on the job and ensure that unsafe working conditions are
corrected. When they fail in any one of these responsibilities, they can
expect inefficient and costly results. Supervision is a method of
preventing accidents through continuous instruction and guidance, official
persuasion, and recourse to enforcement when necessary. Supervision is a
basic accidentprevention
control; it is based on the principle that safety
standards can be ensured if the training and development of good work habits
are provided. Individual competency will then be ensured regardless of
whether or not the supervisor is in the area. When a supervisor fails in
this respect, constant observation and frequent enforcement become
necessary.

## Slide 44
During this learning event, we discussed the maintenance responsibilities
from the squad leader to the battalion commander and how they interface with
each other. Remember that however well developed a program may be, it will
fail or be inefficient if the supervisors do not apply themselves

## Slide 45
Learning Event 3
MAINTENANCE SUPERVISION
Maintenance management is the way the commander brings together people,
equipment, tools, supplies, repair parts, facilities, publications, and time
to promote operational readiness.
SUPERVISORY FUNCTIONS
The supervisory process is organized into five functions: planning,
organizing, coordinating, directing, and controlling. The supervisor
usually deals with several or all of them at the same time. Feedback
enables the supervisor to evaluate the situation and adjust the process to
reach the desired goal. Let us look briefly at each of the supervisory
functions

## Slide 46
· Plan. Planning shows the way to reach a goal or objective. The
supervisor must have a clear idea of what needs to be done. Once the
objective is known, the supervisor outlines the steps to reach it. Judgment
and experience are used to develop a plan that will get the job done on
time, within required standards, and with the least resources.
· Organize. The organizing function provides a tentative list of
required resources and a schedule for meeting the plan.
· Coordinate. Detailed coordination ensures that resources will be
available and that the organization can support the plan.
· Direct. When resources have been organized and coordinated, the
supervisor directs their application according to the plan

## Slide 47
· Control. The supervisor controls the use of resources to ensure that
work is on schedule and according to the desired standards. The chain of
command usually assists in this function. Feedback from reports and
personal observation ensures that the operation is being carried out. When
the objective or level of resources changes, the supervisor may need to
modify the original plan. The cycle repeats until the job is done.

## Slide 48
SUPERVISORY TECHNIQUES
Maintenance supervision is a demanding and difficult job and is influenced
by many factors. There is usually a high sense of urgency to get results.
There are conflicting demands for the supervisor's time. Each supervisor
develops an individual style to meet the challenges of the job. There are
different approaches to supervision, but the following are most common:
Reactive Management. The inexperienced supervisor usually reacts to
requirements as they occur and confronts one challenge at a time. This is
called reactive or crisis management. The theory is to concentrate
resources against a particular requirement, overwhelm it, and move on. This
works well in a true crisis. In daytoday
maintenance operations, however,
there is seldom one crisis at a time. Unit mission requirements and the
training schedule change frequently. What is important today may not be so
important tomorrow. The reactive manager has to constantly juggle limited
resources and stays too long on individual projects to effectively manage
the overall operation.

## Slide 49
Proactive Management. The strategy of proactive management is to influence
events before they happen. The proactive manager anticipates requirements
and plans for the best use of resources. Time is his most important
resource and he uses it to gain the most benefit for the organization. He
directs the efforts of personnel productively while finding time for
management. The most important part of supervision is identifying
objectives and priorities. The proactive manager knows that effective
planning depends on determining what needs to be done and in what sequence.
He directs available resources first toward those actions that will be most
productive for the organization.

## Slide 50
SUPERVISORY FACTORS
Maintenance supervision deals with various factorscommand
emphasis,
management supervision, motivation, skill, and resourceswhich
affect the
way the unit does its maintenance mission. The supervisor uses these
factors as tools to help him guide the effort in the proper direction.
Failure to achieve desired results often stems from failure in one or more
of the maintenance factors. Corrective action depends on the supervisor's
ability to recognize which factors need to be influenced.

## Slide 51
Command Emphasis. The commander sets the tone for what is and is not
important within his command. To place command emphasis on maintenance
operations, the commander must show an active interest in maintenance
operations and the material readiness of unit equipment. Command emphasis,
the most important supervisory factor, influences maintenance and the
supervisor may use it to support the mission. Personal examples, words, and
actions are the best means to demonstrate the areas to be emphasized

## Slide 52
Management. The maintenance supervisor must constantly strive to improve
operations. Since the management process itself plays a key role in
maintenance operations, the supervisor should always be alert for ways to
improve planning, organizing, coordinating, directing, and controlling, as
well as obtaining feedback on results. Under the stress of daytoday
operations these elements lose visibility and may not seem to have a direct
bearing on material readiness. However, a small improvement in the "system"
brings greater overall benefits than a "heroic" effort on one or two items.

## Slide 53
Supervision. The commander depends on the firstline
supervisor for
accomplishing the mission and ensuring the welfare of the soldiers. The
supervisor is a vital link in the chain of command. Receiving instructions
and turning them into tangible results and passing along the commander's
requirements are only minor responsibilities. The major challenge lies in
making sure the people being supervised can accomplish the mission. The
supervisor is the individual soldier's primary source of assistance and
further professional development. Knowing proper maintenance procedures and
being technically proficient in the tasks to be done by the soldiers, the
supervisor also needs to know the standards and objectives set by the chain
of command so that the efforts of the soldiers are guided in the proper
direction. Being constantly aware of mission requirements and the
capabilities and limitations of the soldiers, the supervisor must look
beyond peacetime daytoday
operations and train soldiers to support the
needs of the battlefield. Next to the mission, the welfare of the soldiers
and their professional development should be most important.

## Slide 54
Motivation. Motivation is the desire of the individual to perform a
specific task. The leadership demonstrated by commanders and supervisors
greatly influences the motivation of soldiers under their control. Strong
leadership is the key to motivation. The strong leader defines the
objectives, communicates them, evaluates how well they are being achieved,
and provides feedback to the people doing the work. Most soldiers want to
perform well, but they must know "the rules of the game," the standards
expected of them, and how they are doing. Superior achievement should be
recognized, and the supervisor should have an active interest in the unit
award program.

## Slide 55
Skill. Skill is the technical ability to do the tasks associated with one's
duty position. Training is the means which provides skills to individuals.
The skill of the soldiers is one of the commander's most important assets.
The Army training system depends on the unit commander to continue the
training process begun during advanced individual training. A large number
of training resources are available, and the commander and maintenance
supervisor should use these to the maximum advantages. Soldier's manuals,
individual job books, skill qualification test (SQT) results, and personal
observation provide the firstline
supervisor the means to evaluate and
improve the skills of the soldiers.

## Slide 56
Resources. Resources are the tangible and intangible assets needed to get
the job done. They include people, tools and test equipment, repair parts,
publications, facilities, time, skills, funds, and other items. The
maintenance supervisor's goal should be to maintain readiness at the
required level with the least amount of resource expenditure. The
supervisor determines the resources needed to support specific mission
requirements and advises the commander on the logistic impact of various
courses of action.

## Slide 57
Learning Event 4
STANDING OPERATING PROCEDURE
A standing operating procedure provides the foundation of the unit
maintenance program. The SOP is the standing order of the commanding
officer. It carries the same weight and authority as any other lawful order
of the commander. Failure to comply with the SOP may subject individuals to
disciplinary action. The SOP is developed for common and repetitive
situations. It frees the supervisor to work on nonroutine projects or
problem areas. A sound maintenance SOP is essential to the success of
tactical operations and administrative and logistical procedures. The SOP
provides a guide for inexperienced personnel. Copies of the SOP should be
available for ready reference. New personnel should be briefed on the unit
program and either provided a copy of the SOP or shown where they can get
one.

## Slide 58
The SOP is a "living" document. It should be tailored to the needs of the
unit. Duties and responsibilities of maintenance personnel need to be
spelled out. The soldiers need to know how they are expected to contribute
to the overall program. The SOP should be printed in the most effective and
convenient form. When a better way is found to do an operation, it should
be included in the SOP. Changes to the maintenance program should be posted
in the unit SOP. If it is impractical to post the changes to all copies,
one or two complete record copies should be maintained. When pen and ink
changes interfere with clarity or continuity, a new printing is needed. The
commander must ensure that changes to the SOP are coordinated and that
everyone understands the new procedures.

## Slide 59
CONSIDERATIONS FOR AN SOP
1. The SOP must provide a functional organization for maintenance and
recognize the need for mission accomplishment, quality workmanship,
and tool control.
2. Command policies should be brief statements of what will be done.
3. Appendixes should be used for detailed organization and procedures.
4. Terms that are not common should be defined.

## Slide 60
5. Workflow, inspection, and verification of services should be
continuous.
6. Scholarly treatment, staff jargon, and directives readily available in
Army regulations, technical manuals, and other official publications
should be avoided

## Slide 61
SOP FORMAT
An SOP generally has a standardized format that includes a heading, a body,
and a close (authentication).
Heading. The heading identifies the unit which prepared the SOP, its
location, and mailing address. It gives the date of issue, provides a file
or SOP number for reference, and gives the SOP title.
Body. The information in the body of the SOP is tailored to the needs of
the preparing unit.
Close (Authentication). The close of the SOP contains the signature of the
commander, a list of the annexes to the SOP, and the distribution. When the
SOP is an annex to a higherlevel
document, the close contains the signature
of the authenticating officer of the responsible staff element. In this
case, the signature of the commander is not required. Refer to Extract of
FM 292,
Appendix B, Sample Battalion Maintenance Standing Operating
Procedure.

## Slide 62
LESSON 2
FUNDAMENTALS OF MAINTENANCE OPERATIONS

## Slide 63
Learning Event 1
WORKLOAD ORGANIZATION
The unit maintenance workload can be organized into broad categories for
management control as shown in Figure 1. During maintenance operations the
right personnel, tools, equipment, publications, records and reports,
supplies, repair parts, and time must be brought together to do the job.
These operations fall into the areas of operator/crew preventive maintenance
checks and services (PMCS), unit level repair, provision of repair parts,
requests for higherlevel
support, scheduled services, and dispatch of
equipment. The procedures to guide these operations should be provided by
the unit SOP. This learning event provides a type of workload organization
which may be adapted to suit individual unit requirements.

## Slide 64
MAINTENANCE CYCLE
Most maintenance requirements are part of the maintenance cycle shown by
Figure 1 on page 30. The requirement is usually identified while the
equipment is in use. The equipment is taken out of use, the required
maintenance operation is performed, and the equipment is put back into use.

## Slide 65
OPERATOR/CREW PMCS
The daily PMCS is the foundation of the unit's maintenance program. Some
types of maintenance requirements are identified by other means, such as
malfunctions, oil analysis, and command checks. However, the daily PMCS
ensures that the readiness of all applicable equipment is checked on a
recurring basis and that a record is made of faults which cannot be
corrected on the spot. Maintenance record keeping begins with Department of
the Army (DA) Form 2404 (Equipment Inspection and Maintenance Worksheet).
Figure 2 on page 31 shows the workflow for the daily PMCS. The
operator/crew follow the PMCS inspection steps listed in the applicable
operator's manual. Onthespot
corrections are made whenever possible.

## Slide 66
Faults beyond the operator's/crew's capability and those which require parts
must be recorded on the DA Form 2404. This ensures that repairs are made or
parts demand data are recorded. If no faults are noted, the date is
recorded on the DA Form 2404 "Daily" and the equipment is made available for
use. If a fault beyond the ability of the operator/crew to repair is found,
they report it to their supervisor and the equipment dispatcher for
corrective action by unit maintenance personnel.

## Slide 69
UNIT MAINTENANCE REPAIR
Unitlevel
repairs begin with the identification of a unit maintenance
requirement. The workflow for unit repair is shown by Figure 3. The
records clerk receives the DA Form 2404 from the operator/crew. If the
equipment has a fault but is operational, the DA Form 2404 is given to the
maintenance supervisor. If the equipment is not operational, Department of
Defense (DD) Form 314 (Preventive Maintenance Schedule and Record) is marked
with a red tab, in accordance with DA Pam 738750,
before forwarding the
record to the maintenance supervisor.

## Slide 70
The maintenance supervisor reviews the documents and assigns a mechanic to
do the work. The mechanic verifies the reported faults. If the maintenance
allocation chart shows the fault can be corrected at the unit, the mechanic
completes the repair work. If the work is beyond the unit level, a
maintenance request is initiated. When repairs are finished, DA Form 2404
is posted and the document is forwarded to the maintenance supervisor, who
verifies that repairs have been completed and returns the document to the
dispatcher. The dispatcher makes the item available for use and posts the
equipment records with the current status so that pertinent documents can be
annotated, if applicable.

## Slide 72
REPAIR PARTS PROCEDURES
The general workflow for repair parts requests is outlined in Figure 4.
Local procedures may modify the workflow. When parts are needed to correct
a unit fault, they are posted on DA Form 2404 "Daily." The PLL clerk issues
parts. If parts are not available, the national stock numbers (NSN) are
verified using the 20P
technical manual or the Army Master Data File (AMDF)
and placed on order. For nondeadlined equipment, document numbers for the
ordered parts are posted on DA Form 240814
(Uncorrected Fault Record). The
equipment records clerk receives the DA Form 2404 "Daily." If the equipment
remains operational, it may be used until the parts are received. If the
equipment is inoperative, DA Form 2404 "Daily" is retained until the parts
are received.

## Slide 74
When the parts are received, the mechanic installs them. The DA Forms 2404
and 240814
are posted as the faults are corrected. The equipment records
clerk posts not missioncapable
supply/not missioncapable
maintenance
(NMCS/NMCM) data on DD Form 314 and releases the equipment.

## Slide 75
MAINTENANCE REQUESTS
The workflow for maintenance requests is outlined in Figure 5. The DA Form
2407 (Maintenance Request) is used at unit level maintenance for—
· Requesting maintenance from supporting activities.
· Reporting warranty claims.
· Requesting application of modification work orders (MWO) by support.
· Reporting MWOs done at unit level.

## Slide 77
The unit mechanic verifies that the equipment has a higherlevel
fault and
ensures that all unit faults have been corrected. The DA Form 2407 is
initiated and recorded on DA Form 2405 (Maintenance Request Register). The
equipment is then taken to the supporting maintenance unit. The inspection
section will confirm that direct support (DS) work is required and that all
maintenance has been performed. The supporting maintenance unit will notify
the supported unit when the equipment is repaired. After the equipment is
returned, DA Form 2405 is posted to show the maintenance request is closed.
The unit and/or support maintenance NMCS/NMCM time is posted onto DD Form
314 and the equipment is made available for use.

## Slide 78
SCHEDULED MAINTENANCE SERVICES
Equipment technical manuals and lubrication orders show maintenance and
lubrication services which must be performed at prescribed intervals. The
DD Form 314 is used to schedule maintenance services and also to show when
services were actually performed. The use of this form is described in DA
Pam 738750.

## Slide 79
DISPATCH PROCEDURES
The dispatcher uses DA Form 2401 (Organization Control Record for Equipment)
to identify the user and location of equipment while it is on dispatch or in
use. This tells the commander who is using that equipment, where it is
located, and the expected time of return. Figure 6 shows the sequence of
actions for equipment dispatch. Additional controls may be set locally by
the unit commander.

## Slide 81
1. The equipment operator performs PMCS.
2. If faults are found, action is taken as shown in Figure 6. If no
faults are found, the dispatcher initiates DD Form 1970 (Motor Equipment
Utilization Record) and issues it with the equipment and DA Form 2404 to the
operator.
3. Equipment operators complete applicable portions of DD Fore 1970 as
they use the equipment. Faults found during operation are noted on DA Form
2404.
4. At the end of the mission, the operator performs afteroperations
PMCS, completes DD Form 1970 and DA Form 2404, and returns them to the
dispatcher.

## Slide 82
5. When faults have been noted, the dispatcher copies time of return and
other pertinent remarks from DD Form 1970 to DA Form 2401. After the
information is transcribed, the DD Form 1970 is destroyed unless its
retention for administrative purposes is directed by the local commander.

## Slide 83
MAINTENANCE PLANNING
Maintenance planning deals with what needs to be done and how to do it. The
maintenance supervisor, guided by the training and operational plans of the
commander, uses past experience and estimates to make forecasts of
maintenance requirements to support the commander's operational plan. The
unit's longrange
training plan outlines the major activities of the unit
over an extended time period. It represents events to be supported with
operational equipment. The maintenance supervisor forecasts the unit's
maintenance resource requirements. Estimates of the operational pieces of
equipment required to support the schedule, the number of items in scheduled
and unscheduled maintenance, and maintenance personnel available are
included. Figures 7 through 10 on pages 38 and 39 show a sample longrange
training plan and a combined requirements forecast. Personnel availability
is forecast to enable the supervisor to compare resources with requirements.

## Slide 84
The supervisor analyzes the unit activities and identifies when demands on
maintenance resources will be heavy, moderate, or light. Since the training
schedule is subject to change, the maintenance supervisor may have to change
the support plan accordingly

## Slide 89
The following observations are made on the sample training plan:
1. Heavy demands in equipment occur during November, February, April,
July, and August. The maintenance supervisor must ensure that unit
equipment is in good condition. Personnel needs and maintenance times must
be identified.
2. Moderate demands on equipment will be made during October, May, and
June.
3. Light demands on equipment will be made in December, January, March,
and September. The supervisor can recover from heavy demands during these
times.

## Slide 90
Equipment Operational Requirements. The unit will need all vehicles at the
major training areas. Unit training will require about 75 percent of the
unit vehicles.
Scheduled Services. Scheduled services must be performed according to the
technical manual. The supervisor may need to use the 10percent
variance to
plan services around periods of anticipated heavy use.
Unscheduled Maintenance. Unscheduled maintenance requirements and services
increase with usage. Older vehicles will require more unscheduled
maintenance. Much unscheduled maintenance will take place during periods of
heavy use.

## Slide 91
Personnel Requirements. Personnel availability is affected by departures,
arrivals, leaves, details, and other administrative losses. Available
personnel can be compared against anticipated requirements. Supervised onthejob
and cross training can be programmed against anticipated shortages

## Slide 92
MAINTENANCE CONTROLS
Maintenance controls at the unit level consist of supervisory tools which
provide visibility to the situation and assist in maintenance operations.
Some of the tools, such as TAMMS forms and records, are prescribed by
regulations. Some are developed and maintained on an informal basis.

## Slide 93
1. Equipment Status Chart. An equipment status chart lists assigned
wheeled and tracked vehicles and other selected major items. It also
identifies the assigned operator and shows the equipment status. The
Remarks column explains the faults, when applicable, and supply and
maintenance information. The status chart is usually maintained by the
motor sergeant or a designated representative.
2. Workload Control Board. A workload control board (Figure 11) provides
the repair or service status of the items in the shop. This board may be
used for daily review or planning meetings, assigning work, briefing the
commander, and verifying the accuracy of applicable TAMMS documents.

## Slide 95
3. Work Assignment Sheet. At the close of the duty day, the unit motor
sergeant should review the work accomplished and organize for the following
day using a work assignment sheet as shown in Figure 12. Previous sheets
show the work still in progress and the mechanics who are involved. A new
sheet for the following day assigns new work or reallocates old work. The
work assignment sheet provides the basis for the initial daily work
assignment and the review meeting at the start of the duty day. The Remarks
column may be used to record an individual mechanic's performance or the
need for additional training.

## Slide 97
Learning Event 2
INSPECTIONS
Inspections are means by which commanders can determine the serviceability
of equipment and promote efficient maintenance operations. Although the
most desirable inspection may be one made personally by the commander, the
type of inspection most often conducted is one made by technicians and
specialists under the direction of the commander or the commander's
appointed representative. A commander who is not on the scene of an
inspection must rely on a report of the results. This report must mean the
same thing to the commander as it did to the inspector who prepared it. The
commander's view of this report, actions to require correction of reported
faults and of conditions which cause unsatisfactory equipment and
maintenance operations, and actions to commend superior performance are
almost as important as the inspection itself.

## Slide 98
An inspection limited to the condition of equipment and requiring correction
of identified faults indicates to the commander the readiness of equipment
to perform the mission. The larger the sample inspected, the more valid or
reliable is the indication. Some equipment inspections, such as preparation
for overseas movement or equipment transfer inspections, must be total in
nature in order to accomplish their objective

## Slide 99
An inspection of a unit's maintenance program should include inspections of
· Sample quantities of various types of equipment.
· Records of operation, maintenance, and equipment.
· Personnel strength, training, organization, and productivity.
· Maintenance and supply procedures and shop operations.
· Adequacy of tools, facilities, publications, supplies, and repair
parts.
· Personnel capabilities, as determined from results in evidence and
from questions and answers during the inspection

## Slide 100
The inspection of overall maintenance management and the degree of material
readiness should include the areas listed in the preceding paragraph as well
as various repair parts requests and maintenance requests, with a followup
to supporting maintenance activities.

## Slide 101
An inspection for its own sake may be worse than no inspection at all. Most
inspections are somewhat harassing, disrupt normal operations and schedules,
and generally result in extra policing efforts, "eyewash," and 'paper
maintenance' that add little to equipment readiness or productive
maintenance. Therefore, commanders should establish and make known the
standards by which they will inspect or will have the command inspected.
They should ensure that these standards can be attained within the time,
resources, and support available to the unit and that the soldiers in the
command understand what is expected of them. Each inspection must have a
purpose. The results must be critiqued with the responsible personnel and
followed up to provide assistance, if needed, so as to ensure that the
original inspection objective has been reached.

## Slide 102
FREQUENCY OF INSPECTION
Periodic inspections or services are directed for specific items of
equipment by the applicable technical manual. The inspection intervals vary
by type of equipment, the level of maintenance by which the service is to be
performed, and the services to be accomplished. These inspections are
scheduled and conducted by organizational or support maintenance personnel.

## Slide 103
The Department of the Army does not prescribe the frequency for maintenance
management inspections. Generally, command and maintenance inspections will
be prescribed by directives from Army field commands or other intermediate
headquarters. In determining their own requirements for inspections,
commanders should consider the degree to which these inspections meet
existing needs for the types of information they provide. Duplication of
effort by conducting one inspection on the heels of another may then be
avoided both at the command level and at the inspected unit level.

## Slide 104
Unsatisfactory phases of inspections should be followed up by a reinspection
within 2 to 6 weeks. The reinspection is not a duplication of effort in its
effect. The inspection may be conducted by a command subordinate to the
headquarters which performed the initial inspection, but it

## Slide 105
should be at least one or preferably two command levels higher than the unit
to be reinspected. If a reinspection is made by a command other than the
one which conducted the initial inspection, the procedures and standards to
be used must be clearly stated and understood.
Each time a transfer of equipment occurs between two organizations, an
inspection of the equipment involved should be completed by a common
headquarters. In addition to acting as an arbitrator, the inspecting team
can evaluate the maintenance program of the owning unit. At the same time,
the inspecting team can demonstrate to the unit receiving the equipment the
inspection and maintenance standards acceptable to the command.

## Slide 106
PREVENTIVE MAINTENANCE (PM) INDICATORS
The term "PM indicator" is used to describe salient features of personnel,
materiel, supplies, procedures, and facilities, the known condition of which
will indicate the quality of preventive maintenance. The formal definition
of the term is "areas of possible failure or malfunction in equipment which
can be detected by localized application of the sense of sight, sound,
touch, and smell and which indicate the condition and quality of
maintenance."

## Slide 107
Commanders should determine prior to an inspection which items of equipment
or maintenance functions they are going to inspect. They should select a
few indicators for each item and become thoroughly familiar with them. This
will develop a feeling of confidence and impress personnel of the inspected
unit with the commander's interest in maintenance. Different indicators for
the same equipment should be selected for succeeding inspections so that
personnel will not fall into the habit of maintaining only what they know
will be inspected.

## Slide 108
The program of PM guides for commanders has been established by the
Department of the Army to provide consolidated PM information for use by any
commander. The PM guides can assist in estimating PM requirements, planning
and managing a PM program, instructing subordinates, scheduling and
conducting inspections, and evaluating the effectiveness of PM programs.
During an inspection, commanders should always remember that the most
important indicator of all is the item's performance of the functions for
which it was designed, and the relative chances that it will continue to do
so based on the care that it is receiving.

## Slide 109
There are three primary reasons for commanders to use PM indicators:
1. The commander should inspect. The most critical single factor in an
effective maintenance program is the personal inspection of equipment by the
commander. There is a common tendency to consider the physical inspection
of equipment as a function reserved for the equipment specialist and beyond
the capability or activity of the commander. This is a misleading notion of
the command function and could undermine an otherwise enthusiastic
maintenance effort.

## Slide 110
2. The commander is not a specialist. A commander's inspection must be
limited in scope for practical reasons. The relative complexity of modern
equipment, the extensive technical knowledge required of specialists, and
the normal length of assignments in command positions make it impractical
for most commanders to know highly technical details or to inspect for them.
The PM indicators are a logical compromise solution to this problem.
3. Time is a limiting factor. Even if the commander were a technician,
the attention he must devote to other command responsibilities limits the
time available for thorough inspections of equipment. The use of PM
indicators to concentrate on significant, readily accessible inspection
points makes the most efficient use of the commander's time.

## Slide 111
EQUIPMENT PM INDICATORS
Equipment PM indicators are in most cases detailed and specific. They
enable the commander to know precisely what to look for. However, in
addition to specific equipment indicators, there are several PM indicators
which may have a general application to many types or categories of
equipment. The commander or inspector should be alert for evidence of the
general indicators. The following fall into categories of general equipment
PM indicators:

## Slide 112
1. Adjustments. Proper tolerances, clearances, and travel are required
in many areas. Evidence of chafing, binding, cracking, rips, or split
seams, and erratic operation indicates improper adjustment. Improper
adjustment may frequently be quite evident in the amount of play in belts,
pulleys, levers, or gears, and the amount of lateral movement which may be
felt in bearing adjustment.

## Slide 113
2. Color and Marking. Conspicuous colors are used in areas of caution or
safety. Decals and data plates contain very specific, purposeful
information and those which are missing or illegible should be replaced.
Color codes are generally applicable for various types of ammunition, high
pressure tubing, and electrical circuits.

## Slide 114
3. Cleanliness. Cleanliness as it relates to maintenance must be
considered from the standpoint of its effect upon the proper functioning of
equipment. Uncleanliness may conceal deficiencies and shortcomings
resulting in further damage to the item. Functional surfaces should be
generally free of foreign matter so that cracks, dents, corrosion, or rust
can be readily detected, and so that it will not interfere with the proper
operation or function in areas such as metaltometal
bearing surfaces,
filters, or areas requiring lubrication. Fuel and lubricant leaks create
safety hazards. The accumulation of foreign matter, grease, and oil cannot
be tolerated in areas subject to fire

## Slide 115
4. Equipment Records. Records must be uptodate,
legible, accurate, and
must indicate the true status. Outstanding MWOs, other deferred
maintenance, and the amount of uncorrected faults, along with the supply
action and timely scheduling of maintenance, can be determined from
equipment records as an indicator of the quality of maintenance. Pencil,
ink, or typed entries do not necessarily indicate the quality of
maintenance.
5. Lubrication. Lubrication orders should be on hand and in active use.
No evidence of grittiness or binding should be evident in bearings or areas
requiring lubrication. Grease fittings should be clean and clear, and the
proper tools should be on hand.

## Slide 116
6. Safety Features. Compliance with commonsense safety requirements is a
sound indicator of a good PM program. Fire extinguishers, emergency exits,
and safety devices should be easily accessible and conspicuously marked.
Containers for poisonous or flammable liquids must be isolated and properly
labeled. Electrical grounding systems must be of an approved type, in
place, secure, and provide a positive ground. Warning systems, buzzers, or
lights should be tested to ensure proper operation. Observe for the
presence of protective clothing, guards, shields, or screens, where
appropriate, to preclude injury.

## Slide 117
7. Smell. An inspector should be alert for the presence of unusual
odors. Abnormal odors may be due to electrical circuits shorting out,
overheated motors or other components, lubrication failure, or leaks. A
strong smell of gasoline or other fuels should not be present. Mildew or
rot due to prolonged storage in confined areas gives characteristic odors
which should be investigated.

## Slide 118
8. Stowage. Most major items are used with some ancillary or basic issue
list items of equipment, and the methodical stowage of such material is
indicative of good preventive maintenance. The location and positioning of
tools, accessories, and repair parts in stowage must be such that they are
protected from damage and deterioration. Any stowed material must be
serviceable. Doors, catches, hinges, and handles on stowage compartments
must be secured and functional. Periodic, routine airing of canvas,
camouflage, nets, and blankets is needed to dispel mildew and mold.

## Slide 119
MAINTENANCE MANAGEMENT INDICATORS
No organization or unit which does its own organizational maintenance is too
small to perform some maintenance management functions. A commander's
evaluation of maintenance management within his organization is coequal in
importance to determining the status of equipment. One or more of the
management indicators of maintenance, at one level or another, is generally
the source to which equipment problems can be traced.
Figure 13 shows an incomplete checklist of maintenance management
indicators. The checklist is organized as follows:

## Slide 120
1. The paragraph title shows the subject area covered by the indicators.
2. A suggested guide for the frequency of checks appears in parentheses
after the title.
3. Specific checks are crossreferenced
to the six key supervisory
factors discussed in Lesson l/Learning Event 3command
emphasis,
management, supervision, motivation, skill, and resources.

## Slide 124
4. Rankorder
numbers have been assigned to the maintenance factors
opposite each indicator. These assist the manager in identifying trends and
determining the basic cause(s). When the answer to a particular indicator
is "No," the numbers, beginning with "1", show the maintenance factor which
is the most probable cause for the failure.
The checklist may be used by anyone concerned with maintenance operations.
Daily checks are routinely performed by firstline
supervisors during daytoday
maintenance operations, and by others as required. The manager
should informally perform the weekly, monthly, quarterly, and seasonal
checks in the area of responsibility and encourage others to do the same.
The manager's overall program of checks should ensure that all aspects of
the operation for which the manager is responsible are periodically covered

## Slide 125
In preparation, before making indicator checks, the manager should determine
the objective for the check. This will normally be to determine the
adequacy of some specific aspect of maintenance operations. The manager
then selects the indicators that will best provide the desired information.
After the checks are made, the results are analyzed. Since the checks are
only a sample, the manager must use care in drawing conclusions, either good
or bad, from the results. The results are best used to spot general trends
for further evaluation or action. For example, a relatively large number of
"1" and "2" rankorder
numbers under a particular maintenance factor should
prompt the manager to take a closer look in this general area

## Slide 126
When the underlying cause has been determined to the manager's satisfaction,
required corrective action is formulated. As needed, the unit chain of
command assists in its implementation. Care must be taken so that the
corrective action treats the cause and not the symptom. Correction of only
the specific individual faults uncovered by the check is of limited value.
After corrective action has been implemented, followup
checks are essential
to verify that the desired results have been achieved

## Slide 127
TYPES OF INSPECTIONS
Command Inspections. Command inspections are made to ensure proper use of
equipment to maintain supply economy, to ensure compliance with the
established procedures, and to evaluate operational readiness. Command
inspections are made periodically by unit commanders and/or their superiors.
There are two types of command inspections: formal and informal

## Slide 128
1. Formal Command Inspections. This inspection covers all unit
activities. The unit to be inspected is notified in advance. The notice
should include instructions on inspection procedures and on the arrangement
of the tools, vehicles, and shop. It should also include the date and hour
of the inspection, and the name, rank, and responsibility of each member of
the inspecting party. The inspection should be conducted rapidly,
thoroughly, and efficiently. The inspectors should follow a logical
sequence around each vehicle and through the shop. The findings of formal
inspections on all types of equipment are recorded on DA Form 2404 and
compiled for study and corrective action.

## Slide 129
2. Informal Command Inspections. An informal command inspection may be
made at any time. No advance notice is given and no set procedure is
required. This type of inspection provides a better picture of the
conditions within the unit. The commander sees the unit as it is operating
and improper practices and malfunctions are more easily detected.
Annual General Inspections. Annual general inspections provide commanders
with a continuing assessment of the operational and administrative
effectiveness of their commands. The heads of DA agencies and commanders of
Army field commands and installations that are authorized an inspector
general (IG) on their staff are responsible for making annual inspections of
all elements of their commands, installations, or activities. The overall
annual general inspection objectives are to—

## Slide 130
1. Evaluate management procedures and practices pertaining to personnel,
administration, material, and fund resources.
2. Identify problems, situations, or circumstances that impair mission
performance, and isolate associated causes.

## Slide 131
3. Determine the command or activity best suited for corrective actions
and evaluate the adequacy of past corrective actions.
4. Determine the state of discipline and morale throughout the command.
During the maintenance portion of the inspection, the IG inspects unit
maintenance operations and recordkeeping procedures. Unit material is
inspected for systematic servicing, preservation, adjustment, repair, and
prevention of abuse. In the inspection of organizational maintenance
activities, the IG determines if—

## Slide 132
· The unit has the technical skills, spare parts, and tools to perform
its maintenance functions.
· Applicable MWOs have been applied to the equipment and entered on DA
Form 24085
(Equipment Modification Record).
· The unit is performing only the level of maintenance for which it is
responsible.
· The unit has a current readiness profile of selected items of
equipment listed in DA Pam 738750.
· The operators are reporting accurate equipment status and are
recording data on the applicable TAMMS records.
· The operators are familiar with their equipment and its capabilities
and limitations.

## Slide 133
Technical Inspections. Technical inspections of equipment are made by DS
maintenance personnel. These inspections determine whether equipment should
be kept in service or withdrawn for overhaul or salvage of component parts.
Technical inspections also check the condition of the equipment at the time
of transfer or issue. If technical inspections reveal that organization
maintenance is substandard or that PM deficiencies exist, a report is made
to the commanding officer of the unit concerned. Inspection results are
recorded on the DA Form 2404.
SpotCheck
Inspections. Spotcheck
inspections are often used to ensure the
adequacy and effectiveness of organizational maintenance and supply and to
detect possible failure of equipment before unserviceability occurs. Some
spot checks are conducted periodically, others when requirements develop,
and some as a matter of operational

## Slide 134
routine. These inspections are conducted for specific purposes and include
the following:
· Inspections of work in progress by firstline
supervisors.
· Safety inspections by unit or higher safety personnel.
· Inspections of equipment by designated personnel to ascertain the
effectiveness of the maintenance program.
· Inspection of TAMMS, property accountability, and repair parts supply
documents.
· Roadside spotcheck
inspections of vehicles to verify serviceability,
operator qualifications, and compliance with regulations.

## Slide 135
Visits. A visit can serve as an informal inspection. Unit personal are
more likely to talk freely with a visitor who is interested in their
problems than they are with an inspector. The commander and maintenance
manager should visit the various unit maintenance activities as a matter of
routine. Subjects discussed and observations made during such visits may
include—
· Degree of satisfaction with the support received from the supporting
DS unit.
· Problem encountered in obtaining support.
· Future operations of the unit that my place heavy demands on equipment
and require increased maintenance and repair parts support.

## Slide 136
· Requirements for technical assistance.
· Adequacy of the unit maintenance program.
· Proper use of personnel.
· Adequacy of repair parts support

## Slide 137
Perpetual Inspection. The most important of all types of inspection,
however, is the kind that every officer and NCO performs continually as a
normal part of their daily military activities. Subordinates should be
indoctrinated with the concept that they need to inspect every piece of
equipment they see. All officers and NCOs are responsible for making onthespot
corrective actions whenever and wherever they find deficiencies in
the condition or operation of equipment. They should do this whether or not
they are members of the unit to which the equipment belongs. When a unit
acquires this philosophy of consistent correction as part of the attitude
known as "maintenance consciousness,' every member of the command will soon
recognize their responsibility for maintaining equipment.

## Slide 138
Learning Event 3
ARMY OIL ANALYSIS PROGRAM
The Army Oil Analysis Program (AOAP) analyzes equipment lubricant condition
to detect impending component failures through periodic evaluation of oil
samples. Oil analysis provides a diagnostic tool to determine the interval
conditions of engines, gear boxes, transmissions, and other oillubricated
systems and components. For policies, objectives, and responsibilities
concerning the AOAP, refer to Army Regulation (AR) 75022.
For detailed
procedures, refer to Technical Bulletin (TB) 430210.

## Slide 139
The purpose of the AOAP is to
· Detect potential component failure.
· Determine oil serviceability and necessity for oil change.
· Extend oil life and conserve resources.
· Reduce maintenance costs through preventive maintenance prior to major
repair.
· Develop a data bank relating to component wear or failure.

## Slide 140
DESCRIPTION
Oil analysis is used as a diagnostic tool to determine the physical
condition of used oil and the internal condition of engines, gear boxes,
transmissions, and hydraulic systems.
Spectrometric analysis is used to determine the concentration of various
wear metals in oil samples. Wear metals are metal particles of microscopic
size, produced by the friction of moving parts within mechanical systems,
that enter the oil stream and are dispersed and suspended throughout the
lubricating oil system. The kinds of metal particles and the quantities in
which they are present are detected by spectroscopy. Analysis helps
determine which component parts may have generated the particles. By
periodically sampling and testing the oil from mechanical systems, abnormal
wear can be detected and worn parts can be repaired or replaced before they
cause damage.

## Slide 141
Physical property tests are analytical tests used to detect property changes
in used oil. For example, changes in viscosity, fuel dilution, or water
content may be indicative of faulty equipment, operating conditions, or
maintenance procedures.
A resample is a sample, specifically requested by the laboratory, of the
same oil taken under the same conditions as the previous sample. Selected
equipment/components are those enrolled in the AOAP.

## Slide 142
RESPONSIBILITIES
Unit commanders will
· Implement local AOAP policies and procedures within their unit.
· Ensure that all AOAPdesignated
equipment is enrolled in the program
and that samples are submitted at prescribed intervals.
· Ensure that oil changes conform to warranty requirements.
· Ensure that laboratory recommendations are complied with immediately.
· Ensure that unit personnel are trained in AOAP procedures.
· Appoint a unit AOAP monitor

## Slide 143
SAMPLING
Only the equipment/components listed in the appendices of TB 430210
or
other equipment/components authorized by the PM AOAP will be sampled.
Routine samples are to be submitted at prescribed intervals as established
in the appropriate appendix of TB 430210.
(See Figure 14 for an example.)
Sampling intervals are not the same for all items of equipment. Samples
should be taken as near the prescribed interval as possible. Sampling at
the prescribed time is not always possible. In such instances, a 10percent
variance before or after the scheduled date, hours, or miles for sampling is
permissible

## Slide 145
NOTE: This equipment listing is incomplete. See TB 430210
for a complete
equipment listing and the sample intervals.
Special samples are samples other than those routinely scheduled. Special
samples will be submitted to the laboratory under the following
circumstances:
· At the request of the laboratory.
· Immediately before transfer among commands or overseas deployment of
equipment.
· After indication of a problem; for example, overheating or excessive
oil loss, or loss of oil pressure.

## Slide 146
When a vehicle is in storage, no sampling is required until the vehicle is
scheduled for operation use. Maintenance float equipment will be sampled
after 25 hours of operation or quarterly, whichever occurs first. When a
vehicle is used for developmental purposes, as a training aid, or for static
display, authorization to discontinue sampling or to sample at longer
intervals may be granted by the applicable major command. When the
equipment returns to normal operations, sampling intervals established in
the appendices of TB 430210
will once again apply.

## Slide 147
Special samples will be clearly marked SPECIAL and banded with red tape or
marked in some other conspicuous manner so that the laboratory may easily
identify them. The DD Form 2026 (Oil Analysis Request) that accompanies the
sample to the laboratory will be marked SPECIAL in the Remarks block, and
its borders will be outlined in red.
To support the AOAP, your unit will need to maintain an adequate level of
forms and sampling supplies. Supplies required for oil sampling operations
are listed in Figure 15. Quantities are determined by number and types of
assigned equipment enrolled in the AOAP and the frequency at which they are
sampled.

## Slide 149
The following listed forms are necessary to support the AOAP:
· DO Form 2026, Oil Analysis Request.
· DA Form 2407, Maintenance Request.
· DA Form 240820,
Oil Analysis Log.
· DD Form 314, Preventive Maintenance Schedule and Record.
· DA Form 3254R,
Oil Analysis Recommendation and Feedback.
The AOAP cycle operates as follows:
1. The TB 430210
identifies equipment for the AOAP. A DA Form 240820
is prepared for each component to be sampled.

## Slide 150
2. Sampling supplies are obtained.
3. Sampling dates are scheduled on DD Form 314.
4. An oil sample is obtained and noted on DA Form 240820
(Figure 16).

## Slide 152
5. The DD Form 2026 is prepared requesting an oil analysis (Figure 17).
6. The label on the sample bottle Ls completed, and the bottle and DD
Form 2026 are carried or mailed to the supporting oil analysis laboratory.
7. The oil analysis laboratory analyzes the sample for metal content and
oil quality, notes results on DD Form 2026, and returns the form to the
originating unit.

## Slide 154
8. In addition, maintenance recommendations are annotated on DA Form
3254R
and forwarded to the using unit for action (Figure 18).

## Slide 156
9. The unit takes the appropriate action indicated by the laboratory (DA
Form 2407).
10. The DD Form 2026 is filed and DA Form 240820
is completed.
11. Once maintenance actions have been completed, the supporting AOAP
laboratory should be notified of the results of the servicing action by
completing DA Form 3254R,
with' feedback annotated.

## Slide 157
Samples may be taken without warming a component to operating temperature,
if the equipment has been operated within the last 30 days. If the
equipment has not been operated within the last 30 days, it must be brought
to operating temperature before sampling. This applies to both routine and
special samples. There will be occasions when the laboratory may request
that a component be operated before sampling. This request will be complied
with.
Samples taken from an oil reservoir immediately after addition of new oil
will not be representative and will not become representative until complete
mixing of the old and new oil has taken place. This requires operation
until normal operating temperature has been obtained.

## Slide 158
SAMPLING METHODS
To take an oil sample using the valve method shown in Figure 191.
Remove dust cap assembly.
2. With the engine idling, open (lift handle) sampling valve and drain
out about a pint of oil; then shut off sampling valve.
NOTE: if sampling valve is mounted directly to the pressurized gallery, no
draining is required.
3. Place sample bottle under valve and fill to 1/2 inch from top, and cap
bottle.
4. Return drained oil to reservoir.

## Slide 160
The pump (Figure 20) is used to take samples through the oil filler neck or
through the dipstick hole. The procedure is as follows:
1. Determine how far the tubing has to be inserted into the reservoir by
using the dipstick as a gauge (Figure 20). Cut tubing to a length
approximately 10 inches longer than the dipstick

## Slide 162
2. Attach tubing to sampling pump by inserting tubing through "T" handle
opening. Allow tubing to extend approximately 1/4 inch below pump head
threads, and tighten "T" handle.
3. Attach the bottle to the sampling pump.
4. Carefully insert tubing into reservoir. Do not allow the tubing to
touch the bottom or sides of the reservoir, since any sludge entering the
tubing will contaminate the sample.
5. Hold sampling pump horizontally and pump until oil starts entering the
bottle. Fill the bottle to approximately 1/2 inch from the top. Depress
the vacuum relief valve (on top of pump) to stop flow.

## Slide 163
6. Withdraw tubing from reservoir. Loosen "T" handle and remove tubing
from pump. Discard tubing.
7. Replace reservoir cover.
Once you have drawn a sample, fill in your equipment bumper number and
component serial number on the sample bottle label (Figure 21) to avoid
confusion with other samples taken

## Slide 165
OIL SAMPLE SHIPMENT
Complete a DD Form 2026. This form must accompany all oil samples to the
laboratory. The following instructions explain the information required for
each block on the DD Form 2026 (Figure 17).
1. To Oil Analysis Lab. Enter the name of your supporting laboratory.
2. From Major Command/Operating Activity. On the first line, enter your
major command (for example, FORSCOM, TRADOC, USAREUR, EUSA). On the second
line, enter the full unit designation, and address, unit identification code
(UIC), and telephone number.
3. Equipment Model/APL. Enter the nomenclature and model number of the
component; for example, Engine AVDS 17902A,
XMSN CD 8506A,
Hydr Sys.

## Slide 166
4. Equipment Serial No. Enter component's serial number.
5. End Item Model/Hull No. Selfexplanatory.
6. End Item Serial No./Equipment identification code (EIC). Selfexplanatory.
7. Date Sample Taken. Enter day, month, and year sample was taken.
8. Local Time Sample Taken. Leave blank.
9. Hours/Miles Since Overhaul. Enter cumulative number hours/miles on
the component since new or last overhaul.
10. Hours/Miles Since Oil Change. Enter number of hours/miles since last
oil change on the component. If neither the component nor the end item has
an odometer or hourmeter, enter the total estimated hours.

## Slide 167
11. Reason For Sample. Check the block that is applicable. When the
reason is other, explain under Remarks; for example, initial sample, loss of
engine power, excessive smoke.
12. Oil Added Since Last Sample. Selfexplanatory.
13. Action Taken. Leave blank.
14. Discrepant Item. Leave blank.

## Slide 168
15. How Malfunctioned. Leave blank.
16. How Found. Leave blank.
17. How Taken. Selfexplanatory.
18. Sample Temperature. Selfexplanatory.
19. Type Oil. Selfexplanatory.
20. Remarks. Selfexplanatory.

## Slide 169
When samples are to be mailed, use the shipping sack. Insert the oil sample
bottle into the plastic bag and place the completed DD Form 2026 into the
shipping sack along with the plastic bag. Send it by firstclass
mail to
your supporting laboratory. Do not use bulk mail or parcel post.
When delivering the oil sample directly to the laboratory by courier, fold
the completed DD Form 2026 in half (lengthwise), wrap it around the oil
sample bottle, and secure it with a rubber band. Dispatch by courier to the
laboratory. Regardless of shipping method used, oil samples are to be
dispatched to the laboratory on the same day they are taken.

## Slide 170
FEEDBACK DATA
Laboratory recommendations will be annotated on DA Form 3254R
(Figure 18)
for components, when the oil sample analysis indicates a problem. The form
will be used only when a maintenance action is recommended and not to
request resamples or recommend oil change. The DA Form 32541
will be
forwarded to the using unit. This form may be reproduced locally on 8 1/2inch
by 11inch
paper.
After personnel in the using unit have performed the laboratoryrecommended
inspection or maintenance action, they will complete the lower portion of DA
Form 3254R.

## Slide 171
Block 14 will be used to explain any diagnostic performed, discrepancies
found, and actions taken to return the component to a serviceable condition.
The DA Form 3254R
will be returned to the laboratory within five working
days after maintenance is accomplished.
If a component is evacuated for repair, a copy of DA Form 32544
will
accompany it along with other appropriate paperwork. The support
maintenance or overhaul facility

## Slide 172
will record the maintenance accomplished on the DA Form 3254R
and return it
to the originating laboratory within five working days after maintenance is
accomplished.
NOTE: The AOAP pressuresensitive
labels will be used on components going
to a maintenance/overhaul facility. Two labels will be affixed to
opposite sides of the component and two on the opposite sides of the
outside of the shipping container. These labels will be supplied by
the laboratory along with the DA Form 3254R.

## Slide 173
To summarize1.
Remember to follow TB 430210.
2. The AOAP is a very effective maintenance diagnostic tool. It is not a
substitute for good maintenance.
3. For equipment under warranty, follow manufacturer's instructions for
oil/filter changes.
4. Keep sampling supplies and forms on hand.
5. Keep up your good maintenance.

## Slide 174
LESSON 3
TACTICAL AND GARRISON MAINTENANCE SITES

## Slide 175
Learning Event 1
TACTICAL MAINTENANCE SITES
The tactical situation and mobility requirements may limit the type and size
of facilities which can be established. Therefore, available resources must
be organized for maximum production. Each unit must develop SOPs for moving
to a new area, establishing and conducting maintenance operations, and
moving on to a new location, if necessary. The speed with which the
maintenance element can set up shop at a new location has a direct bearing
on the productive maintenance time available.

## Slide 176
SITE SELECTION
The unit commander will make a map reconnaissance before occupying an
unfamiliar bivouac area. After this, the commander sends out a
reconnaissance party to select operating sites and explore primary and
alternate routes of march. The ideal field maintenance site should
· Have ready access to supported elements, the main supply route (MSR),
and the local road Net.
· Be large enough to spread out yet small enough to defend, with room,
if possible, for vehicles, facilities, repair parts, and supply storage.
· Be reasonably flat, with firm soil and good drainage to permit parking
and movement of heavy vehicles.
· Be free of nuclear, biological, chemical (NBC) contamination and be
upwind from known contaminated areas and likely NBC attack targets

## Slide 177
· Be easy to secure, with streams and marshes, where available, used for
flank security.
· Have terrain features that provide cover and concealment. Those
features between the site and likely NBC targets should give added
protection.
· Be outside Natural air corridors to reduce the chance of air attack
and to assist in air defense.
· Have a source of potable water, if possible.

## Slide 178
The reconnaissance party briefs the unit commander on their findings. The
commander then selects the site which has the most favorable
characteristics. The commander organizes and briefs an advance party to
occupy and prepare the area for the unit.
ADVANCE PARTY COMPOSITION
The makeup and size of the advance party is governed by two things: the
tactical situation and the amount of work required to prepare the site for
occupancy. Personnel in the advance party may include

## Slide 179
· First sergeant.
· Assistant section chiefs/platoon sergeants.
· Food service personnel.
· Tactical wire operations specialist.
· Field sanitation team.
· Maintenance personnel.
· Additional troops for labor and security

## Slide 180
ADVANCE PARTY DUTIES
The advance party will place road guides and route markers from the old
bivouac site to the new location. These will be picked up by the last
vehicle in the convoy. The first task of the advance party on arrival is to
clear and secure the new site. After dismounting, the troops are organized
into fire teams. These fire teams move through the area searching for
mines, booby traps, information of intelligence value, and any other signs
of the enemy's presence. As soon as the area has been cleared, a light
security screen is provided around the bivouac site. This is done by
establishing observation posts and strong points along likely avenues of
approach to provide early warning and limited protection during the
occupation of the bivouac site. The tentative location of the company and
platoon command posts (CP) should be identified and provision for wire
communications made. Platoon and maintenance section representatives select
and mark off their areas. See Figure 22 for a sample maintenance section
layout.

## Slide 182
Roads and trails should be selected which provide for a oneway
traffic
pattern. Alternate exits should be selected and marked to provide emergency
exits, if the main exit is blocked. Individual parking areas should be
determined, with special consideration being given to the heaviest and most
awkward vehicles, such as tractors and trailers. Assistant platoon
sergeants should thoroughly reconnoiter their assigned areas, determining
tentative locations for individual foxholes and carefully locating crewserved
weapons.

## Slide 183
If possible, latrines and garbage sumps should be dug and screens and tents
erected. As the main body of the unit arrives, the vehicles should rapidly
clear the approach route, be guided into the bivouac site, and be parked.
Drivers should perform afteroperations
maintenance and top off fuel tanks.
Assistant drivers and operators should maintain their positions on the
perimeter and begin preparation of fighting positions and other defense
measures.

## Slide 184
BIVOUAC LAYOUT
Mess Facilities. Special attention must be given to the selection of the
mess area. It should be
· Centrally located within the perimeter.
· Away from interior roads to avoid contamination of food by dust.
· Located a minimum of 100 yards from latrines.
Serving Lines. These should be—
· Marked with engineer tape.
· Located to take advantage of available cover and concealment.
· Planned so that 5yard
intervals can be maintained between
personnel.

## Slide 185
Latrines. Latrines should—
· Be located on the side of the bivouac opposite prevailing winds.
· Be at least 100 yards downhill from the water supply.
· Be adequate for a minimum of 8 percent of the unit at one time.
· Have handwashing
facilities located near the exits.

## Slide 186
Maintenance. The selection of the maintenance location is dependent upon
accessibility of entrance and exit routes. The area should be centrally
located within the perimeter. The maintenance tent should have an entrance
and exit at both ends. See Figure 22 for an example of an organizational
maintenance layout.
Figure 23 shows a sample unit motor pool office layout housed in a generalpurpose
medium cent. The sidewall of the tent may be rolled up to allow the
prescribed load list (PLL) clerk to issue parts and to move small items from
the offloading
area to the storage location.

## Slide 188
Figure 24 depicts a layout example of a maintenance company, forward (DS) in
a field environment.

## Slide 190
It is estimated that a minimum of 25,000 and a maximum of 40,000 square
meters of usable area are required for a DS company forward. The minimum
area would provide for vehicle dispersion of approximately 12 meters. From
the standpoint of passive defense, the maximum area is more desirable. It
is the largest dispersion that can be attained without serious degradation
of unit efficiency and without increasing vulnerability to guerrilla
attacks. The maintenance company, rear, because of larger size, more
vehicles, greater supply stockage, and more workload, would require an area
one and onehalf
to twice as large.
Command post. The CP must be centrally located within the perimeter.
From here, it can exercise control over the company, remain well defended,
and have lines of communications with subelements.

## Slide 191
Fuel Tankers. The fuel tankers should be located as near as possible to
the primary entrance where returning vehicles are topped off, and then moved
to a protected position within the perimeter (away from likely avenues of
attack) that offers protection to the tanker as well as to adjacent
facilities.
Ammunition. The basic load of ammunition should be removed from the
transporting vehicles. It must be stockpiled and protected by sandbags or
an earth revetment, and located near the supply tent

## Slide 192
Troop Areas. Personnel will be permitted to sleep only in designated
areas. These areas should be close to the section of the perimeter these
troops are to defend. Vehicles will not be allowed to move without ground
guides in areas where troops are sleeping

## Slide 193
BIVOUAC DEFENSE
As soon as the main body closes the bivouac site, primary emphasis should be
on establishing and improving the defenses of the area. Platoon leaders and
the company commanders should confirm the CP locations and quickly review
the placement of the perimeter. Special emphasis is placed on siting crewserved
weapons to ensure allaround
defense. Where authorized, provisions
should be made to ensure construction of road blocks, placement of
antivehicular and antitank mines on likely avenues of highspeed
approach,
and the laying of a defensive antipersonnel minefield. If available, barbed
concertina wire, trip flares, and booby traps should be emplaced.
Individual and crewserved
positions are prepared and camouflaged, and wire

## Slide 194
is laid to CPs and observation and listening posts. A secondary wire net
over different routes should be provided, if possible, to ensure effective
communications if the primary wire is cut by enemy action. If possible, the
RC292
radio antenna at the company CP should be removed several kilometers
from the bivouac site to confuse enemy directionfinding
equipment. Trucks
and tents should be camouflaged with natural vegetation or the lightweight
screening systems. Range cards for each individual position and crewserved
weapon should be prepared. Coordination with supporting artillery, mortars,
and reaction forces should be made, and defensive map overlays prepared.

## Slide 195
ACTIVE DEFENSE
Active defense of a maintenance company's site does not Include fighting
beyond the perimeter of the bivouac area. Troops who man observation and
listening posts must go beyond the bivouac boundaries. Other members of the
unit do not go beyond the bivouac boundaries. Enemy ground forces may
strike a company at several points at the same time before mobile defense
forces can reach it. Therefore, the company commander must be prepared to
use his own forces effectively at all times. Here, it is assumed that the
maintenance unit is without outside assistance.
NOTE: A maintenance unit uses concealment, dispersion, and deception to
protect itself. It does not take offensive action.

## Slide 196
ALERT SYSTEM
The alert system for a maintenance unit provides for a twostage
alert. The
first stage, "attack likely," warns unit personnel by audible or visual
signal that an attack will probably take place. Troops are positioned in
pairs, and one soldier remains alert at all times. (If the situation
permits, the other member of the team may sleep.) During the 'attack
likely' alert, as many soldiers as possible man their defensive positions.
But every effort should be made to continue with the unit's normal mission.
When the secondstage
alarm, "attack imminent," is given, all personnel stop
their normal duties and man their defensive positions. The reserve force is
held in position near the CP until deployed by the unit commander.
Personnel remain in their defensive positions until the allclear
signal is
given.

## Slide 197
FIRING ON THE ENEMY
When enemy forces are observed advancing on the bivouac, fire on them with
longrange
weapons. This fire must cover the withdrawal of outposts when
the enemy threatens their security. Attackers must be kept under accurate
fire as they approach. When they are within 150 yards or less, they should
be hit with fire from all weapons. Enemy combat elements sighted in the
vicinity should not be fired on when it is apparent that they intend to
bypass the unit bivouac. However, information of enemy troops in the area
should be rapidly forwarded to the nearest senior commander of friendly
forces.
NOTE: Fire from machine guns should be strictly controlled to avoid
premature disclosure of their positions.

## Slide 198
COUNTERATTACKING
Make every effort to destroy the enemy if they penetrate the perimeter
defense. The commander may use his reserve forces to destroy attackers and
restore the integrity of the unit's position, or to block further advance by
the enemy. Supporting artillery and air support and the shock action of
armor may not be available. Therefore, the advantage of counterattacking
must be balanced against the advantages of continuing the fight from
positions which offer some cover from enemy fire. The chance of a
successful counterattack by maintenance troops is not good. Remember;
defense of the area does not include pursuit of hostile forces, only
elimination of the enemy from the bivouac area.

## Slide 199
WITHDRAWING
When faced with a superior force which threatens largescale
defeat or
destruction, withdraw. But first get approval of the next higher command.
However, when withdrawals are necessary, the immediate commander must make a
decision fast. The commander will want co withdraw before the defending
force is heavily engaged. When withdrawal from contact is necessary, a
small detachment is used to cover the withdrawal. Before withdrawing from
the area, destroy all equipment, supplies, and ammunition of value to the
enemy. When possible, the security force covering the withdrawal is
provided motor transportation. During periods of fighting with the enemy,
the platoon leaders should continuously provide situation and status reports
to the company commander. Use all means of communications to keep the
company commander informed. The commander must have information in order to
make sound, timely decisions.

## Slide 200
PASSIVE DEFENSE
Passive defense measures are taken to keep the enemy from seeing the bivouac
area. Passive security measures include concealment, camouflage of
positions, control of movement, noise and light discipline, and minimum
radio and telephone traffic. Concealment and dispersion are important
passive defense measures against attack from the air. Construct twoman
foxholes with adequate overhead concealment immediately after occupying a
site. Foxholes are usually camouflaged with growth from the surrounding
area. To conceal, use wooded areas and blackout lights, cover reflective
surfaces, use protective shadows, and limit movement. Use radios and
telephones as little as possible. One method of deceiving the enemy is to
make vehicle tracks into an unoccupied wooded area and conceal tracks
leading into the real bivouac area.

## Slide 201
CLEARING THE BIVOUAC AREA
A unit normally starts preparing to clear a bivouac soon after it receives
word to move. The sequence used to clear a bivouac area can vary every
time. A good rule to follow is to concentrate the efforts of the unit in
the areas that take the most time.
1. Loading. First, unit members should pack their individual clothing
and equipment. Then, organizational equipment not immediately required for
defense of the area can be loaded on vehicles and secured for the move. One
exception to this procedure may be the kitchen equipment, which may be used
to serve a hot meal just before departure. This is preferable to feeding
individual rations while the unit is en route.

## Slide 202
2. Vehicles on Dispatch. Drivers of vehicles on dispatch should be
permitted to deliver their cargo. Companies about to move must either tell
supported activities that support will be discontinued or the location of
the new area.
3. Maintenance Section. The maintenance section will try to get all
inoperative vehicles in operating condition as rapidly as possible.
Vehicles which cannot be moved with the unit should be evacuated to the
nearest maintenance support activity. In a DS company, equipment which
cannot be repaired or evacuated will be destroyed.
4. Refueling. Fuel tanks of all vehicles should be topped off. If
petroleum, oils, and lubricants (POL) supplies are

## Slide 203
available, the basic load should be replenished. Any fuel that cannot be
moved will be destroyed.
5. Mess. When possible, personnel should be served a hot meal before the
unit's departure. When this is not feasible and the distance of the move is
great enough to permit, serve a hot meal en route. To accomplish this,
dispatch the kitchen ahead of the main body. Give the mess steward
instructions to rendezvous with the main body. The rendezvous should be a
predetermined point where adequate parking facilities are available. After
serving this meal, the mess section may be directed to join the advance
party. The mess section should depart with a full supply of water, fuel,
and rations.

## Slide 204
6. Garbage Sumps and Latrines. Fill garbage sumps with at least 2 feet
of dirt. When closing latrines, spray with an approved insecticide to kill
flies and other insects. Spray the contents of the pit, and side walls, and
the ground surface. Spray at least 2 feet around the pit. Then, fill the
pit to the top with successive 3inch
layers of earth. Pack each layer down
and spray its surface with insecticide. Mound the latrine over with at
least 1 foot of earth. Finally, mark the covered latrine with a sign
reading LATRINE CLOSED and the date.
7. Road Clearance. The road clearance is obtained from higher
headquarters or traffic control headquarters. Request road clearance as
soon as the unit is alerted to move

## Slide 205
8. Communications. Wire communication will be discontinued and all wire
recovered. Radio nets will be opened in accordance with the unit signal
operation instructions (SOI).
9. Closing Bivouac. After the unit is prepared for departure, the entire
area is policed. When the main body has moved from the area, a small
detachment should inspect the bivouac site. The detachment checks for
proper police and searches for items of equipment that may have been
overlooked.

## Slide 206
DESTRUCTION OF EQUIPMENT
Equipment may have to be destroyed to prevent its capture and subsequent use
by the enemy. The authority for ordering destruction of equipment is vested
in division and/or higher commanders, who may delegate authority to
subordinate commanders when the situation requires.

## Slide 207
DEGREE OF DAMAGE
Destruction should be such that the equipment and essential repair parts
cannot be restored to operation either by repair or cannibalization.
Classified equipment must be destroyed to prevent the enemy from gaining
knowledge about its operations and functions. Associated classified
documents must also be destroyed to render them useless to the enemy

## Slide 208
METHODS OF DESTRUCTION
Detailed methods of destroying specific items are in applicable technical
publications. The following methods may be used singly, or in combination:
1. Improper operationoverloading,
shortcircuiting,
or operating
without lubricants.
2. Fireuse
of gasoline, kerosene, diesel fuel, incendiary grenades,
flamethrowers,
or thermal devices.
3. Weapons fireany
rifle, machine gun, antitank weapon, or other weapon
which may be accurately aimed.
4. Demolitionany
military high explosive and fragmentation grenades.
5. Mechanical destructionsmashing,
bending, cutting, or slashing using
sledges, hammers, axes, rocks, heavy wrenches and similar hand tools,
crowbars, cutting torches, and so forth.
6. Use of natural surroundingssubmergence,
burial, concealment, or
scattering using shovels, spades, hoes, or other digging equipment.

## Slide 209
PRIORITIES FOR DESTRUCTION
Priority must always be given to the destruction of classified equipment and
associated documents. High priority is also given to destruction of weapons
and ammunition. When lack of time or means limits complete destruction of
equipment, priority is given to destruction of essential parts. These same
parts are to be destroyed on all like equipment

## Slide 210
Learning Event 2
GARRISON MAINTENANCE SITES
Maintenance units operating in a garrisontype
environment usually operate
in buildings. These may be expressly designed as shop buildings,
warehouses, aircraft hangars, or similar structures. In this type of
operation, the size of the area and the number, types, and sizes of
available buildings determine the area layout. A wellorganized
motor pool
is essential for control, management, and support of maintenance operations.
The unit mission and type of equipment will determine the type of facility.

## Slide 211
FACILITIES LAYOUT
Garrison maintenance facilities include buildings, hardstands, water supply,
electrical power, road nets, fences, and other real property. The largest
shop area is used for wheeled and tracked vehicles. Maintenance facilities
must
· Provide easy access.
· Be readily secured.
· Be centrally located.
· Have storage space for supplies, repair parts, tools, and equipment.
· Have a source of water.
· Have effective drainage.
· Have a rest/break area with adequate ventilation and heat for
operators and mechanics.
· Provide sufficient light.

## Slide 212
The facilities layout will depend on the size and location of the unit and
the facilities available. Major layout considerations include—
· Establishing a control point.
· Selecting equipment holding areas.
· Designing the shop area.

## Slide 213
· Controlling traffic flow.
· Establishing a secure area to control repair parts, tools, and test
equipment.
· Providing adequate lighting and safety.
· Ensuring security

## Slide 214
In laying out the area, the same considerations apply as in field
operations. For example, the control office, the supply office, and the
initial inspection section should be near the entrance to the area. Supply
traffic should be kept out of the maintenance areas. Elements with related
or complementary functions should be located near each other. Although
certain types of repair and parts fabrication are accomplished with
equipment mounted on vehicles, these vehicles, space permitting, can be
moved inside buildings. Refer to Figures 25 and 26, and to Figures 27 and
28 on pages 92 and 93 for suggested facilities layouts.

## Slide 219
DIRECT SUPPORT SHOP ORGANIZATION AND LAYOUT
The maintenance shop of a DS maintenance unit is normally composed of a
control element (maintenance control section), a service and recovery
element, and one or more maintenance platoons or sections. The shop is
responsible for receipt, inspection, control, repair, and/or evacuation of
all equipment received from supported units. Shop layout and workflow are
of prime importance in facilitating these operations. A good layout will
speed the flow of work through the shop and minimize the movement of repair
parts, tools, and equipment. (See Figure 29.) Principles to be observed
when laying out the facility include—

## Slide 220
1. Work sections should be located for ready access to each other.
2. Supply storage areas should be located to permit easy access for
trucks.
3. The service section should be located to provide easy access to all
maintenance shops.
4. Electronics and instrument repair should be accomplished in a dustfree
area.
5. The service and recovery element should be located in the vicinity of
the maintenance platoon or section to facilitate allied trades support and
the movement of vehicles.
6. The control section and the inspection element should be located near
the main entrance to the facility.
7. The supply platoon should be located near an entrance to keep heavy
traffic out of the work areas.

## Slide 222
FACILITIES MANAGEMENT
The unit commander and maintenance personnel must keep their facilities
repaired and make improvements which permit more efficient operation or
improve working conditions. The battalion S4 has staff responsibilities for
facilities management.
Most installations have selfhelp
programs for minor repairs and basic
improvements. Specific procedures are provided by the facility engineers at
each installation.
More complex maintenance and repairs involve support from the facilities
engineers. Work requests are grouped in two categories, as follows:

## Slide 223
· Service orders (SO) are used for small maintenance and repair jobs,
such as emergency repair of broken plumbing.. The repair service is
normally requested telephonically.
· Individual work orders are used for new work, repair, and minor
construction; inspections; PM; recurring maintenance and repair work for
buildings, grounds, surfaced areas, and utility systems; and miscellaneous
maintenance. The DA Form 4283 (Facilities Engineering Work Request XFA,
XFB, XFC) is used to request this type of support.

## Slide 224
LESSON 4
FUNDAMENTALS OF SUPPLY OPERATIONS

## Slide 225
Learning Event 1
SUPPLY PROCEDURES AND TERMINOLOGY
This learning event presents an overview of supply room procedures,
including storage, maintenance, safety, security, protection against weather
damage, and supply terminology. The success or failure of the entire Army
supply system rests to a great extent on the proper implementation of supply
procedures at the unit level. When equipment is received, managers and
supply personnel incur an obligation to account for it until it is returned
to the supply support activity. Accounting for equipment also includes
preparing and processing adjustment documents in the event equipment is
lost, damaged, or destroyed. As a maintenance supervisor, you will play a
very important part in supply management and accountability.
During this learning event, supply room procedures and supply terminology
will be discussed. This discussion is designed to show you, the maintenance
supervisor, the relationship between maintenance and supply. Your ability
to accomplish your maintenance mission will depend upon good unit supply
procedures.

## Slide 226
SUPPLY TERMINOLOGY
1. Inventory. The physical count of items on hand for verification with
the recorded balances.
2. Negligence. An act or an omission to act that a reasonable person
would not perform or fail to perform under similar circumstances. Full
consideration will be given to the degree of care and resourcefulness which
might reasonably be expected of the person concerned, considering their age,
experience, and special qualifications, as well as to the specific nature of
the property (personal or supervisory responsibility) in determining the
reasonableness of the act or mission in question. Monetary liability will
result when a person's negligence, willful misconduct, or wrongful
appropriation of government property is the direct or proximate cause of any
loss, damage, or destruction of such property.
3. Organization Clothing and Equipment. Clothing and equipment
authorized by the applicable common table of allowances maintained and
accounted for on the organization property book (for example, clothing, such
as parkas or shelter halves).

## Slide 227
4. Recoverable Item. An article selected on the basis of dollar value
and requirements, which is essentially worthy of being repaired and used
again.
5. Report of Survey. An official report used to record the circumstances
concerning the loss, unserviceability, or destruction of property, and which
serves as or supports a voucher for droppage of items from the property
records on which they are listed.
6. Responsibility. The obligation of an individual with respect to the
proper custody, care, and safekeeping of property entrusted to the
individual's possession or under their supervision, with or without receipt,
regardless of the condition of property (serviceability). There are two
distinct types of responsibility: command and direct

## Slide 228
· Command responsibility. Applies to the officer in command of an
installation, unit, or major activity, who has command responsibility for
the security of all public property of his command, whether in use or in
storage. Command responsibility extends to a thorough observation of
subordinates and enforcement of all security, safety, and accounting.
· Direct responsibility. Applies to individuals to whom public arms
and/or equipment is entrusted for care and safekeeping, whether such
property is in their personal possession, in use, or in storage. Direct
responsibility is divided into two types: personal and nonpersonal.

## Slide 229
Personal
responsibility. The relationship between an individual
and arms or equipment, including hand tools issued or otherwise acquired for
or converted to the individual's exclusive personal use, with or without
receipt. In addition, without exception, an individual has personal
responsibility for property that the individual has converted to their own
use without permission or authority; for example, a stolen vehicle.
Nonpersonal
responsibility. The relationship between an
individual and property under their control or supervision, within the scope
of the individual's employment, for which the individual does not have
personal responsibility.

## Slide 230
7. Sensitive Item. Material requiring a high degree of protection and
control because of statutory requirements or regulations, such as medical
items (narcotics, taxfree
alcohol, precious metals); highvalue,
highly
technical, or hazardous items; and small arms, ammunition, explosives and
demolition material.
8. Sets, Kits, Outfits (SKO). The assemblage of various items that
comprise a set of equipment designated for a specific use, such as a
carpenter tool set complete with all saws, hammers, levels, squares, and so
on.

## Slide 231
9. Statement of Charges. A form used by a responsible supply officer to
charge an enlisted soldier, officer, or Department of the Army civilian
employee for the loss, damage, or destruction of government property. This
form cannot be used when charges against any one individual exceed one
month's base pay. Reimbursement by the individual charged is accomplished
by payroll deduction.
10. Supply Economy. The careful, thrifty management and use of supplies
and equipment. Supply economy is the basic reason for conserving,
maintaining, repairing, recovering, preserving, safeguarding, and salvaging
supplies. Each soldier has a responsibility for supply economy.

## Slide 232
11. Surveying Officer. The officer authorized to make an inquiry and fix
responsibility for damage, loss, or destruction of military property when
such losses are determined to be not due to normal fair wear and tear.
12. Unserviceability. A more inclusive term than damage or destruction.
It indicates, in military usage, that the article(s) to which the term is
applied is/are no longer useful for the intended purpose. Damage or
destruction may or may not be involved. The term indicates property that
has deteriorated through use, but it may include property no longer usable
for its original purpose, regardless of the reasons for its condition

## Slide 233
UNIT SUPPLY ROOM PROCEDURES (STORAGE AND MAINTENANCE)
One of the first things that must be considered in discussions of supply
room procedures is the supply room itself. Other things that must be
considered in determining whether or not the supply procedures and security
measures are adequate include safety provisions, security against theft, and
protection against weather damage. Also considered will be certain items
that require special storage procedures.

## Slide 234
The layout of storage facilities is an important factor in determining the
efficiency and security of the storage operation. Therefore, each unit will
require certain storage facilities to protect, secure, and handle supplies
essential to its operation. A supply room is always necessary for storing
supplies and for controlling the issue of supplies. An arms room is
required to store weapons, and a toolroom or auxiliary storage room is
needed for storing miscellaneous supplies, such as tools, expendables, and
housekeeping supplies. A building away from the maintenance building is
necessary for storing paint if it is kept on hand in the unit.
A toolroom or auxiliary storage room may be used for storing tools and other
items that should be placed under lock and key.

## Slide 235
For safety, flammable scrap materials must be stored in open storage areas.
Working materials, such as paint, excelsior, and rags, when not properly
stored, present an extreme fire hazard. Therefore, these materials should
be stored in receptacles which are fireproof, sparkproof, and properly
marked to identify their usage. Selfclosing
metal receptacles must be
provided for all discarded oily waste, rags, excelsior, or mechanic's
clothing. Provisions of local SOPs should also be considered when
establishing safety procedures.
When supplies are scored, theft and pilferage are a problem. Supplies can
be stolen in large quantities (theft) and in small quantities (pilferage).
Some of the most desirable items are clothing, foodstuffs, and small tools.
Items such as small tools and clothing are considered "sensitive" items;
they must be kept under continuous surveillance. Constant inspections and
lockandkey
security are the best protection against thef

## Slide 236
Protection against weather damage is important when caring for supplies.
Determine whether the item should be stored in a temperatureand
humiditycontrolled
warehouse, a storage warehouse, a shed, or an open storage area.
Supplies stored in the open must be protected from adverse weather
conditions.

## Slide 237
Materials become unserviceable for many reasons. The life expectancy of
many items is influenced and limited by humidity and temperature. Humidity,
the moisture in the air, has a deteriorating effect on most supplies.
Supplies must be constantly inspected to ensure that they have not been
damaged by temperature extremes. For instance, paints may be severely
damaged or even become useless when subjected to temperatures below
freezing. Often overlooked as a storage hazard is the proximity of the
supplies to sources of artificial heat, such as stoves or suspended heaters.

## Slide 238
Dunnage, paulins, and tents are the three primary means of protecting
supplies in the open from weather elements. Dunnage is any material that is
used in transportation and storage to support and secure supplies, to
protect them from damage, or to provide ease in handling. Paulins are
sheets of canvas or other moistureresistant
material. They are used to
cover supplies in open storage to protect them from the sun, wind, rain,
snow, or ice. Paulins must be overlapped in a direction away from
prevailing winds, folded, and securely fastened to give maximum protection.
After adverse weather, paulins must be checked for damage. Tents often
provide excellent protection from the weather, If erected properly. Tents,
like paulins, must be checked after adverse weather conditions

## Slide 239
Learning Event 2
PRESCRIBED LOAD LIST, REQUESTING SUPPLIES, SUPPLY STATUS, CANCELLATION,
TURNIN
PROCEDURES
Manual procedures to manage and operate a supply operation for support units
below the wholesale level are used by all Army elements. Deviations from
procedures outlined below will only be made with prior approval of
Headquarters, Department of the Army (HQDA). Requests for deviation from
accounting procedures will be prepared and processed using AR 7355.
The supply sergeant will supervise the supply operation and must therefore
know the procedures well enough so that he can teach his subordinates.
Supervisors must be familiar with the form used to request supplies as well
as what their unit is authorized, how to replenish supplies, how to set
priorities, and when and how to cancel or turn in supplies and equipment.

## Slide 240
PRESCRIBED LOAD LIST (PLL)
A PLL of repair parts is a quantity of essential supplies authorized to be
on hand at the user level. The supplies are maintained at unit level and
enable the unit to sustain itself until resupply can be effected. The PLL
is made up of a basic load (when kept) and an operational load of repair
parts.
1. The basic load supports unit maintenance operations in combat for 15
days. Basic load items can also be used to support peacetime operations.
2. The operational load supports daily unit maintenance operations.
Normally, this is also for a prescribed number of days of supply.
To manage and evaluate PLL procedures effectively, managers must be
completely familiar with the PLL and what it is, the policies that apply to
the PLL, the records that are required to manage the PLL, and the Uniform
Materiel Management and Issue Priority System (UMMIPS).

## Slide 241
The DA Form 2063R
(Prescribed Load List). The completed DA Form 2063R
(Figure 30), approved by the commander, is the PLL in the manual system. It
identifies the quantity of repair parts and maintenancerelated
items
authorized to be on hand or on order at the user level. The PLL consists of
the following:
1. Items designated for initial stockage for assigned equipment.
2. Any additional repair parts or maintenancerelated
expendable supplies
that have generated sufficient demands (at least three demands in the most
recent 180 days for Active Army (360 days for Army National Guard (ARNG)/
United States Army Reserve(USAR)) to qualify for stockage.
PLL Policy. The following are the policies that determine the procedures
for PLL:

## Slide 242
1. The total number of PLL lines may not exceed 300. Units may request
exceptions from the major Army command (MACOM). Units with a combat PLL or
an essential repair parts stockage list (ERPSL) may exceed this limit. The
DA Pam 71021
provides details.
2. The commander keeping the PLL is also its approving authority.
3. All PLL stocks must be on hand or on request.
4. Units that regularly support other units without maintenance
capabilities will include the supported unit's equipment in their PLL
computations.
5. Technical manuals identify repair parts by NSN, name, and
recoverability code. They also prescribe the level of maintenance
authorized to request and use the repair parts. The Army Master Data File
(AMDF) can be used to check request data for items assigned an NSN.

## Slide 244
6. An inventory of the PLL must be made when DA Forms 3318 (Record of
Demands Title
Insert), shown in Figure 31, are reviewed. The review period
is 90 days for the Active Army and 180 days for the ARNG/USAR

## Slide 246
7. Units authorized to perform maintenance above the unit level may
include items prescribed by technical manuals for the maintenance level they
perform if they qualify for stockage. These items are not subject to the
300line
limit placed on PLLs

## Slide 247
8. Property book accountability is not established for prescribed loads.
However, the unit commander is responsible for exercising adequate care and
surveillance over such supplies.
9. Prescribed load list stocks and records are maintained in units which
are authorized personnel, tools, and equipment to perform maintenance.
10. Demandsupported
repair parts for any equipment on which the unit can
perform maintenance are included in the PLL.
11. The PLL stocks and records will be kept in an area convenient for
maintenance personnel.
Types of Stockage. Three types of stockage are on hand at the unit level:
initial, consumable item, and direct exchange (DX) stockage.

## Slide 248
1. Initial stockage of repair parts is established for new units and
units having a change in equipment. Initial stockage is based on essential
needs supported by data from technical manuals or by historical usage data
of units with the same equipment. When technical or usage data are not
available, PLLs and/or card decks may be requested through the supply
support activity (SSA) from Commander, USAMC Materiel Readiness Support
Activity, ATTN: AMXMDS,
Lexington, KY 405115101
(except for medical,
missile, United States Army Intelligence and Security Command, and
communications security equipment

## Slide 249
2. Consumable item stockage refers to items consumed in performing
maintenance, such as nuts, bolts, screws, tubing, other common hardware, and
other quick supply store (QSS) items. These items may be requested and
stocked based on usage. They may be on hand in quantities up to an
estimated seven days of supply and are not included in the operational load.
The DA Form 3318 is not required unless they are basic load items. When a
repair is requested and it does not appear on the PLL or DX list, the repair
parts clerk must check the QSS list. This list is published periodically by
the SSA. After the part required has been identified as a QSS item, it is
requested from the SSA on a QSS want slip. No posting to other supply
records is required for QSS items.

## Slide 250
3. Direct exchange stockage items are repair parts considered to be
recoverable/repairable. These are supplied from the SSA to using units
through a system known as DX. Under this procedure, unserviceable items are
exchanged for serviceable items on a oneforone
basis. A list of items
authorized to be exchanged is provided to the using unit by the SSA. When
the using unit's parts clerk determines that the unserviceable item is DX,
he prepares DA Form 2402 (Exchange Tag). If the DX item is PLL, the parts
clerk will exchange the item, if available. The DA Form 3318 is then
posted. The DX items that are not stocked or are at zero balance will be
assigned the appropriate Urgency of Need Designator (UND). Commanders or
their designated representative must authenticate each highpriority
DX item
by placing their signature in Block 8 of DA Form 2402. When the DX item is
turned in to the SSA, copy 1 of the DX tag is retained by the parts clerk as
a dueout,
if a serviceable item is not on hand. Supervisors must ensure
that all unserviceable DX items are turned in promptly to the SSA for
exchange and that dueouts
for DX items are on file in the unit's repair
parts section. Parts clerks should be required to make frequent contact
with their SSA to check on these dueouts.

## Slide 251
Nonstocked Item Demand File. A separate file of DA Forms 3318 (Figure 31)
must be kept to record demands for nonstocked items. These items may be
added to the PLL after meeting the stockage criteria of three demands in the
most recent 180 days (360 days for ARNG/USAR). The items may be added to
the PLL at the time of the third demand.
1. When a nonstocked item is demanded for the first time, take the
following actions:

## Slide 252
a. Prepare a DA Form 3318 for the item. The Title Insert section need
not be completed at the time the form is prepared. (Keep only one card for
each stock number.)
b. enter the demand on the form. It is not necessary to keep track of
dueouts
or the request sent to the SSA. Use the document register for this
purpose.
c. File the form in the nonstocked file in national item identification
number (NIIN) sequence.

## Slide 253
2. When a nonstocked item is demanded for the second and following times,
take the following actions:
a. Enter the demand on the DA Form 3318.
b. Line out demands that are more than 180 days old (more than 360 days
old for ARNG/USAR).
c. Review the form to see if the stockage criteria have been met.
3. When review of the nonstocked file is necessary (at least once every
90 days (180 days for ARNG/USAR)), take the following actions:

## Slide 254
a. Remove cards from the file that no longer apply to the equipment on
hand or have had no demands in the most recent 180 days (360 days for
ARNG/USAR).
b. Submit cancellation requests for any dueins
that do not apply to
equipment on hand.
4. When an item meets the PLL stockage criteria, inform the unit
commander. The commander will decide whether to add the items to the PLL.
When the items will be added to the PLL, take the following actions:
a. Add the quantities of the three demands. Enter this quantity in the
Quantity Demanded column of DA Form 3318. (Use the next available line.)
Underline this entry. Do not count any of the demands above this line
during future reviews.

## Slide 255
b. Determine the initial stockage quantity for the item. Follow the
procedures in DA Pam 71021.
c. Prepare a request for the initial stockage quantity, using UND C.
Enter the request on the first available line in the Request section of DA
Form 3318.
d. Complete the Title Insert section of DA Form 3318.
e. File the DA Form 3318 in the PLL visible file.
f. Prepare a change to the PLL. Use DA Form 2063R.
Obtain the unit
commander's approval.
g. Send the PLL change and the request for initial stockage to the SSA

## Slide 256
5. When a nonstocked item has met the PLL stockage criteria, but is not
added to the PLL, take the following actions:
a. Write "Commander does not desire to stock this item" on DA Form
3318. Make this entry on the next line of the Demands section.
b. Continue keeping the card in the nonstocked file. Start keeping
track of demands again.
Uniform Materiel Movement and Issue Priority System (UUMIPS). The UUMIPS is
designed to ensure that items are delivered according to the military
importance of the requesting unit and the urgency of need for other items.
The system is based on a combination of factors relating the mission of the
requisitioner, force/activity designator (FAD), and the UND of the request.

## Slide 257
1. The FAD is expressed by Roman numerals I, II, III, III, IV, or V; The
permanent orders activating the unit usually include the assigned FAD. A
unit has only one PAD. The highest priority units are assigned FAD I; the
lowest are assigned FAD V.
2. The UND is determined by the using unit. It is used to express how
urgently the unit needs the requested supplies. The UND is identified by
the letters A, B, or C.
a. The UND A is used to request material identified in the modification
table of organization and equipment (MTOE) with equipment readiness code
(EC) A, and/or required for immediate installation on, or repair of,
missionessential
material without which the unit or activity is unable to
perform its assigned mission.

## Slide 258
b. The UND B is used to request material identified in the MTOE with
ERC B and/or required for immediate installation on, or repair of, missionessential
material without which the ability of the unit or activity to
perform its assigned operational mission is impaired. It is also used when
material is required for immediate use for installation on, or repair of,
auxiliary equipment.
c. The UND C is used to request material identified in the MTOE with
ERC C and/or required for scheduled repair, maintenance, manufacture, or
replacement of all equipment and/or material required for purposes not
covered by any other UND.

## Slide 259
3. The priority designator (PD) for a supply request is determined by
relating the FAD to the UND of the needed item. Use Table 4 to select the
PD on the line that relates the unit FAD and UND. The PDs for all supply
requests will be determined according to the UMMIPS (AR 72550).
Commanders
will either personally review or delegate, in writing, to specific persons
the authority to review all requests based on UNDs A and B. This review
will be done prior to sending the request to the SSA (AR 7102

## Slide 261
PLL Replenishment. Priorities are assigned to replenishment requests, as
follows:
1. The UND C is normally used to determine the PD for replenishment when
items on the PLL are used and the line is NOT at zero balance.
2. The UND B may be used to determine the PD for replenishment of a line
item when the line IS at zero balance.
3. The UND A is not authorized to be used in determining the PD for PLL
replenishment.
PLL Records. The PLL records consist of the following:
1. The DA Form 2063R
(Prescribed Load List).
2. The DA Form 3318 (Record of Demands Title
Insert). This form is used
to record all item information, such as

## Slide 262
NSN, technical manual data, nomenclature, and so on. It is also used to
record demands, requests, receipts, inventories, and reviews. These forms
are maintained in a visible file in the NIIN sequence, which is the last
nine characters of the NSN. The primary purpose of DA Form 3318 in the
manual system is to allow units to adjust their stockage based on demand
experience.

## Slide 263
REQUESTING SUPPLIES
Units must submit all requests for supplies to the specific SSA that
supplies the item. The SSA stock record officer then determines the source
of supply for the requested item.
Requests are prepared when
· Authorized PLL stockage levels increase.
· Items are added to the unit equipment authorization.
· Maintenance personnel need repair parts not carried on PLL, although
authorized.
· The QSS and selfservice
supply center (SSSC) lines at the direct
supply unit are at zero balance and your request is high priority.
· Stocks need to be replenished

## Slide 264
Priority designators for all requests for issue are determined according to
the UMMIPS described in AR 72550.
Commanders will personally review or
delegate, in writing, to specific persons the authority to review all highpriority
requests for issue based on UND A and 3 (PDs 01 through 08). This
review is done before the requests for issue are sent to your Materiel
Management Center/Stock Control Section (MMC/SCS).

## Slide 265
Use of Forms to Request Supplies. The DA Form 2765 (Request for Issue or
TurnIn)
Prepunched/Preprinted (Figure 32) is primarily used to request
initial issue, expendable, durable, or nonexpendable supplies listed in the
AMDF. The DA Form 2765 Manually Prepared (Figure 33) on page 118 is used
when a prepunched/preprinted DA Form 2765 is not available.

## Slide 267
Use of Forms to Request Repair Parts. The following forms will be used to
request repair parts: (The DX and QSS requests will be addressed later in
this learning event, under Types of Stockage.)
1. The DA Form 2765 (Request for Issue or TurnIn)
Prepunched/Preprinted
(Figure 32) is normally available for each item in the PLL. In the manual
system, these should be filed behind each corresponding DA Form 3318.
Supervisors should always check to make sure that prepunched/preprinted DA
Forms 2765 are being used if they are available. The use of these cards
lessens the possibility of errors considerably and makes requests easier and
faster to prepare

## Slide 269
and submit. Prepunched/preprinted DA Forms 2765, when available, are
provided by the SSA with the letter "P" entered in block 3 of DA Form 27651.
Prepunched/preprinted OA Forms 2765 are provided only for items on the
PLL.
2. The DA Form 27651
(Request for Issue or TurnIn)
(Figure 34) on page
120 is a fourpart
carbon interleaved form. The first (hard) copy is
retained by the SSA as a voucher copy. The second (tissue) copy is returned
to the requesting organization for quantities established as a dueout.
The
third (tissue) copy Is used by the requesting activity as a suspense copy.
The fourth (hard) copy will be returned by the support activity to the
requesting organization with the supplies requested.

## Slide 271
3. The DD Form 13486
(DOD Single Line Item Requisition System Document)
(Figure 35) is used to request nonNSN
items, classified items, MWO and
modification kits, and items requiring exception data. The DD Form 13486
is prepared in three copies. Copies 1 and 2 are forwarded to the SSA and
copy 3 is filed in the duein
status.

## Slide 273
4. The DA Form 2064 (Document Register for Supply Actions), shown in
Figure 36, is used to record requests, receipts, turnins,
cancellations,
followups,
supply status, and document numbers assigned to supply
documents. It serves as a suspense file for open supply transactions. It
is one of the most important documents in a repair section. Together with
the DA Form 3318 (Figure 31), the DA Form 2064 comprises the basic audit
trail for all supply transactions in the repair parts section.
There are two types of document registers for supply actions: nonexpendable
and expendable/durable.
1. The nonexpendable document register is kept at property book level.
2. Expendable/durable document registers are kept by each element within
a unit that is authorized to submit supply requests to an SSA

## Slide 274
Property Book Officer. The property book officer (PBO) designates elements
within a unit that are authorized to request expendable and durable
supplies. The PBO does this by using a DA Form 2496 (Disposition form
(DF)). The OF will also specify the class of supply, the DOD activity
address code (DODAAC) to be used, and any restrictions. For example, only
one element within a unit is authorized to request durable items. This will
normally be the unit supply. Other elements would be restricted from
requesting durables.
The PBO makes sure document numbers are not duplicated. The PBO does this
by1.
Obtaining a separate DODAAC for each unit requesting supplies.
2. Providing, by DF, separate blocks of document serial numbers to
elements within a unit. Separate blocks are required when supply requests
are sent by more than one element of a unit assigned a DODA

## Slide 275
SUPPLY STATUS
Supply status tells the requester of a decision made by a supplier on a
specific supply request. Supply status is received from the SSA on status
cards and/or listings. Supply status is in the form of status codes. The
codes are explained in DA Pam 71021.
There are two types of supply
status: shipment and exception status.

## Slide 277
1. Shipment status is the status of estimated or actual shipment dates.
2. Exception status results from any of the following supply decisions
made by the supplier:
· Substitution of an authorized stock number.
· Change of unit of issue and/or quantity.
· Establishing a back order when material cannot be sent by the
standard delivery date or the required delivery date.
· Partial supply action on a requested quantity.
· Request rejection (returned without action) for a specific reason.
· Cancellation confirmed.
· Procurement of material for direct shipment from vendor to customer.
· Indication that material may not be sent to the requester within the
set time frame for the assigned priority or the required delivery date.
DueIn
Status File. A duein
status file is maintained under the manual PLL
system. The file contains

## Slide 278
· Status cards with information in the form of status codes about duein
material.
· Duplicate/carbon copies of requests.
When status is received, DA Form 2064 document Register for Supply Actions)
is posted with the status and date of status. The status cards are filed by
document number sequence.
Status cards are destroyed.
· On receipt of the total quantity of duein
material.
· On cancellation, verification, or rejection.
Followup
Procedures. Followup
actions are sometimes needed to determine
the status of an unfilled request.

## Slide 279
1. Followup
actions for PD 01 through PD 08 requests must be initiated,
if no status has been received according to the policy established for the
PD concerned. If status has been received, followup
actions must be
initiated when the expected delivery date on the latest status card has been
exceeded.
2. Followup
actions for PD 09 through PD 15 are taken at the time of the
monthly reconciliation of dueins,
if no status has been received. Followup
actions are recorded on the document register and the card is forwarded
to the SSA. When status is received, the document register is posted. The
status cards are filed in the duein
status file in front of all the other
cards for the same supply requests

## Slide 280
CANCELLATION ACTIONS
When all or part of a quantity ordered is no longer needed, the unit may
request cancellation. Detailed cancellation procedures are in DA Pan 71021.
A request for cancellation is not complete until the SSA verifies that
the request is cancelled. Upon receipt of cancellation status, the document
register is annotated with the cancellation.

## Slide 281
TURNIN
PROCEDURES
Items are turned in when they are
· Excess to authorized allowances.
· Not needed and the authorization is not mandatory.
· Unserviceable or not economically repairable.
· Found on post.
NOTE: For detailed turnin
procedures, refer to DA Pam 71021.
Where Property Is Turned In. Items are always turned in to the SSA that
normally issues the items. The SSA evaluates the property's condition,
accounting requirements code (ARC), recoverability code (RC), and may
approve direct turnin
to the Defense Reutilization and Marketing Office
(DRMO). Items are not turned in directly to the DRMO without SSA approval

## Slide 282
Forms Used for TurnIn.
Listed here are the forms used for turnins,
with
descriptions of the type of property turned in with each form. No form is
used to turn in items "Found on Installation' or excess, serviceable SSSC
items.
1. The DD Form 13481
(DOD Single Line Item Release/Receipt Document),
shown in Figure 37, is used when items reviewed by the supporting SSA have
been approved for direct turnin
to the DRMO. The items on this form have
no value except for their basic content (scrap). This form is also used
when items are disposable at the organization level and the items do not
require turnin
credit.

## Slide 284
2. The DA Form 27651
(Request for Issue or TurnIn)
shown in Figure 34 is
used for all other property not listed above.
3. The DA Form 581 (Request of Issue and TurnIn
of Ammunition), shown in
Figure 38, is prepared in sufficient copies to meet local needs. The DD
Form 13481
(Figure 39) and the DA Form 27651
(Figure 40) on page L28 are
designed as carbon sets and no additional copies should be required.

## Slide 288
TurnIn
of Property Book Items. Property book items must be either excess
or unserviceable not repairable by support maintenance, before they can be
turned in. Do not use a return advice code. If the item is excess and has
a technical publication, enter the words "TurnIn
Excess Suspended." The
SSA will perform a technical inspection after the item is turned in. If the
item is excess but does not have a technical publication and works, enter
the words "TurnIn
Excess Serviceable."
If it does not work, enter the words "TurnIn
Excess Unserviceable." If the
item is not excess, enter the words "TurnIn
Replacement Unserviceable." If
the item is also unserviceable, enter an explanation, such as "T" for fair
wear and tear. Use the same document number that was assigned to the item.
Make sure the following documents accompany the turnin:

## Slide 289
1. Two copies of DA Form 2062 (Hand Receipt/Annex Number) signed by the
commander or PBO, one copy of which is for suspense. The suspense copy is
destroyed when final credit is received.
2. The number 4 (blue) copy of the DA Form 2407 (Maintenance Request)
classifying the item as unserviceable, when a replacement is required.
3. Two copies of DA Form 4615
(Vehicle Classification Inspection) are
required if the items are in Federal supply group (FSG) 23, FSG 24, and
replacement is required.
TurnIn
of Expendable and Durable Supplies. Serviceable expendable and
durable supplies must be turned in to the SSA, when they are excess.
Unserviceable expendable and durable supplies with RCs A, D, F, H, and L
must also be turned in to the SSA.

## Slide 290
TurnIn
of "Found on Installation Property." All "found on installation
property" is required to be turned in to a stock record accountable officer.
When known, "found on installation property" is turned in to the SSA that
would supply the item. If not known, it can be turned in to any SSA.
TurnIn
of Inventory Temporarily In Use (ITIU). The ITIU items are owned by
the SSA that issued the items. They remain on the SSA's accountable
records. The ITIU items must always be turned in to the SSA that issued
them

## Slide 291
TurnIn
of Returnable Containers. There are two types of returnable
containers: vendorowned
and governmentowned
containers.
· Vendorowned
containers are assigned local management control
numbers by the SSA before issue to the unit. Prior to turning in vendorowned
containers, a new document number must be assigned.
· Governmentowned
containers are containers with NSNs, such as drums
or cylinders, and are not assigned document numbers. Use the same document
number on which the container was received from the SSA.
Return of Discrepant Shipments. There are two types of discrepant
shipments: items that were not requested and items with hidden defects

## Slide 292
Turn in items not requested by using. DA Form 27651.
Do not assign a new
document number. Use the same one on which the item was received from the
SSA. Do not enter the turnin
on the document register. Enter return
advice code 1T in Block 22.
Turn in items having hidden defects using DA Form 27651.
Do not assign a
new document number. Use the same one on which the item was received from
the SSA. Do not enter the turnin
on the document register. Enter return
advice code 7U in Block 22.

## Slide 293
For property book items, check the property book to see if the document was
posted as an increase to the balance. If it was, post the turnin
as a
decrease. If it was not, file the document in the supporting document file
along with the original document, after posting.
For other than property book items, destroy the turnin
document.
Return of Property Issued to Support DAApproved
Emergency Requirements.
Property issued to support DAapproved
emergency requirements will be turned
in when the emergency is over. This includes property rented or leased

## Slide 294
Do not assign a new document number. Use the same one on which the item was
received from the SSA. Do not enter on the turnin
document register.
Enter return advice code 7P in Block 22. On completion of the turnin,
file
the document in the general administrative logistics file.

## Slide 295
For property book items, after receipt by the SSA, post the turnin
as a
decrease to the property book balance. Complete the document register, then
file it in the supporting document files. Destroy other turnin
documents.
Return of Items to the SSSC. The SSSC items that are no longer required are
returned when they are in the same condition or the same unit pack as
purchased.

## Slide 296
No paperwork is required when returning SSSC items. Simply return the
items. Credit will be given to the unit.
If the items do not meet the above criteria, use the procedure for turnin
of expendable and durable supplies to turn them in.

## Slide 297
Learning Event 3
INVENTORIES, TOOLROOM CONTROL, HAND RECEIPTS
This learning event describes how supply room supervisors train their
subordinates in inventory procedures, toolroom control, and accounting for
property through hand receipting. Also covered in this learning event are
the regulations governing procedures in these areas, the forms used, and the
assignment of responsibilities.
INVENTORIES
Persons receiving inventories must observe the following procedures to
ensure accuracy of records

## Slide 298
1. Make sure items are for the unit.
2. Make sure items match description on receipt.
3. Count all items. Make sure quantity agrees with quantity recorded on
document.
4. Check end items for completeness.
5. Check serial numbers if items have them. Make sure they match receipt
documents.
6. Visually check condition of items for damage.
7. Sign receipt document.

## Slide 299
When the property is to be issued on hand or subhand receipts, the receiving
person must also take the following actions:
1. Make sure items and their description on hand or subhand receipts
match.
2. Make sure quantities match and end items are complete.
3. Verify serial numbers with receipts.
4. Sign hand or subhand receipts.
The clerk must record all discrepancies and report them to the proper
authority. The clerk must make sure all errors are corrected before signing
the hand or subhand receipts, or, if serviceability is questionable, he must
inform the

## Slide 300
PBO, who will resolve the matter. The AR 73511
contains the procedures
used to account for lost, damaged, or destroyed tools stored in the
toolroom.
In addition to the receipt and issue of property inventories, other
inventories are used to account for property.
1. Change of responsible officer inventories are taken when the officer
is replaced. This inventory is jointly conducted by the incoming and
outgoing officers. All the unit property is inventoried at that time.
2. Annual inventories are conducted by the responsible officer. This is
a 100percent
physical inventory of all unit property. The date of the
inventory is based either on the date of last change of responsible officer
or the annual inventory, whichever is Later. A cyclic inventory may be used
in lieu of the annual inventory.

## Slide 301
3. Cyclic inventories are conducted by the responsible officer, in lieu
of annual inventories, when the officer elects to do so or when the property
book is kept at other than unit level and the PBO requires it.
4. Change of PBO inventory is taken when the PBO is changed. The
inventories are conducted jointly by the outgoing and incoming PBOs.
5. Annual property book inventories are required when property books are
kept at other than the using unit level. The PBO conducts these
inventories

## Slide 302
TOOLROOM CONTROL
Maintenance operations require many tools and equipment. Some tools, such
as the general mechanics' tool kit, are usually issued to the mechanic.
Other specialized tools and test equipment are made available on an asrequired
basis. Initial issue and replacement tools are obtained through
the unit supply.
When assuming command of the unit, commanders also assume responsibility for
unit property. They may use hand receipts to further assign responsibility
to specific individuals. When an item has not been further assigned by a
hand receipt, the commander is responsible.

## Slide 303
Tools are usually components of a larger set, kit, or outfit (SKO).
Responsibility is assigned using a hand receipt or handreceipt
annex which
lists existing shortages. All components which make up the SKO are listed
on the hand receipt. The responsible person signs for all the items listed
on the receipt. When more than one SKO is maintained in the toolroom, the
tools among the SKO should not be mixed.
Formal inventory requirements are outlined in DA Pan 71021.
Local
commanders usually establish an increased inventory requirement. Tools are
normally inventoried—

## Slide 304
· Every 30 days when the tools have been issued to the using
individual.
· Upon change of handreceipt
holder.
· Upon change of responsible officer.
· Under special circumstances as directed by the commander:
Prior
to and following major field exercises.
Upon
discovery of forced or unlawful entry.
Upon
discovery of open or unattended storage area.
Upon
destructive or illegal action by responsible individuals.

## Slide 305
Silhouette layout mats are available to assist in the inventory of general
mechanics' tool kits. The tools are placed on the corresponding silhouette
on the mat. Shortages are readily apparent. A layout may be ordered for
each tool kit.
Tool control in an organizational maintenance element usually centers around
control of general mechanics' tool kits, the tools and equipment in the
organizational shop equipment sets, and the physical construction and
operation of the toolroom itself.

## Slide 306
Tool kits are usually hand receipted to the users, kept locked by the
mechanics, and stored in the toolroom. At the beginning of the work period,
the toolroom attendant issues the locked tool kits to the mechanics, who
return the locked tool kits when finished. The users are responsible for
the

## Slide 307
contents, while the toolroom attendant is responsible for the locked tool
kit. Each tool kit is identified by a control number and is receipted for
by the users in a manner similar to other tools issued by the toolroom. A
storage rack is normally provided for storage of the tool kits. For
additional security, at the end of the work period a chain may be run
through the tool kit handles and secured to some object.
Equipment, sets, and special tools are made available to mechanics on an asrequired
basis:

## Slide 308
· The small tools contained in shop equipment sets may be stored in
cabinets or other containers. A locator system allows the toolroom
attendant to find the needed tools. If more than one tool has the same NSN,
a separate card should be prepared for each tool.
· Frequently used larger tools may be displayed on a locally produced
shadow board. This shadow board makes it easier to identify, issue, and
control frequently used tools.
· When space is limited, prime storage space should be given to
frequently used items. Less frequently used items can be stored in less
convenient locations.
· The commander should prescribe policy for storage and issue of bolt
cutters.

## Slide 309
The toolroom should provide both security for the tools and convenience for
the mechanics by limiting access to unauthorized personnel. Field
expedients and limited access should be used to provide storage and security
in the field. The unit MTOE may permit use of a shop van or a cargo vehicle
to support field operations.
The unit motor sergeant is usually in charge of toolroom operations:
· A primary and alternate toolroom attendant should be appointed

## Slide 310
· The toolroom attendant checks the condition of tools before issue
and after return. Tools should be cleaned by the user before return. The
attendant is responsible for cleaning dirty tools found in the toolroom.
Tools should be returned to their storage location immediately upon return
and acceptance. The attendant checks for tools not returned by closing time
and notifies the motor sergeant.

## Slide 311
A tool signout
register provides the easiest control. The attendant prints
the name and grade of the individual, the type of tool, and the date and
time in and out. The individual drawing the tool then signs the register.
A tool check system for tools on the shadow board may speed service and
still provide control. With this system, each mechanic is issued a number
of metal tags stamped with a number corresponding to the tool kit. When the
mechanic needs a tool from the shadow board, the tag is given to the
attendant. The attendant removes the desired tool, issues it, and hangs the
metal tag in its place. The same care must be used with this system to
safeguard the tool checks as with the actual tools.

## Slide 312
HAND RECEIPTS
Hand receipts are required whenever property book or durable items are
issued. The hand receipt lists the property that has been issued. The
signature of a person on a hand receipt establishes direct responsibility.
Prepare separate hand receipts for installation and organization property.
Forms. The following forms are used for hand or subhand receipts:
1. Use DA Form 2062 (Figure 41) to record the issue of property book and
durable items. Prepare the form in two copies. The DA Form 2062 may be
overprinted. The person who prepares the form mast keep all copies of
hand/subhand receipts current.

## Slide 313
a. Hand receipts are prepared by the PBO. The original is kept by the
PBO. Copy 2 is provided to the handreceipt
holder.
b. Subhand receipts are prepared and issued by the handreceipt
holder.
The original is kept by the handreceipt
holder. Copy 2 is given to the
subhandreceipt
holder. There is no restriction on the number of times
property can be subhead receipted, but under normal circumstances this
should not exceed from commander to supervisor to user. Figure 41 shows DA
Form 2062 prepared as a hand or subhead receipt.

## Slide 314
2. Use DA Form 3161 (Figure 42) on page 138 for issue and turnin
transactions between the PBO and the handreceipt
holder. The form is also
used for issue and turnin
transactions between the handreceipt
and
subhandreceipt
holders. Prepare the form in two copies. The original is
kept by the person who issues or turns in the item. The

## Slide 317
person receiving the property keeps the second copy and files copies of
change documents with the proper hand or subhand receipt. The DD Form 1150
may be used in lieu of DA Form 3161 as a change document (Figure 43).
3. The DA Form 2402 (Exchange Tag) and the DA Form 2407 (Maintenance
Request) may be used to document items turned in for repair between the PBO
and the handreceipt
holder. When DA Form 2402 is used, the PBO or
authorized representative must sign and date the reverse side of each tag
used. The DA Pam 738750
gives instructions for preparing these forms. See
Figure 44 on page 140 and Figure 45 on page 141 for examples of these forms
used to turn in items for repair.

## Slide 321
Temporary HandReceipt
Procedures. When property is issued or loaned for
periods of up to 30 calendar days, the following procedures may be used:
1. Prepare DA Form 3161 in two copies (Figure 46) as a temporary hand
receipt. The person issuing the items keeps the original copy. The person
receiving the items keeps the second copy. The DD Form 1150 may be used in
lieu of DA Form 3161 as a temporary hand receipt.
2. Prepare a folder for filing temporary hand receipts. File the
original copies in date sequence.
3. Destroy both copies of temporary hand receipts when the property is
returned.

## Slide 322
4. Review the temporary hand receipt file daily to find if any are due to
expire shortly. Five days prior to expiration of the temporary hand
receipt, take the following actions:
a. Notify the hand receipt holder and arrange for return of the
property not later than the expiration date. Destroy all copies of the hand
receipt when the property is returned.
b. If the user still needs the property, issue it using handreceipt
procedures.
5. Prepare a log book, a locally designated form, or a card file to be
issued for one day or less. Minimum entries for locally designed forms or
log books are NSN, noun nomenclature of tool, and signature of individual

## Slide 324
Learning Event 4
ACCOUNTABILITY AND RESPONSIBILITY, HANDLING OF DAMAGED PROPERTY, REPORT OF
SURVEY
This learning event covers policies and procedures for accounting for US
Army property. It defines accountability and responsibility, handling of
damaged property, and reports of survey.

## Slide 325
ACCOUNTABILITY
Accountability is the obligation of a person to keep an accurate record of
property, documents, or funds. It is imposed by law, lawful order, or
regulation. It is concerned primarily with maintaining formal records that
contain item identification data, quantities, values, balances, and property
transactions.

## Slide 326
RESPONSIBILITY
Responsibility results from the possession of property or the command or
supervision of others who have possession of property. It involves a basic
obligation for the proper custody, care, use, and safekeeping of government
property. Any person may incur responsibility for the care and custody of
property, even if the person has not signed a receipt for it.
Responsibility is based on possession of the property or the scope of the
individual's employment or duty. The assignment to duty may be by written
or oral orders of a superior. Examples of responsibility incurred in this
way are command responsibility, supervisory responsibility, direct
responsibility, and personal responsibility

## Slide 327
Command Responsibility. This is the obligation of a commander to ensure the
proper care, custody, and safekeeping of all government property within his
or her command. It is the special relationship between a commander and the
property within his or her command. It is inherent in command and cannot be
delegated. It is evidenced by assignment to a command position at any level
and includes—

## Slide 328
· Ensuring the security of all property of the command, whether in use
or in storage.
· Observing subordinates to ensure that their activities contribute to
the proper custody, care, use, and safekeeping of all property within the
command.

## Slide 329
· Enforcing all security, safety, and accounting requirements.
· Taking administrative or disciplinary measures when necessary.
Supervisory Responsibility. This is the obligation of a person for the care
and safekeeping of government property issued to or used by the person's
subordinates. It is inherent in all supervisory positions and is not
contingent upon signed receipts or responsibility statements. It is the
relationship between a person and the property in the possession of the
personnel under that person's direct supervision. It arises because of
assignment to a specific position and includes

## Slide 330
Providing proper guidance and direction
· Enforcing all security, safety, and accounting requirements.
· Maintaining the proper physical and psychological environment for
the proper care and use of government property.

## Slide 331
Direct Responsibility. This is the relationship between a responsible
officer and the property for which the officer has been formally tasked to
provide care and custody. It is inherent in each property account.
However, it may be delegated by the accountable officer through formal
written designation or issue of property on a hand receipt. Direct
responsibility results from assignment as an accountable officer, receipt of
formal written delegation, or acceptance of the property on a hand receipt
from an accountable officer. It includes taking all reasonable and prudent
actions to ensure the specified property is properly used, cared for, and
safeguarded.

## Slide 332
Direct responsibility is a formal assignment of property responsibility to a
person within the supply chain who has the property within their custody,
but not necessarily in their possession or for their use. Accountable
officers always have direct responsibility unless it has been specifically
assigned to another person. Accountable officers may delegate such
responsibility by written designation or by issue of the property on a hand
receipt.

## Slide 333
Personal Responsibility. This is the relationship between a person and the
property in their physical possession. It applies to all government
property issued for, acquired for,

## Slide 334
misappropriated, or converted to the person's exclusive use, with or without
receipt. It includes taking all reasonable and prudent actions to properly
use, care for, and safeguard property. Personal responsibility always
accompanies the physical possession of property.
Command responsibility and supervisory responsibility depend on the location
of the property within the chain of command. This responsibility is a part
of a job or position and is incurred by assuming that command or supervisory
position. It can be delegated.

## Slide 335
Responsible Officer. A responsible officer is a person who has been tasked
by formal assignment or designation with the direct responsibility for
specifically identified government property. The responsible officer will
be designated in writing, and will be directly responsible for the care,
use, and safekeeping of the property specifically entrusted to their
custody. Designation as an accountable officer carries with it designation
as a responsible officer unless some other person has been specifically
designated as the responsible officer by regulation or other competent
authority. Direct responsibility imposed through designation as an
accountable officer may be delegated. Such delegation can only be made by
the accountable officer and must be in writing. No further delegation is
authorized.

## Slide 336
Property issued by an accountable officer on a hand receipt (called the
primary hand receipt) carries with it the delegation of the direct
responsibility and designates the recipient as the responsible officer for
the listed property. Further hand receipting (subhand receipting) does not
transfer direct responsibility nor relieve the primary handreceipt
signatory of their duties as the responsible officer.
Any employee of the US Army, civilian or military, may be designated as a
responsible officer.

## Slide 337
Responsibilities by Rank in Battalion. Each person within the battalion,
from the commander to the individual mechanic, has specific responsibilities
within the organization for control and use of tools. For the organization
to work smoothly, each person must meet their responsibilities.
The commander sets unit tool control policy, establishes a toolroom with
adequate security for unit tools, and assigns responsibility by use of hand
receipts. Individual use

## Slide 338
items, such as general mechanics' tool kits, are hand receipted to user.
The commander is also responsible for all tools not further hand receipted,
for enforcement of supply discipline according to AR 7355,
AR 73511,
AR
7102,
and DA Pam 71021,
and for conducting command inspections.
The unit supply sergeant's responsibilities include ensuring that all
authorized tools are on hand or on requisition, turning in excess tools and
conducting inventories, and informing the commander of the results. The
supply sergeant also takes action to account for tools lost, damaged, or
destroyed through other than wear and tear before issuing or requesting a
replacement.
The BMO provides overall management for the battalion tool control program.
The BMO's responsibilities also include enforcing the commander's policies
and implementing directives

## Slide 339
Battalion motor sergeants manage the battalion headquarters tool control
program, act as handreceipt
holders for tools issued to tool room, and
appoint primary and alternate toolroom attendants. Their responsibilities
include supervising layout and operation of the toolroom, conducting daily
inspections, determining status of tools not returned by closing time, and
supervising inventories. They also initiate appropriate adjustment document
action for lost, damaged, or destroyed tools.
Toolroom attendants follow procedures outlined by the battalion motor
sergeant. These procedures include accounting for all tools issued to the
toolrooms, checking the condition of tools before issue and after return,
and putting tools in proper place after return. They also clean and
maintain tools in the toolroom and report to motor sergeant all tools not
returned by closing time.

## Slide 340
The individual mechanic signs hand receipts for the general mechanics' tool
kit and other individual use items as directed by the commander, keeps the
tool kit secured with lock when not in use, stores the locked tool kit in
the toolroom, and conducts inventories as required.
Relationship Between Accountability and Responsibility. Accountability
pertains to maintaining formally prescribed property records for a property
or sales account. It is an obligation officially assigned to a specific
person and may not be delegated. Responsibility pertains to the care,
custody, and safekeeping of government property. Th

## Slide 341
specific type of responsibility depends on the relationship of the person to
the property. Accountability and the four types of responsibility described
above are separate obligations and they are incurred for separate reasons.
Accountability and each of the types of responsibility carry specific
duties. Monetary liability can be assessed against any person who fails,
through negligence or misconduct, to perform those duties and where such
failure is the direct or proximate cause of a loss to the United States
government.

## Slide 342
HANDLING OF DAMAGED PROPERTY
Qualified technical inspectors, property classification officers, or other
designated officers or persons may classify property physically on hand as
unserviceable. From its general condition and appearance, the property may
be classified as unserviceable through fair wear and tear (FWT).
Damaged property (regardless of Federal supply classification) may be
determined unserviceable by technical inspection or may be classified as
unserviceable through other than FWT. If so, the commander responsible for
the property will investigate the circumstances. Upon completion of the
commander's investigation, one of the following actions will be taken:

## Slide 343
1. If negligence or misconduct is not involved, the commander will attach
a statement to the maintenance request or turnin
document stating, "I have
reviewed the circumstances surrounding the damage to the above item(s) and
find no evidence of negligence or misconduct." The commander will sign the
statement.
a. The appointing authority will review this statement and concur or
nonconcur. If the appointing authority concurs, he or she will enter
"Concur" on the statement and sign it. If the appointing authority
nonconcurs, he or she will enter "Nonconcurinitiate
a report of survey" on
the statement and sign it.

## Slide 344
b. The commander must request from the maintenance activity the actual
cost of damage only when a report of survey is initiated. The commander of
the maintenance support activity will consolidate cost data through the
appointing authority to the approving authority as requested by the
approving authority.

## Slide 345
c. For the ARNG, state Adjutant Generals (AG) may authorize the
reporting of repair costs using the property accountability management
information system (PAMIS) reporting procedures per National Guard Bureau
Memorandum (NGBM) 7001,
Chapter 18.
2. If liability is admitted and the extent of damage does not exceed the
responsible person's monthly basic pay, prepare DD Form 362 (Statement of
Charges for Government Property Lost, Damaged or Destroyed) or DD Form 1131
(Cash Collection Voucher). See Figures 47 and 48 on pages 150 and 151.
3. If liability is admitted and the extent of damage exceeds the person's
monthly basic pay, initiate a report of survey

## Slide 346
4. If negligence or misconduct is involved and liability is not admitted,
initiate a report of survey (discussed in the next paragraph).
a. In no case will separate reports of survey be prepared for the same
incident unless the damaged property is recorded on separate property
accounts.
b. When the report of survey is approved or when the property is
released by the survey officer, attach a copy of the report of survey or the
survey officer's release statement to the maintenance request. If the item
is not economically repairable, attach a copy of the approved report of
survey, or the survey officer's release statement, and a copy of the
maintenance request classifying the item to the turnin
document. Damaged
property for which negligence or misconduct is suspected will not be
repaired or disposed of, or continued in use, until the survey officer
prepares a release statement.

## Slide 347
REPORT OF SURVEY
The rest of this learning event outlines the procedures for processing DA
Form 4697 (Department of the Army Report of Survey) and/or conducting an AR
156
investigation. Liability for damage to property, whether by negligence
or misconduct, is resolved by the report of survey. This section gives
general guidance to those persons who are initiating reports or
investigations, when negligence or misconduct is suspected and liability is
not admitted.

## Slide 350
Survey Requirements. A report of survey or an AR 156
investigation will be
prepared when
· Sensitive items are lost or destroyed.
· Directed by higher authority or DA directives.
· Property loss is discovered as a result of change of accountable
officer's inventory, unless voluntary reimbursement is made.
· The value of the damages/shortages exceeds the responsible person's
monthly pay.
· A person refuses to admit liability and does not offer payment for
the value of the property.
· A person admits liability and the loss, damage, or destruction
exceeds the person's monthly basic pay.
· The total handling loss of a specific bulk petroleum product is
above the allowable loss for that product and the dollar value is greater
than $250.00.

## Slide 351
Processing Times. Reports of survey will be initiated and presented to the
appointing authority not later than the fifteenth calendar day after the
date the discrepancy is discovered. The appointing authority will process
and present it to the approving authority not later than 55 calendar days
after discovery. The appointing officer/authority should complete his
responsibility within 40 calendar days. When an investigator is appointed,
he is given 30 days to conduct the investigation. When the approving
authority receives the investigation report, he has 20 calendar days,
including any legal review, to process it. The total processing time will
be no longer than 75 calendar days

## Slide 352
Statement of Charges. Immediately upon determining that responsibility
should be placed on specific individuals, the surveying officer will inform
the appropriate commander so that a statement may be made on the appropriate
clearance form that a report of survey is being processed against
individuals.
The surveying officer must be free from bias or prejudice and must not begin
an investigation with predetermined ideas. The surveying officer should
determine the actual facts, not as they were reported but as they exist, and
should make an intelligent, concise statement of his

## Slide 353
findings of loss or damage occurred and whether fault or neglect is
involved. In instances where fault cannot be established, the surveying
officer will recommend that all individuals be relieved of liability for
property.
After his findings are recorded, the surveying officer makes recommendations
based on policies set forth in regulations and places responsibility on some
individuals, while absolving others. The surveying officer ensures that the
total cost is properly computed and covers loss, damage, or destruction of
the property being investigated. The surveying officer's findings will
include a decision on monetary liability. Items classified as not
economically repairable will be turned in. The surveying officer will
recommend disposition of property in his report

## Slide 354
Based on the facts developed by the investigation, the surveying officer
will make recommendations on, but not limited to, the following:
· Monetary liability.
· Relief from responsibility and accountability.
· Disposition of any unserviceable property.
Once the investigation is completed, the surveying officer will return all
copies of the report, along with all exhibits, to the appointing authority

## Slide 355
The appointing authority reviews the report for correctness and forwards it
to the approving authority. The approving authority will review all reports
of survey arising at the activity except those listing property for which he
is responsible or accountable. The approving authority will review the
reports personally; this authority will not be delegated.
If there is no evidence of negligence or willful misconduct, the approving
authority must decide whether the evidence submitted supports the decision.
After reviewing the report and supporting evidence, the approving authority
may select one of the following courses of action:

## Slide 356
· Reject the report and direct that an investigation be made. In this
case, the report will be returned to appointing authority for appointment of
an investigating officer.

## Slide 357
· Reject the report and request more data. The approving authority
will specify the data required.
· Approve the report and complete the appropriate forms.
If there is evidence of negligence or willful misconduct, the approving
authority will decide whether—1.
Correct procedures were followed.
2. An adequate and unbiased investigation has been made by surveying
officers.
3. The recommendations of the surveying officer and the appointing
authority indicate a decision based on the findings.

## Slide 358
Where monetary liability is recommended, a judge advocate or civilian
attorney will review the findings and give opinions as to adequacy of
evidence and propriety of findings, before the approving authority's action
on the case.
When the monetary charges are assessed, the approving authority will forward
the report to the finance and accounting officer (FAO), not later than the
second duty day after the date the approving authority signs the document.
The final action on reports of survey establishes indebtedness of persons by
administrative procedure. The person charged may appeal the decision