## Slide 1
A simple or circular curve is one with uniform radius; compound and reverse curves are
merely combinations of simple ones. A compound curve consists of two simple curves of different radii, both
bending in the same direction. A reverse curve is made up of two curves going in opposite directions, one
following on the other; the letter S is an example. Reverse curves require a tangent between them at least the
length of a locomotive. But a tangent of at least 300 feet makes construction and maintenance as well as train
movements easier.

## Slide 6
3.16. GENERAL
The requirements for well-maintained curved track are the same as those for straight track, but many maintenance joBs are more difficult to perform on curves, and some faults of curved track must be corrected more requently than the same ones on tangents. For instance, rails wear faster on curves. And while both curves and
tangents require proper lining, you can line a straight stretch of track by eye but must calculate corrections in detail to line a curve properly. Although the design and construction of curved track are intended to counterbalance the forces applied
by trains rounding curves, they can never compensate for them entirely. Sooner or later the continual passage of trains results in track movement, and the lining is disturbed. First, the ride becomes uncomfortable and the rails suffer great wear; eventually, the curve becomes unsafe for scheduled speeds. Constant watchfulness by maintenance men, however, can prevent this happening. Curves are checked frequently, and when one becomes distorted, it is lined promptly to avoid further damage. Engineers use surveying equipment to lay out railway curves; in the past they were lined in the same way. Now, however, they are almost always lined by a comparatively simple method known as stringlining. When poor riding qualities or visual inspections indicate that a curve is poorly lined, a stringlining job is
required.

## Slide 8
3.17. BASIS
When a string is stretched tautly between two points on the inside or gage side of the outside rail of a
curve, the distance between the midpoint of the string and a point five-eighths of an inch from the very top of thE rail is proportional to the degree of curvature. This is the basis of stringlining. A longer distance between the
midpoint and the rail signifies a sharper curve than does a shorter one. This distance is known as an ordinate,
though some railroaders call it an offset. The measurements marked m in figure 3.4 are ordinates.
Figure 3.4. Ordinates on a Simple Curve. When the string used is 62 feet long, the ordinate in inches equals the degree of curvature. For example, if a 62-foot string is stretched between two points on the inside of a rail on the simple portion of a curve and the ordinate measures 2 inches, then it is a 2-degree curve. If the ordinate were 3 1/2 inches, it would be a curve of 3 degrees 30 minutes. For this reason, a 62-foot string is usually used in stringlining. On a smooth or properly lined simple curve, the degree of curvature is the same at all points. Since measured ordinates are equal to curvature, all those in such a curve should be of equal length. If they are not, the curve is out of line. Similarly, on a properly lined spiral, curvature changes at an even rate. Therefore, ordinates on a spiral measured at equal distances should vary an even amount from one to the next.

## Slide 10
3.18. EQUIPMENT
What equipment do you need to put stringlining into actual practice in the field? To mark off the stations
and measure the ordinates, you need a tape at least 31 feet long, graduated in feet. Any such tape will do,
provided the same tape is used to measure all the stations on a curve. You also need a strong string, 62 feet long
or longer, marked at the 62-foot point. A ruler, graduated in inches and eighths of an inch, is required for
measuring ordinates. One graduated in inches and tenths will do, if a similar rule is used for all lining of a
particular curve. However, in this discussion, all ordinates are expressed in eighths of an inch. You also need a
notebook, a pencil, and a heavy crayon. A pair of wooden blocks, 1 by 1 by 2 inches, known as offset blocks, are
helpful. To mark the distance the track is to be moved, you need wooden stakes, surveyor’s tacks, and a ruler or
tape.

## Slide 12
3.20. MEASURING ORDINATES
After the curve is divided into stations, you begin to measure the ordinates. Take the string and stretch it
from Sta. 0 to Sta. 2, holding it on the inside of the head of the rail. The midpoint of the string will be opposite
Sta. 1. Measure with the ruler between the head of the rail and
the string at Sta. 1, and enter the distance in eighths of an inch
in your notebook beside the station number. If there is no
distance, write down 0. Next stretch the string between Sta. 1
and Sta. 3, measure at Sta. 2--the midpoint of the string, and
record the result. Continue to measure at each station all
around the curve until the far end of the string is at the last
station you have laid off. Record the result at each station.
When you are on the curve itself, you will get some
result at each station. Say, for instance that at Sta. 19 you
measured 1 1/2 inches between the string and the head of the
rail. Since 1 1/2 inches is 12/8 inches, you would enter +12 in
your notebook. Inches and eighths should be converted to
eighths of an inch and recorded in that way, as the sketch
illustrates. If you find that the string at its midpoint is pressed
against the rail, especially on or near tangents, this shows
either that the rail is absolutely straight or that it has curved
inward at that point. Here the offset blocks are used, as shown
in the sketch. Use one block at each end of the string, and
place it between the string and the head of the rail. This keeps
each end of the string exactly 1 inch from the rail. Now
measure at the midpoint of the string. If you measure 1 inch,
the track is absolutely straight, and you enter 0 in your
notebook. But if you measure only 1/2 inch, it means that the rail curves inward there. The midpoint of the
string is 1 inch minus 1/2 inch, or 1/2 inch, or 4/8 inch nearer the rail than are the ends of the string. Therefore,
you would enter -4 in your notebook, indicating a reverse bend of 1/2 inch.
Now that you have measured and recorded the ordinate at each station, you have finished the first phase
of your fieldwork. Next, you must take your notebook home or to the office and calculate how much you need to
move the track at each station to achieve a smooth curve. Columns 1 and 2 of figure 3.5 show the station
numbers and measured ordinates of a short curve.

## Slide 14
3.21. EVALUATING FIGURES
For instructional purposes, the curve described in figure 3.5 has been purposely shortened and simplified;
in practice, you would rarely see one like it. A railway curve usually contains dozens if not hundreds of stations.
Remember, the longest in the United States is over 9 miles! A curve may be compound, that is, consisting of two
or more joined circular curves of different degree; or it may be reverse, curving first in one direction and then in
another. But the principles discussed apply to them all. With this method, you can line any curve if you work
carefully, check your figures at every opportunity, and adjust your results as often as necessary. The following
subparagraphs and annex A explain generally the use and evaluation of figures.

## Slide 15
a. Annex A. The curve calculated in figure 3.5 is diagramed in annex A, sheet 1. Study that sheet as
you read the explanation of it. The solid line represents the track itself, while the broken lines are the 62-foot
string stretched from station to station. The curvature in the diagram is greatly increased, so that you can easily
see and compare the ordinates at each station, and so that the distortion of the curve is obvious. The actual curve
is so gentle that the largest measured ordinate is only 9/8 inch. However, a 200-ton locomotive at 60 mph (96
kmph) would slam into such a stretch with a great deal of force. Even such minor deviations in high-speed track
would cause an uncomfortable ride and high maintenance costs; therefore, the curve should be relined.

## Slide 16
b. Analysis. You can see from the diagram that the curve should make a continuous turn to the right.
However, at Sta. 1 there is a slight bend to the left. In column 2 of figure 3.5, you see a negative ordinate listed
for that station, while all the others are positive. A negative ordinate always indicates such a wrong or
reverse bend. When it is not designed into a curve, it is called a dogleg. At Sta. 8, the diagram shows another
dogleg. In column 2, the measured ordinates decrease from Sta. 5 through Sta. 7, increase at Sta. 8, and then
continue to decrease. If these faults were corrected, it would be a fairly smooth curve. The stringline calculation
shows you how to correct them.

## Slide 17
c. Selecting new ordinates. Next, you must select an ordinate for each station of the new curve. Since
the ordinates are smaller near each tangent, it should be a spiraled curve. This means that the new ordinates
should increase by regular amounts to a maximum, remain constant for several stations on the circular part of the
curve, and then decrease to zero at about the same rate they increased. One thing limits you at this point: the sum
of the proposed ordinates must always equal the sum of the measured ordinates. Note that columns 2 and 3 of
figure 3.5 each total 36. This principle gives you a chance to check your work; if they are not equal, the proposed
ordinates must be revised. By looking at the measured ordinates, you can see that there are 10 stations on the
curve, but that stations 0 and 9 are on the tangents and can have no ordinates, while stations 1 and 8 are at the
ends of the tangents and will have very small ordinates. If the curve is spiraled, the ordinates at stations 2 and 7
will be less than those on the circular part of the curve. Therefore, most of the curvature will be at stations 3
through 6 where the curve is circular.

## Slide 18
You may have a track chart, similar to the one in annex C, which shows what the curvature should be. If
you do, you can simply change degrees to inches--1 degree equals 1 inch, convert the inches to eighths, and enter
the result at each of those stations. If you don’t, you usually take the average ordinate on the circular part of the
curve. Here, for stations 3 through 6, the ordinates are 7, 7, 9, and 6, a total of 29 and an average of more than 7.
But if you use an ordinate of 7 at each of the four stations, they total 28, while the sum of proposed ordinates can
be only 36. This leaves only 8, or 4 for each of the two spirals located on either end of the curve. So perhaps 7 is
too large; try 6 for each of the ordinates on the curve. Then the total is 24, and the spirals have 6 each. Since
there are two stations on each spiral, values of 2 and 4 provide a regularly increasing curve to full curvature of 6.
Therefore, in column 3 of figure 3.5, you enter these figures--2, 4, 6, 6, 6, 6, 4, 2. Sometimes, on long curves, it
is necessary to try three or four different spirals before you get one that fits, but here it was easy.

## Slide 19
d. Calculating errors. The difference between the measured and the proposed ordinate is the error at a
station. If the proposed ordinate is larger than the measured ordinate, the error is entered as minus, such as that at Sta. 7. If the measured ordinate is the larger of the two, the error is plus, as at Sta. 5. If the measured ordinate is minus, the
error is the sum of the measured and proposed ordinates, and is minus, as at Sta. 1. Calculate the error at each
station and enter it in column 4. The sum of the entries in this column must be zero.

## Slide 20
3.22. CALCULATIONS
Making the calculations for columns 5, 6, and 7 of figure 3.5 gives you the distance the track must be
moved or “thrown” at each station. They consist of rounding out the ordinate readings by borrowing from the
high ones and lending to the low. Properly done, the calculations provide you with uniform curvature, the result
you wish to obtain. The remainder of the paragraph takes you through the steps.
You first figure out the sum of errors up to and including each station, and enter it in column 5. At Sta. 0
where there is no error and no previous error, the sum of errors is 0. At Sta. 1, the error is -3, but there is no
previous error. As the zigzag arrow shows, 0 is added to -3, and the result is -3. At Sta. 2, previous errors add up
to -3, and the error is +1; -3 +1 equals -2. This calculation is made at each station to the end of the curve. The
total of this column must also be zero. This leads you to where you can figure half of the necessary throw

## Slide 21
For each station, you add the sum of errors at the previous station--column 5, and the half throw there--
column 6, as the arrows between those columns indicate. At Sta. 0, there is no previous error and no previous
half throw so that the half throw is 0. The same thing is true at Sta. 1, but at Sta. 1 there is an error and this will
affect Sta. 2. To find the half throw at Sta. 2, add the sum of the errors at Sta. 1 to the half throw there. Here -3
+0 equals -3, so that figure is entered. At Sta. 3, the figures for Sta. 2 are added; -2 and -3 equal -5, which is the
half throw for the station.
This process is repeated at each station to the end of the curve. Note that the figures in this column need
not add up to 0; however, the last entry in the column, the half throw at the last station, must be 0. If it is not, it
must be adjusted by the method discussed in paragraph 3.24.
The half throw at each station is doubled and entered in column 7. This is the full throw, the amount the
track must be

## Slide 22
moved or “thrown” at each station, expressed in eighths of an inch. If the throw is negative or minus, the track
must be moved in, that is, toward the low or inside rail. If the throw is positive or plus, the track must be moved
out, that is, toward the high or outside rail. When the full throws for all stations have been calculated, the
paperwork of stringlining is complete. Remember, there must never be any throw at the last station.
Sheet 2 of annex A is an overlay showing the same curve after the throws calculated in figure 3.5 have
been made. Place it over sheet 1, annex A, so that stations 0 and 9 coincide on the two sheets. You can then see
that the throwing results in a smooth curve, as intended

## Slide 24
3.23. MARKED POINTS
Many railway curves are marked with stakes to show where the tangents end, the spirals end, and so forth. These points are shown in drawings, and may be marked in the field, by letters. As shown in the upper
sketch, the point where the tangent ends and the spiral begins is TS--tangent to spiral, while the point where the other spiral ends and the tangent begins is ST--spiral to tangent. The circular part of a curve begins at SC--spiral to curve, and ends at CS--curve to spiral. As shown in the lower sketch, if there are no spirals, the curve begins at TC--tangent to curve--and
ends at CT--curve to tangent. When these points are marked by stakes, they help greatly in choosing proposed ordinates. For example, the curvature between SC and CS is constant. The correct proposed ordinate for this stretch is almost certainly the average measured ordinate, to the nearest whole number, for the same distance. When ordinates have been assigned to the circular part of the curve, it is easy to set up smooth spirals between TS and SC and between CS and ST. Remember, though, that the sum of the proposed ordinates must always equal the sum of the measured ordinates. You can adjust your curve
to arrive at this by changing the ordinate by one unit, either plus or minus, at one or more stations

## Slide 25
3.24. ADJUSTING FINAL THROW
If the ordinate at any station deviates by one-eighth inch from a smooth curve, the riding quality of the
track is not affected because the variation is too slight to be noticed. This fact makes it possible to adjust a curve
slightly to make it come out right. Often you measure and calculate a curve, only to find that a throw is required
at the last station. Since the rule says that there can be no throw there, you have to adjust your proposed curve.
You do this by changing the proposed ordinates at two of the preceding stations, one +1 and one -1, so that the
total still equals the sum of the measured ordinates.

## Slide 26
Here are the calculations for the last few stations on a spiral of a typical curve. At the last station--Sta.
22, there is a half throw of +3, as shown in part A of table VI in which the proposed ordinates for stations 16 and
19 are circled. It is these two that you are to change. Since the last throw is plus, you increase the proposed
ordinate at Sta. 16 by 1 and decrease that at Sta. 19 by 1. Note that the stations chosen are three stations apart;
this is because the final half throw is 3. Also note that the proposed ordinate at the earlier or lower numbered
station was increased, because the final half throw is plus. Now the proposed ordinate at Sta. 16 is 10, and that at
Sta. 19 is 2, as shown in part B of table VI in which all the corrected numbers are outlined in heavy black lines.
Note particularly that all full throws from Sta. 17 through Sta. 22 decreased.

## Slide 27
The rules to follow in adjusting a final half throw are given below. However, remember this one
precaution: it is usually easier and produces a better curve if the stations chosen are on the circular part of the
curve rather than on a spiral.
(1) Choose a pair of stations on the curve, whose numbers differ by the amount of the final half
throw.
(2) If the final half throw is plus, add 1 to the proposed ordinate at the earlier station, and take 1
away at the later station.
(3) If the final half throw is minus, take 1 away from the proposed ordinate at the earlier station, and
add 1 at the later.
(4) Recalculate the curve from the earlier station

## Slide 30
3.25. ADJUSTING OTHER THROWS
Sometimes a curve includes a point at which the track cannot be moved, such as a bridge, a turnout, or a
restricted clearance. At such a point, the throw or throws must be zero. You must adjust the curve by the method
given in paragraph 3.24 so that they are zero.
At other times, a series of throws may be very large; they can be reduced by the same method. Assume
that you have six half throws that come out to +24, +31, +37, +34, +29, +26. All you have to do is reduce the
third half throw to +25 by choosing a pair of stations 12 numbers apart; the others will become proportionally
smaller. However, when you adjust throws on a curve, always remember to recalculate from the adjustment on to
the end of the curve and to make sure that the last throw is zero.

## Slide 31
3.26. SUMMARY
Stringlining is a method of determining the curvature of a rail. By stretching a string tautly between two
points on the inside of the outside rail on a curve, the distance, that is, the ordinate, from the midpoint of the
string to a point five-eighths of an inch from the very top of the rail is equivalent to the degree of curvature. A
long distance indicates a sharp curve; a short one, a light one.
When using a 62-foot string, the length of the ordinate in inches equals the degree of curvature. The
curvature of a correctly lined simple, or circular, curve measures the same throughout. On a spiral, the curvature
progresses evenly.
In the field, you use a tape 31 feet or longer, a string 62 feet or longer marked at the 62-foot mark, a ruler
graduated in inches and eighths of inches, a notebook, a pencil, a crayon, offset blocks, wooden stakes, and
surveyor’s tacks.

## Slide 32
Follow the steps given here to stringline a curve, including evaluation of the figures and the calculations
involved. Mark and record stations at 31-foot intervals all around the curve. Stretch a 62-foot string tautly
between each set of alternate stations, and measure and record the distance from the string’s midpoint to the rail.
Choose a new ordinate for each station so as to insure a smooth curve. The total of new ordinates must equal the
total of measured ordinates. Find and record the difference between the measured and the new ordinates at each
station. If the measured ordinate is greater, the difference is plus; if less, the difference